## Slide 1: Mobile Robots Part II
Robotics
a.a. 2018-2019

## Slide 2: Sensing
Module 9

## Slide 3: Sensors
Sensors allow measurements of physical quantities
Two kinds:
  Proprioceptive
    Measurement of quantities pertaining to the “self”, i.e. the robot,
    Example: joint positions, wheel speed/angular position, …
  Exteroceptive
    Measurement of quantities related to the environment where the robot lives.
    Example: position of the rover, position of obstacles, temperature, illumination, …

## Slide 4: Proprioceptive sensors
Perception of the internal state of the robot
  Position of components
    Pose of the links
    Angular position of the wheels
  Speed
  Acceleration

## Slide 5: Proprioceptive sensors
Position sensors
  They provide a signal proportional to the displacement measured between a part and a reference position
  Linear
    Linear potentiometers, linear encoders
  Angular
    Potentiometers, rotary encoders, resolvers
Example of measurements:
  Steering angle ( in the figure )
  Wheel rotation speed

## Slide 6: Proprioceptive sensors
Speed sensors
  Generally derived from position sensors’ readings
Acceleration sensors
  Measure of linear acceleration using inertial forces
  Usually Micro Electro-Mechanical Systems (MEMS)
    Principle:
Measurable strain
Test Mass
Strain-gauge
Cantilever

## Slide 7: Proprioceptive sensors
Inertial Measurement Unit (IMU)
  Array of accelerometers used to measure the complete inertial configuration of a system
    3 accelerometers for accelerations
    3 gyroscopes for rotation speed around the axes
  NOTE: If used for measuring the gravity vector, it’s considered an exteroceptive sensor.

## Slide 8: Exteroceptive sensors
Proximity sensors
  Detection of obstacles/hazards
  Examples:
    Contact/collision sensors
    Infrared reflection sensor
    Magnetic sensor
Distance sensors
  Examples:
    Ultrasound
    Laser scanner (2D or 3D)
    Rotating laser scanner (LiDAR)
    Vision systems
Force sensors
  Load sensing, overload detection
  Examples: load cell, strain gauge
Environmental sensors
  Temperature, humidity, illumination, radiation, …

## Slide 9: Proximity sensors
Contact/collision sensor
  Bumper in simple mobile robots

## Slide 10: Proximity sensors
Infrared reflection sensor
  Contact-less
  Fail-safe
  Very limited range (4-40 cm or 20-150 cm)
  Reflection is impaired for some materials



## Slide 11: Distance sensors
Most widely used in modern mobile robotics
Crucial for mapping and navigation
  Much larger range (100s of meters or more)
  Enables position determination techniques
  Motion and path planning can be done earlier
  Better hazard and obstacle avoidance

## Slide 12: Distance sensors
Operating principles:
  Range-finding
    Evaluation of distance through emission-reflection and collection of a signal (sound, light, radar, ...)
    Time of flight (TOF)
    Interferometry
  Scanning
    Multidirectional range-finding
    2D or 3D mapping of objects/environment
  Vision systems
    Image processing/analysis
    Stereoscopy

## Slide 13: Distance sensing
Range finding
  Using the Time-Of-Flight:

## Slide 14: Distance sensing
Emitter
Beam pattern
Ultrasound
  Use of wave propagation and reflection (20-50Hz)
  Distance is proportional to Time-of-flight (TOF) along the measurement path
    Example:
  Range is limited
    (echo)
    (angular dispersion )
  Low accuracy because of beam pattern spread

## Slide 15: Distance sensing
Mapping with ultrasound sensor

## Slide 16: Distance sensing
Laser scanner
  Fixed or rotating (LiDAR - Light radar)
  Scanning:
    Set of successive range measurements of the environment
    Range-finding with a narrow beam of light
    The result is a map of the environment
  2D or 3D
  Resolution , range approximately
Sick S300
2D laser scanner

## Slide 17: Distance sensing
Mapping with LiDAR
Credits: http://octomap.github.io/
Credits: http://rrt.fh-wels.at/sites/robocup/mapping.html

## Slide 18: Distance sensing
Vision systems
  Stereo vision
    Depth perception using 2 or more cameras
    Allows 3D mapping of the environment
    Sturdy compared to LiDAR
    Drawbacks:
      Computationally intensive
      Less accurate than LiDAR

## Slide 19: Distance sensing
Mapping with vision systems
C. Laeger et al., Remote image analysis for Mars Exploration Rover mobility and manipulation operations

## Slide 20: MAPPING
Module 10

## Slide 21: Environment mapping
Creation of a virtual map of the environment surrounding the robot
Contains information on:
  Obstacles
  Terrain geometry
  Locations and Points of Interest (POI) (e.g. goal)
  Position of the robot itself
Crucial for definition of traversability paths
Obstacles
Terrain
geometry
Robot position
POI

## Slide 22: Environment mapping
Type of map:
  Continuous
    Features are determined by mathematically defined objects
      Polygons, lines, points etc.
      High accuracy
      High computational cost
  Discrete
    Based on the decomposition of the environment in discrete elements
      Grids: occupancy grid
      Lower accuracy
      Large datasets

## Slide 23: Continuous maps
Topological map
Nodes
Connections

## Slide 24: Discrete maps
Occupancy grid-based map

## Slide 25: Discrete maps
Variable-cell occupancy grid-based map

## Slide 26: Discrete maps
Occupancy-grid

## Slide 27: Environment mapping
Rules:
  Precision of map precision of goals
  Precision of map accuracy of the sensors
  Complexity of map computational cost

## Slide 28: Environment mapping
Map representation
  Metric framework
    2D or 3D space
    Records raw objects at precise coordinates
    Example:
      2D matrix
      Each pixel either contains an object (green/yellow) or doesn’t (gray)
  Topological framework
    Records objects and places identifiers
    Records relations between objects/places
    Map is a graph

## Slide 29: Position determination
Belief representation:
  Single unique position?
  Set of possible positions?
  How are they ranked?
Single-hypothesis
  The robot identifies one single unique position
  a certain probability distribution
Multiple-hypothesis
  The position is described in a fuzzy way
  This allows a better description of the degree of uncertainty

## Slide 30: Position determination
Single-hypothesis
Multiple-hypothesis
Continuous environment
Discrete environment

## Slide 31: Position determination
Real map
Occupancy grid-based map
Line-based map
Topological map

## Slide 32: Navigation
Module 11

## Slide 33: Navigation
Definition
  Determination of position and orientation relative to the environment,
  The planning and execution of the maneuvers required to get from point A to point B.

## Slide 34: Position determination
Example: Odometry
Example: triangulation
Idiothetic sources
  Related to self-motion
  Uses proprioceptive sensors
    Number of wheel rotations,
    IMU
    Also called odometry or dead reckoning
Allothetic sources
  Related to external references
  Uses exteroceptive sensors
    Objects/obstacles
    Landmarks
    Terrain geometry
    Points of interest

## Slide 35: Example: odometry
Odometry
  We know at every instant
  We can calculate the configuration at time :
  Same thing can be done with an IMU, by knowing , which are the accelerations in the local frame of reference
Initial position

## Slide 36: S.L.A.M. Simultaneous Localization and Mapping
The computational problem of simultaneously mapping the environment and localizing the robot within
Very computationally intensive
Implemented in varying ad-hoc architectures in the whole industry
  E.g. Autonomous cars

## Slide 37: Reactive navigation
Line following
  A somewhat «legacy» technology
    No mapping required,
    Limited position determination required,
    Simple sensors (IR or magnetic if the line is magnetized)
    Virtually zero flexibility
  Can be coupled to other more advanced form of navigation
Video logistics
Video carts

## Slide 38: Path planning
Aim: producing a continuous path between two points, A (start) and B (goal).
Several possible paths:
Approaches:
  Search algorithms
  Fields
A
B
Obstacles

## Slide 39: Path planning
A path-planning or navigation problem can be represented as a graph
  Weights can be assigned to the single branches to account for distance, slope, terrain, …
The aim is to find the shortest or best path through the nodes, from A to B
A
B
Nodes
A
B

## Slide 40: Path planning
Determination of the nodes
  Grid-based search
  Edge visibility graph
Search for optimal path This is achieved by graph exploration through efficient search algorithms:
  Dijkstra, A*, ...

## Slide 41: Edge visibility graph
The process is repeated for every visible edge
The result is a graph connecting point A to B

## Slide 42: Path planning
Example of graph navigation in matrix form
4 | 3 | 2 | 1 | 0
5 |  |  | 2 | 1
6 | 5 | 4 | 3 | 2
 |  |  | 4 | 3
8 | 7 | 6 | 5 | 4
A
B
Distance matrix
Step 1 Define matrix
Step 2 Find minimum distance path by selecting the lowest neighbor
Exact
Optimal

## Slide 43: Path planning
A larger example
  1000x1000 grid
  Long computation
B
A

## Slide 44: Path planning
Artificial potential fields
  Point A is starting point
  Obstacles are repulsors
  Goal B is an attractor
B
A

## Slide 45: Path planning
Potential where
Gradient
Path follows easily
Potential
Gradient

## Slide 46: The “real world” issue
Module 12

## Slide 47: «The Real World»
Issues in the real world
  Geometry of the terrain
    Loss of contact with the ground
    Slopes
  Terrain yield
    Traction loss
    Sinking
  Position determination accuracy

## Slide 48: Terrain geometry
Loss of contact
  Up to this moment we have dealt with flat ground
    Simultaneous contact with all wheels
  Discontinuities loss of contact
  Possible solutions
    Three wheeled systems
    Suspension systems
    Rocker-bogie

## Slide 49: Terrain geometry
Rocker-bogie
  Based on the Whippletree mechanism
  Advantages:
    Distributes loads equally on the wheels
    Allows contact even on complex geometries

## Slide 50: Terrain geometry
Slopes
  The actuation motors limit the maximum slope angle
    Thus:
  The maximum slope angle is

## Slide 51: Terrain Yield
Traction loss
  Bad for odometry: introduces errors (drift)
    Consider using exteroceptive sensors
  Can prevent overcoming slopes
    Lower friction coefficient limits acting between wheels and ground
  Solutions:
    Keep ground pressure under control
      contact surface

## Slide 52: Terrain Yield
Sinking
  Can happen in 2 occasions
  Very high wheel pressure and/or very loose soil
  Due to digging by slipping wheels
The demise of JPL’s Spirit rover, in 2010