## Slide 1
Dissipative Particle Dynamics and mesoscale techniques
A.A. 2019-2020
CORSO DI SIMULAZIONE MOLECOLARE

## Slide 2
MULTISCALE SIMULATION
Meccanica
Quantistica
(elettroni)
Meccanica
molecolare
(atomi)
Modellazione
di
mesoscala
(insiemi di atomi o molecole)
Simulazione di processo
FEM
Engineering design
1Å
LUNGHEZZE
CARATTERISTICHE
1nm
1μm
1m
years
hours
minutes
seconds
microseconds
nanoseconds
picoseconds
femtoseconds
Quantum mechanics
(electrons)
Molecular mechanics
(atoms)
(groups of atoms or molecules)
Process
simulation
FEM
Engineering design
1Å
TEMPI
CARATTERISTICI
1nm
1μm
1m
Dissipative Particle Dynamics
Morfologia
Miscibilità e compatibilità
Fenomeni di diffusione
Stabilità strutturale
Tensione superficiale
Fenomeni di aggregazione
e coagulazione
Mesoscale modeling
1mm
1mm
Mesodyn
1mm

## Slide 3
SOFT NANOTECHNOLOGY
Nanotechnology is the understanding and the control of matter at dimensions of roughly 1 to 100 nanometers, where unique phenomena enable novel applications.
At this level, the physical, chemical, and biological properties of materials differ in fundamental and valuable ways from the properties of individual atoms and molecules or bulk matter.

## Slide 4
MANUFACTURING AT THE NANOSCALE

## Slide 5
MANUFACTURING AT THE NANOSCALE
In the "top-down" approach, nano-objects are constructed from larger entities without atomic-level control.
The process involves material wastage and is limited by the resolution of the tools you can use, restricting the smallest sizes of the structures made by these techniques.
Examples of this kind of approach include the various types of lithographic techniques (such as photo-, ion beam-, electron- or X-ray- lithography) cutting, etching, ….

## Slide 6
MANUFACTURING AT THE NANOSCALE
In the "bottom-up" approach, materials and devices are built from molecular components which assemble themselves chemically by principles of molecular recognition
molecules can be designed so that a specific conformation or arrangement is favored due to non-covalent intermolecular forces.
this technique is limited in how big the structures can be made.
Chemical synthesis, self-assembly, and molecular fabrication are all examples of bottom-up techniques. Self-assembly occurs when little manipulation occurs, but components spontaneously come together to form ordered nanoscale structures, for instance in the formation of nanotubes and some monolayers.
The limits of feature size and quality of these two approaches have started to converge in recent years, leading to new hybrid techniques of manufacture.

## Slide 7
DPD - The particle or BEAD
What is a DPD particle?
molecule
part of a molecule
fluid element = many molecules
The colored area symbolizes the interaction range of all forces acting on a particle

## Slide 8
DPD - The particle or BEAD
Atomistic and mesoscopic model of the same complex macromolecule
bead of type A
bead of type B
bead of type C

## Slide 9
DISSIPATIVE PARTICLE DYNAMICS (DPD)
conservative force
dissipative force
random force
Instantaneous force acting on particle i:
between no bonded particles
between bonded particles
spring force
angle force

## Slide 10
DISSIPATIVE PARTICLE DYNAMICS (DPD)
In DPD the force between particles i and j is given by the sum:
conservative force
dissipative force
random force
Instantaneous force acting on particle i:
We assume pairwise additivity for all three types of force.

## Slide 11
DPD – Equation of motion
Beads follow Newton’s equation of motion
fi is the total force acting on particle i
All the masses are normalized to 1 for simplicity. All beads have the same volume.
Integration of the equation of motion as in MD
Conservative, Dissipative and Random force obey Newton’s third law Fij = - Fji :
- mass, momentum and energy are conserved
- hydrodynamic behavior correctly treated
where
DPD looks like MD

## Slide 12
DPD - The conservative force
SOFT REPULSION ACTING ALONG THE LINE OF CENTERS
aij = bead –bead repulsion parameter or DPD interaction parameter
aij >0 purely repulsive
aij related to Flory-Huggins parameter
aij depends on the underlying chemistry of the system
rC = cut-off radius
rC sets the basic length scale of the system
where

## Slide 13
DPD - The dissipative (frictional) force
component of the relative speed
of i with respect to j in the direction
of rij
THE DISSIPATIVE FORCE IS INTENDED TO MODEL THE FRICTION BETWEEN DIFFERENT PARTICLES DUE TO THEIR RELATIVE VELOCITY
= friction coefficient (>0)
= weight function
positive definite and vanishing for rij>rC
= relative speed
where
>0 if two particles move towards each other
FijD is repulsive – force towards j
<0 if two particles move away from each other
FijD is attractive – force away from j
and are yet to be defined!

## Slide 14
DPD - The random force
= noise amplitude (>0)
= weight function
positive definite and vanishing for rij>rC
= Gaussian noise variable
Stochastic properties of the noise, :
(variance)
can have either sign, the random force can be either repulsive or attractive.
(mean)
THE RANDOM FORCE MIMICS THERMAL FLUCTUATIONS AND MAINTAIN ENERGY INPUT INTO THE SYSTEM IN OPPOSITION TO THE DISSIPATION
and are yet to be defined!
where

## Slide 15
DPD – The spring force
where
θ
US total bond potential
ks = spring constant
r0 = bond lenght
Default
the distance from a bead to a bonded and a non-bonded neighbor is approximately the same
UA total angle potential
kA = angle constant
θ0 = equilibrium angle
kA sets the stiffness of the chain
no introduction of another length scale

## Slide 16
DPD – Relation to Flory-Huggins theory
Map DPD simulation behaviour onto physical phase diagram of real fluids (compare the free energy of a DPD fluid with the Flory-Huggins theory)
ρ = 3
ρ = 5
ρ = 3
ρ = 5
Map DPD simulation compressibility behaviour onto physical compressibility of water
DPD – Relation to Flory-Huggins theory
DPD – Relation to Flory-Huggins theory

## Slide 17
DPD – Scaling of length, velocity and time
All beads have the same mass, m, interaction radius, rc, velocity distribution, kBT
It is convenient to use them as units of mass, length and energy
All the quantities in a DPD simulation are dimensionless

## Slide 18
Running a DPD calculation
Specifying the structure of the mesoscale system
Define all chemical species present (beads)
Define the mesoscale molecular topology
Define the bead interaction
Define the input system
Define the length and the outputs of the simulation
Define the amount of each mesoscale molecule present in the system
Define the size of the simulation cell
Choose a value for the grid spacing
Specify the cell density and the number of beads
STEPS TO DO
RUN!

## Slide 19
VANTAGGI E SVANTAGGI
DELLA SIMULAZIONE DI MESOSCALA
Method | Main idea | Pro | Cons
Mesoscale | Introduce simplification to atomistic methods to remove the faster degree of freedom and/or treats groups of atoms as individual entities interacting through effective potentials | Can be used to study features of complex systems on the order of 108-109 atoms Can study dynamical processes on timescale inaccessible to classical methods, up to seconds | Can often describe only qualitative tendencies; the quality of quantitative results may be difficult to ascertain In many cases, the approximations introduced limit the ability to physically interpret the results

## Slide 20
SELF-ASSEMBLY OF NANOSTRUCTURES
ON GOLD NANOPARTICLES
Color legend:
solvent=turquoise
TEG/PEG=green
C8=grey
F8=purple
gold=brown
Stripes
Stripe thickness ~ 0.65-0.7 nm
1

## Slide 21
Effect of core size and grafted composition
Color legend:
solvent=turquoise
TEG/PEG=green
C8=grey
F8=purple
gold=brown
2
3
Janus
nanoparticle
Stripe-like pattern

## Slide 22
DEGRADABLE SELF-ASSEMBLY DENDRONS
FOR GENE DELIVERY

## Slide 23
DEGRADABLE SELF-ASSEMBLY DENDRONS
FOR GENE DELIVERY
Cholesterol

## Slide 24
DEGRADABLE SELF-ASSEMBLY DENDRONS
FOR GENE DELIVERY
DNA
water

## Slide 25
DEGRADABLE SELF-ASSEMBLY DENDRONS
FOR GENE DELIVERY
MESOSCALE SIMULATIONS

## Slide 26
DEGRADABLE SELF-ASSEMBLY DENDRONS
FOR GENE DELIVERY
MESOSCALE SIMULATIONS
Chol_G2
CholSS_G2
Chol2SS_G2

## Slide 27
DEGRADABLE SELF-ASSEMBLY DENDRONS
FOR GENE DELIVERY
CholSS_G2
Chol2SS_G2
Chol_G2
ATOMISTIC
SIMULATIONS

## Slide 28
SOFT NANOTECHNOLOGY
Complex fluids, nanostructured fluids, soft matter, …..
- Contain nanoscale structures
- (Usually) formed by the self-assembly of molecules
- For example, surfactants and block copolymers
C7
C4
C2
C1
C3
C5
C6
C8
C1
C2
C3
C4
C5
C6
C7
C8
Water loving
Hydrophilic head
Water hating
Hydrophobic tails
TYPICAL STRUCTURE OF A SURFACTANT

## Slide 29
MODERN SURFACTANTS
Typical anionic surfactants
Typical cataionic surfactants

## Slide 30
MODERN SURFACTANTS
Typical nonionic surfactants (very mild)
Typical lipids
Notice the double tails. Most lipids can be found in
biomembranes. In general, they are
insoluble.

## Slide 31
PACKING PARAMETER
V tail volume per molecule
A cross-sectional area per surfactant molecule
L length of hydrophobic tail
packing parameter
V (volume)
A (cross-section)
l (length)

## Slide 32
PACKING PARAMETER

## Slide 33
Esercitazione di mesoscala-Esempio
Predizione della morfologia di un surfattante
in soluzione
Sodio Lauril Solfato (SDS)
Mesoscale model of SDS
Head
Tail
H
T
T
T
T
H2O
H2O
H2O
H2O
H2O
H2O
H2O
H2O
H2O
H2O
W