## Slide 2
1) particles entrapping (adsorbed onto the thallus surface or within intercellular spaces);
2) extracellular ionic binding (mainly at cell wall level, secondarily at cell membrane level);
3) intracellular ionic binding.
The basic of (bio)-accumulation processes in lichens and mosses

## Slide 3
The sequential elution technique (Brown and co-workers)
Ext. particulate
extracellular
intracellular
insol. particulate
Vol.: 0.5 ml/ mg
(EDTA)
Alternatives:
(cold NHO3)
Sample 1
Sample 2
TOTAL CONTENT
FRACTIONS

## Slide 4
Cosa si è capito usando la tecnica delle eluizioni sequenziali:
Le componenti costituite dal particolato e dalla frazione ionica legata extracellularmente sono prevalenti.
Ci sono alcuni elementi che entrano con più facilità di altri a livello citoplasmico, ma non sono strettamente parlando di interesse ecotossicologico, ma piuttosto fisiologico (es. K+).
La frazione extracellulare di parete può subire dei «turn-over» importanti, non è cioè stabile.
Il forte aumento del numero di analisi richieste da questa tecnica ne limita di fatto in maniera notevole l’uso in studi applicativi, e questo è un vero peccato.

## Slide 5
H2S (hydrogen sulphide)
- The main reduced sulphur compound cycling throught the atmosphere (Brown & Bell, 1986; Sawyer et al., 1994).
1200 tons H2S x year!
(Dall´Aglio, 1988)
- Its principal sources are biogenic processes and phenomena related to volcanic activity.
- Anthropogenic sources are industrial fonts, like the paper-industry and the exploitation of geothermal fields.

## Slide 6
STUDY AREA: Mt. Amiata (Italy-Tuscany), 1738 m s.l.m.
Climatic diagram of Abbadia S. Salvatore (according to Walter & Lieth 1960; data from Barazzuoli & Salleolini 1992), 2 km far from the study area. The x-axis = the months of the year, from January to December. The y-axis = mean monthly temperatures (lower line) and mean monthly precipitations (upper line).a

## Slide 8
H2S vent connected to the Hg mine galleries
Gasses emitted:
- H2S
- CO2
- H2O
Abbadia S. Salvatore, loc. Acquapassante

## Slide 9
Map of the transect from the H2S vent (square) through the chestnut wood of Acquapassante (M. Amiata, Central Italy). Capital letters and broken lines identify the three areas where specimens of Parmelia sulcata were collected and transplanted. The numbers refer to the trees surveyed by Tretiach & Ganis (1999). The dotted areas correspond to an 8-years-old coppice that interrupted the mature chestnut wood.
H2S vent
100 ppm
2 ppm
0.5 ppb
Tretiach M. & Ganis P., 1999. Effects of H2S on epiphytic lichen vegetation: a study case from M. Amiata (Central Italy). Lichenologist 31: 163-181.
Notes: 9
serrdbsshhshst

## Slide 10
BIOMASSA (mg dm-2)
Biomass of selected fruticose and foliose lichens along the transect of the study area ( Ramalina fastigiata, R. farinacea, Evernia prunastri, Parmelia sulcata).
DISTANZA MASSIMA DALLA SORGENTE (m)
Notes: 10
serrdbsshhshst

## Slide 11
Parmelia sulcata Taylor
The selected species

## Slide 12
Correlation between mean yearly radial thallus growth rate (cm yr-1, abscissa), and distance of each thallus from the H2S emitting chimney.
C
B
A
r2=0,792
Mean yearly radial growth (cm yr-1)
Distance (m)
Notes: 12
serrdbsshhshst

## Slide 13
Seasonal radial growth (mm) in 30 thalli of Parmelia sulcata, 12 from A ( ), 9 from B ( ), and 9 from C ( ); t = Student’s values (* = 1% < p < 5%; ** = p < 1%).
t(A-B) 3,07** 2,71** 0,54 3,94**
t(A-C) 9,12** 9,15** 2,14* 6,34**
t(B-C) 4,43** 6,16** 2,46* 2,78**

## Slide 14
L’evidente differenza nella crescita lineare è legata ai drastici effetti dell’H2S sul processo fotosintetico dei fotobionti: ratei più ridotti di assimilazione della CO2 implicano per il micobionte meno molecole organiche da utilizzare per il proprio metabolismo e quindi per la crescita.
Si tratta di una vera e propria azione di inibizione, perché l’H2S si lega reversibilmente al sistema multi-enzimatico della fotolisi dell’acqua, inattivando il flusso di elettroni della catena redox. Ad altre concentrazioni, altri fenomeni correlati causano poi danni permanenti ai fotosistemi.
Bertuzzi S., Tretiach M., 2013. Hydrogen sulphide inhibits PSII of lichen photobionts. Lichenologist, 45: 101-113.
Tretiach M. & Baruffo L., 2001. Effects of H2S on CO2 gas exchanges and growth rates of the epiphytic lichen Parmelia sulcata Taylor. Symbiosis 31: 35-46

## Slide 16
%

## Slide 17
Vicino alla sorgente
Lontano dalla sorgente

## Slide 18
Vicino alla sorgente
Lontano dalla sorgente

## Slide 19
Vicino alla sorgente
Lontano dalla sorgente

## Slide 21
Vicino alla sorgente
Lontano dalla sorgente

## Slide 25
the target species;
the sampling;
sample processing and analysis;
difference among species;
how to compare different data sets: the naturality scale proposed by Nimis & Bargagli (1999) and the NEW scales (Cecconi et al. 2019).
Biomonitoring of persistent pollutants by using autochthonous material

## Slide 27
Foliose lichens are preferred, because relatively large quantities of material are necessary for the analytical work. Fruticose lichens are unfortunately very rare in urbanized areas.
LICHENS
Epiphytic (= growing on plants, usually trees) lichens are preferred to epilithic (= growing on rocks) ones, because soil contamination is generally lower.

## Slide 28
The selected species are rather resistant to airborne pollutants, and have a broad distributional range on the territory. This makes comparisons among different survey areas possible.
Parmelia sulcata Taylor
Punctelia subrudecta s. lat.
Flavoparmelia caperata (L.) Hale
Xanthoria parietina (L.) Th. Fr.

## Slide 29
Sampling sites
The stations must be homogeneous, selected far from roads with heavy traffic (or all of them should be near roads with heavy traffic...), in areas covered by meadows.
Lichen sampling is carried out on trunks of deciduous trees, with inclination <10o, without decorticated areas, or evident injuries.
The most common tree species is selected.

## Slide 30
Sampling: from 1 to 2 m above ground, using a ceramic knife („Made in Japan“!), and putting the material in envelopes made with Whatman paper, and – when dry - in a numbered petri dish (preservation?).
If there are more than three thalli, sampling must be random.
1 m
2 m

## Slide 31
Sampling chard
photographs of the trees;
a short description of the area;
list of species sampled and list of accompanying taxa;
exposition on the truncks;
height above the ground;
lichen health indications (N: necrosis; D mechanical damage; S: bleaching; 0=absent; 1=low; 2=med-ium; 3=strong);
map (1:5000) of the area;
UTM coordinates;
Critical remarks.

## Slide 33
WHEN - Not during rains or at the end of a prolonged drought season. Sampling should be carried out in the shortest time, e.g. in one-two days, without rain events in between. It is preferable that a single operator carries out the sampling.

## Slide 34: Sample preparation

## Slide 35
Come preparare i campioni prima dell’analisi?
Una preparazione accurata di campioni di Xanthoria parietina abbatte le concentrazioni di elementi ampiamente diffusi nel suolo quali Al e Fe, mentre per gli altri elementi la variabilità nell’intercettazione delle particelle di suolo non consente di fare previsioni affidabili.
Loppi, Paoli, Frati, Baragatti (2004)

## Slide 36
Zonation of trace metal accumulation in three species of epiphytic lichens belonging to the genus Parmelia
Bargagli, Iosco, D’Amato (1987)
Confronto tra specie:
Flavoparmelia caperata
Parmelia saxatilis
Parmelia sulcata
Confronto tra ambienti
Al, Cr, Cu, Fe, Mn, Pb, Se, Zn
Confronto tra parte interna ed esterna del tallo
Lavaggio dei campioni
Notes: 36

## Slide 37: Mean metal content in the peripheral (Pe) and central (C) parts of five thalli of Flavoparmelia caperata.
0
5
10
15
20
25
30
35
40
Al
Ba
Cr
Cu
Fe
Mn
Ni
Pb
Pe
Pi
M
C
I
II
III
IV
ppm (g g-1)

## Slide 38: Mean metal content in the external (Pe) and central (C) parts of five thalli of Parmelia caperata.
0
5
10
15
20
25
30
35
Mg
Zn
Pe
Pi
M
C
I
II
III
IV

## Slide 39
The central part of foliose lichens (C), being older, has higher metal contents than the peripheral lobes (Pe).
2
5.2
5.6
7.3
16.2
Pe
Pi
M
C
0
1
1
2
2
3
3
Cr ppm
Distanza
dalla strada
(m)
Parte
del tallo

## Slide 40
Flavoparmelia caperata (L.) Hale

## Slide 41
Under the stereomicroscope...
Approximately 2-4 hours are needed to clean a sample of 200 mg (!).
Foliose lichens

## Slide 42
The fragments obtained are carefully homogenized in a agata mortar or are finely chopped using a ceramic knife.
Great care must be used to avoid contamination. A good rule is to dress lattice gloves rinsed in distilled water, and dried out.

## Slide 43
The pulverized samples can be preserved for a long time in small envelepes of Whatman paper closed in petri dishes or in teflon tubes until use.
Before analysis, they are dried out at low temperatures (40°C, although a thermal treatment at 120o does not reduce the Hg content!). A small aliquot is used to determine the water content of the material, which generally is below 5-6%.