## Slide 1
Green chemistry: integrating sustainable processes with renewable products

## Slide 2: Green chemistry
The chemistry sector, its impact on economy and society
Evolution of chemistry to meet environmental urgencies

## Slide 3
Specialty chemicals
low volume–high value products that constitute raw materials for the production of pharmaceuticals, auxiliaries for industry, crop protection and pigments among others.
Consumer chemicals
products such as detergents, perfumes and cosmetics sold directly to consumers.
Commodities:
A basic good used in commerce that is interchangeable with other commodities of the same type. Most often used as inputs in the production of other goods or services. The quality of a given commodity may differ slightly, but must meet specified minimum standards.
What chemical industry produces: definitions

## Slide 4
During economic crisis of 2008-2009 the world consumption of chemical products has increased by +3.9% per year
Projections: +4.5% growth in 2011-2020.
15% of EU GDP
20% of global production
Italy:
-ranked 10 globally
-ranked 3 in EU (excellence in fine chemistry and specialty chemistry)
Chemistry is the manufacturing sector that delivers products with the highest added value in Europe
L’Industria chimica in cifre, Federchimica, 2014.

## Slide 5
  Centralità di Ricerca e Innovazione
Imprese con R&S
interna in Italia (% sul totale imprese)
Chart: 
Imprese con R&S
interna in Europa (% sul totale imprese)
Note: imprese con più di 10 addetti
Fonte: Eurostat - Community Innovation Survey, 2014
Chart: 
 | 17.8109 | 42.1345
42%
Chart: 
 | 17.8109 | 42.1345
18%
42%
Industria
Manifatturiera
Chimica
Numero di imprese con R&S interna nella chimica europea
Germania
1.278
Italia
683
Spagna
548
Francia
541
Olanda
224

## Slide 6
  Dall’elevata produttività maggiore difesa dai concorrenti emergenti
Valore aggiunto per addetto (indice manifattura =100)
Impianti e tecnologie complesse
Intensità di capitale
Innovazione basata sulla ricerca
+
+
Elevata qualifica e produttività consentono
maggiori remunerazioni
Fonte: Federchimica su Istat, 2015
Notes: Aggiornato i dati con quelli forniti da Juliette

## Slide 7
Industria chimica leader in Sostenibilità economica e competitività
ISCO - Indicatore sintetico di competitività ISTAT (indice industria manifatturiera =100, anno 2015)
Fonte: Istat
Farmaceutica
Bevande
Altri mezzi di trasporto
Macchinari
Apparecchiature elettriche
Metallurgia
Gomma e plastica
Pelle
Elettronica
Carta
Autoveicoli
Tessile
Alimentari
Mobili
Prodotti in metallo
Minerali non metalliferi
Abbigliamento
Prodotti petroliferi
Riparazione e manutenzione macchinari
Legno
CHIMICA
Altre manifatture
MANIFATTURA
Chart: 
 | 133.6 | 125.4 | 123.6 | 118.4 | 115 | 111.2 | 108.3 | 104.2 | 103.7 | 102.6 | 102.3 | 101.7 | 100 | 97.9 | 96.6 | 93.7 | 90.5 | 88.7 | 85 | 83.2 | 81.9 | 63 | 58.6 | 53.7
Stampa

## Slide 8
Chimica delle specialità
Chimica come infrastruttura tecnologica
Materie prime organiche
Industria petrolifera
Energia
Aria
Acqua
Industria estrattiva
Processo
chimico
Materie prime inorganiche
Carta
Consumo
Costruzioni
Gomma/plastica
Agricoltura
Servizi
Tessile/cuoio
Mobile
Auto
Alimentare
Metalli
Meccanica
Beni intermedi
Chimica di base e fine
Processo
chimico

## Slide 9
Infrastruttura tecnologica per il Made in Italy
La chimica è il turbo del Made in Italy
Flessibilità
Personalizzazione
Innovazione
Specializzazione
Biella - Prato
tessile
Como
seta
Brianza - Alto Livenza
arredamento
Premana
forbici
Milano - Varese
plastica
Bergamo
bottoni
Sassuolo
ceramica
Castel Goffredo
calze da donna
Vigevano
calzature
Verona - Alpi Apuane
marmi
Rossano Veneto
selle per biciclette
Cadore
ottica
Pesaro
cucine
Solofra Arzignano - S.Croce
concia
Vicenza - Arezzo
oreficeria
Montebelluna
calzature sportive
Rimini - Forlì - Pesaro
mobili
Bologna
imballaggio
Fermo
footwear
Le Murge
divani

## Slide 10
Specializzazione italiana
nella Chimica fine e delle specialità
Fonte: Istat, Eurostat, anno 2015
Quota della Chimica a valle (% sul totale del valore della produzione)
Note: la chimica a valle comprende la chimica fine, specialistica e per il consumo
Chart: 
 | 57.0246 | 42.9754
UE
Italia
45%
57%
Saldo commerciale della Chimica fine e delle specialità (milioni di euro)
Chart: 
 | 45.1469 | 54.8531
2007
2009
2011
2013
2015
2017
Chart: 
 | 1006 | 938 | 203 | 526 | 534 | 1078 | 1945 | 2503 | 2738 | 3171 | 3262

## Slide 11
Da Chimica 1.0 a Chimica 4.0
Chimica 1.0 Chimica del Carbone
Chimica 2.0 Petrolchimica
Chimica 3.0 Specialità e Globalizzazione
Chimica 4.0 Digitalizzazione? Economia circolare?
Bioeconomia?

## Slide 12
“European Chemicals Industry,
Enabler of a Sustainable Future”
«Le principali sfide dell’umanità richiedono nuove soluzioni molte delle quali possono essere implementate solo grazie a nuovi materiali e sostanze»
Sostenibilità alimentare
Cambiamento climatico
Uso più efficiente delle risorse
Nuove esigenze connesse all’invecchiamento

## Slide 13
Tanta Chimica negli obiettivi ONU

## Slide 14
  Crescente costo
  della regolamentazione
Chart: 
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Prodotti chimici | 21.3151 | 19.3523 | 20.6149 | 26.8247 | 46.3654 | 57.8214 | 58.3591 | 55.8999 | 57.8461 | 58.6286 | 58.0111
Energia | 15.7577 | 7.901 | 8.5716 | 8.5716 | 9.7119 | 12.9874 | 12.9874 | 12.9874 | 13.2018 | 21.1915 | 34.4365
Emissioni e processi industriali | 24.4263 | 23.6624 | 24.4807 | 29.7206 | 37.3936 | 53.8317 | 65.0632 | 62.5813 | 62.8678 | 77.2659 | 75.1461
Sicurezza dei lavoratori | 36.0638 | 36.0638 | 36.0638 | 36.0638 | 36.0638 | 36.0638 | 36.0638 | 36.0638 | 36.0638 | 36.0638 | 36.0638
Trasporti | 0 | 0 | 0 | 0 | 1.8922 | 6.2102 | 6.2102 | 6.2102 | 6.2102 | 6.2102 | 6.2142
Specifici prodotti chimici | 1.8813 | 2.5284 | 0.64716 | 0.64716 | 0.64716 | 2.1972 | 2.1972 | 2.9781 | 2.9781 | 2.9781 | 2.9781
Commercio e dogane | 0.55581 | 0.55581 | 0.55581 | 0.55581 | 0.55581 | 0.55581 | 0.55581 | 0.55581 | 0.55581 | 0.55581 | 0.55623
Costi della regolamentazione per l’industria chimica europea
(indici 2004=100)
Costi della regolamentazione per l’industria chimica europea
(%, media 2004-2014)
Chart: 
| valore aggiunto | RLG
Chimica | 12.1 | 30.1
% sul valore aggiunto
% sul risultato lordo di gestione
Fonte: CCA Report, «Cumulative Cost Assestement for the EU Chemical Industry», Technopolis Group, 2015

## Slide 15
REACH is the European Regulation on Registration, Evaluation, Authorisation and Restriction of Chemicals. It entered into force in 2007, replacing the former legislative framework for chemicals in the EU.
REACH shifts the responsibility from public authorities to industry with regards to assessing and managing the risks posed by chemicals and providing appropriate safety information for their users. It impacts on a wide range of companies across many sectors beyond the chemical industry. It requires new forms of cooperation among companies, enhancing communication along the supply chain.
Objectives of REACH
The main aims of REACH are to ensure a high level of protection for human health and the environment.
https://ec.europa.eu/growth/sectors/chemicals/reach_en

## Slide 16
NO DATA NO MARKET!
Register information in the data-base of the European Chemical Agency

## Slide 17
-80% emissioni in acqua dal 1989 -95% emissioni in aria dal 1989 -62% emissioni di gas serra dal 1990
Fonte: Federchimica - Responsible Care ®, ENEA – ODYSSEE Project, ISPRA, Istat, ICCA - McKinsey
1 tonnellata di CO2 emessa per la produzione chimica evita 2,6 tonnellate di gas serra da parte dei clienti industriali o dei consumatori finali
Sostenibilita: dall’innovazione di processo all’innovazione di prodotto
Notes: Beyond any prejudice, chemical industry gives a fundamental contribute in terms of environmental sustainability.
Not only it has drastically reduced its emissions in the last 25 years, but it also helps to reduce emissions of downstream users: every 1 tons of CO2 emitted for chemical production prevents 2,6 tons of greenhouse gas emitted from industrial customers or end users.

## Slide 18
Industry | Product scale (t/year) | Kg waste / Kg product (E factor)
Oil refining | 106-108 | <<0.1
Bulk chemicals | 104 - 106 | 1-5
Fine chemicals | 10- 104 | 5 - 50
Production of waste by various branches of chemical industry
Sheldon R.A., Green Chemistry, 2007, 9, 1273-1283.
Pharma | 1- 103 | 25 - > 100
CHEMISTRY ENVOROMENTAL IMPACT!

## Slide 20
Environmental quotient, EQ,
EQ = Environmental Factor × Q
http://www.sheldon.nl/bi/EFactor.aspx
What is important is the environmental impact of this waste, not just its amount. One kg of sodium chloride is obviously not equivalent to one kg of a chromium salt.
EQ, is obtained by multiplying the E factor with an arbitrarily assigned unfriendliness quotient, Q. For example, one could arbitrarily assign a Q value of 1 to NaCl and, say, 100-1000 to a heavy metal salt, such as chromium, depending on its toxicity, ease of recycling, etc. The magnitude of Q is obviously debatable and difficult to quantify but, importantly, ‘quantitative assessment’ of the environmental impact of chemical processes is, in principle, possible.

## Slide 21
Steps of an industrial chemical process
The efficiency and sustainability of a process depend on all steps taken as a whole

## Slide 22
12 Principles of Green Chemistry
Developed by Paul Anastas and John Warner:
the list outlines an early conception of what would make a greener chemical, process, or product.
Anastas, P. T.; Warner, J. C. Green Chemistry: Theory and Practice, Oxford University Press: New York, 1998, p.30. B

## Slide 23
Anastas, P. T.; Warner, J. C. Green Chemistry: Theory and Practice, Oxford University Press: New York, 1998, p.30. B
Prevention It is better to prevent waste than to treat or clean up waste after it has been created.
Atom Economy Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
Less Hazardous Chemical Syntheses Wherever practicable, synthetic methods should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
Designing Safer Chemicals Chemical products should be designed to affect their desired function while minimizing their toxicity.

## Slide 24
Anastas, P. T.; Warner, J. C. Green Chemistry: Theory and Practice, Oxford University Press: New York, 1998, p.30. By permission of Oxford University Press.
Prevention It is better to prevent waste than to treat or clean up waste after it has been created.
Atom Economy Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
Less Hazardous Chemical Syntheses Wherever practicable, synthetic methods should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
Designing Safer Chemicals
Safer Solvents and Auxiliaries The use of auxiliary substances (e.g., solvents, separation agents, etc.) should be made unnecessary wherever possible and innocuous when used.
Design for Energy Efficiency Energy requirements of chemical processes should be recognized for their environmental and economic impacts and should be minimized. If possible, synthetic methods should be conducted at ambient temperature and pressure.
Use of Renewable Feedstocks A raw material or feedstock should be renewable rather than depleting whenever technically and economically practicable.
Reduce Derivatives Unnecessary derivatization (use of blocking groups, protection/ deprotection, temporary modification of physical/chemical processes) should be minimized or avoided if possible, because such steps require additional reagents and can generate waste.
Catalysis Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
Design for Degradation Chemical products should be designed so that at the end of their function they break down into innocuous degradation products and do not persist in the environment.
Real-time analysis for Pollution Prevention Analytical methodologies need to be further developed to allow for real-time, in-process monitoring and control prior to the formation of hazardous substances.
Inherently Safer Chemistry for Accident Prevention Substances and the form of a substance used in a chemical process should be chosen to minimize the potential for chemical accidents, including releases, explosions, and fires.

## Slide 25
Anastas, P. T.; Warner, J. C. Green Chemistry: Theory and Practice, Oxford University Press: New York, 1998, p.30. By permission of Oxford University Press.
Prevention It is better to prevent waste than to treat or clean up waste after it has been created.
Atom Economy Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
Less Hazardous Chemical Syntheses Wherever practicable, synthetic methods should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
Designing Safer Chemicals
Safer Solvents and Auxiliaries The use of auxiliary substances (e.g., solvents, separation agents, etc.) should be made unnecessary wherever possible and innocuous when used.
Design for Energy Efficiency Energy requirements of chemical processes should be recognized for their environmental and economic impacts and should be minimized. If possible, synthetic methods should be conducted at ambient temperature and pressure.
Use of Renewable Feedstocks A raw material or feedstock should be renewable rather than depleting whenever technically and economically practicable.
Reduce Derivatives Unnecessary derivatization (use of blocking groups, protection/ deprotection, temporary modification of physical/chemical processes) should be minimized or avoided if possible, because such steps require additional reagents and can generate waste.
Catalysis Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
Real-time analysis for Pollution Prevention Analytical methodologies need to be further developed to allow for real-time, in-process monitoring and control prior to the formation of hazardous substances.
Inherently Safer Chemistry for Accident Prevention Substances and the form of a substance used in a chemical process should be chosen to minimize the potential for chemical accidents, including releases, explosions, and fires.

## Slide 26
Anastas, P. T.; Warner, J. C. Green Chemistry: Theory and Practice, Oxford University Press: New York, 1998, p.30. By permission of Oxford University Press.
Prevention It is better to prevent waste than to treat or clean up waste after it has been created.
Atom Economy Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
Less Hazardous Chemical Syntheses Wherever practicable, synthetic methods should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
Designing Safer Chemicals
Safer Solvents and Auxiliaries The use of auxiliary substances (e.g., solvents, separation agents, etc.) should be made unnecessary wherever possible and innocuous when used.
Design for Energy Efficiency Energy requirements of chemical processes should be recognized for their environmental and economic impacts and should be minimized. If possible, synthetic methods should be conducted at ambient temperature and pressure.
Use of Renewable Feedstocks A raw material or feedstock should be renewable rather than depleting whenever technically and economically practicable.
Reduce Derivatives Unnecessary derivatization (use of blocking groups, protection/ deprotection, temporary modification of physical/chemical processes) should be minimized or avoided if possible, because such steps require additional reagents and can generate waste.
Catalysis Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
Design for Degradation Chemical products should be designed so that at the end of their function they break down into innocuous degradation products and do not persist in the environment.
Real-time analysis for Pollution Prevention Analytical methodologies need to be further developed to allow for real-time, in-process monitoring and control prior to the formation of hazardous substances.
Inherently Safer Chemistry for Accident Prevention Substances and the form of a substance used in a chemical process should be chosen to minimize the potential for chemical accidents, including releases, explosions, and fires.

## Slide 27: Comparison between stoichiometric and catalytic reactions
Atom Utilisation: catalyst is regenerated

## Slide 28
Sugar
Fats
Aminoacids
Etc…
Chemicals
Materials
Drugs
Fuels
bioconversion
The cell:
The most complex and efficient
chemical laboratory
at low environmental impact

## Slide 30
Insoluble immobilized industrial enzyme

## Slide 31: Some comparison between chemical and biocatalyzed processes

## Slide 32
Chemical vs enzymatic reactions:
Peptides and proteins are hydrolyzed chemically at very harsh conditions:
Options:
a)Aqueous HCl 6M, 100 °C for several hours
b)Sodium hydroxide
Increasing the energy of the system: Highly active reactants

## Slide 33
Enzymes make reactions happen at mild teperature and pH
Decreasing energy by stabilization: CATALYSIS

## Slide 34
Subtilisine from Bacillus specie: digests proteins under mild conditions
In 2002 produced 900 tons for additives in detergents
Also known as Subtilisin Carlsberg
A serine protease

## Slide 35: Why traditions matter!
A statue of company founder Jacobson. C. Carlsberg stands outside the Carlsberg Laboratory in Valby, Copenhagen.
“Jacobson specifically wanted a laboratory that expanded science for the benefit of society,” Its charter declares that “the principal task of The Carlsberg Laboratory shall be to develop as complete a scientific basis as possible for malting, brewing and fermenting operations.” And on the wall of the building’s central grand staircase, the following mantra is inscribed in gold leaf: “No result of the Laboratory’s activities which is of theoretical or practical importance shall be kept secret.”
Carlsberg Foundation was founded in 1876 and owns 30.3% of the shares in Carlsberg Group and has 74.2% of the voting power.

## Slide 36
DK
Microorganisms
Feed enzymes
Food enzymes
Technical enzymes
World leaders in enzymes & microorganisms
Research
Production
Sales offices
Others
Novozymes
DSM
Genencor
6%
20%
25%
45%
4%
BASF
Biocatalysis
Small part to increase

## Slide 37
http://www.novozymes.com
The global market for enzymes was estimated at about 4.5 bln dollar in 2012 and is expected to grow at almost 8 bln dollar in 2020. Europe is the world leader in key industrial biotechnologies such as enzyme technologies, with Novozymes from Denmark holding a market share of >45% worldwide.
Source. Festel G., Detzel C. and Maas R., Industrial Biotechnology – Markets and industry structure, Journal of Commercial Biotechnology, Volume 18, No. 1, 2012

## Slide 41: Figura 11.5 Effetto del cambiamento di energia di reagenti e stato di transizione sulla velocità di reazione. (a) Un’energia dei reagenti più elevata (curva rossa) corrisponde ad una reazione più veloce (DG‡ più piccolo). (b) Un’energia dello stato di transizione più alta (curva rossa) corrisponde a una reazione più lenta (DG‡ più grande).
How can we accelerate chemical reactions?
-using more reactive substrates (high energy, low selectivity, side products)
-decreasing the energy of the transformation path through stabilization of the highest energy state.
Increasing the energy of the system: Highly active reactants
Decreasing energy by stabilization: CATALYSIS

## Slide 42
How can enzyme hydolyse the peptide bond at room temperature and neutral pH?
Why enzymes are more efficient than «chemists»??
Enzymatic reaction

## Slide 43
A serine protease mechanism .
NHR2
H2NR2
Acyl-enzyme intermediate
Nu
Chemical reaction

## Slide 44
«……the catalytic power of enzymes is largely due to the preorganized electrostatic environment of their active site»
A Warshel et al, Chem Rev,
2006, 106, 3210.
Nobel laureate for chemistry 2013

## Slide 45
Oxyanion hole
Stabilizes the tetrahedral intermediate
Serine Hydrolase enzymes active sites:
pre-organized reaction environments
The energy cost is paid during the protein/enzyme synthesis
Nature does not save matter: differentiation and selection

## Slide 46
A serine protease mechanism: pre-organized reaction environment
Oxyanion hole
Stabilizes oxyanion of the intermediate
Ser
H2NR2
Acyl-enzyme intermediate
+
Chemical reaction
able to decrease the energy of the transition state of the rate determining step

## Slide 47
H2NR2
A serine protease mechanism: different synthetic routes by changing the nucleophile .

## Slide 48
Serin hydrolases can catalyze the synthesis of peptide bond by changing the nucleophile and working under dry conditions
+ H2O

## Slide 49: Enzymatic synthesis of Aspartame in industry
Mild conditions: no racemization, less side products
Moving from natural to non-natural substrates: industrial synthesis of dipeptide Aspartame
T
h
e
r
m
o
l
y
s
i
n
H
2
O
,
p
H
=
6
-
7

## Slide 50: Meccanismo di formazione dell’anidride simmetrica a partire dall’O-acilisourea
Chemical routes for the synthesis of peptide bonds:
Amino and carboxy groups must be protected
Acyl group must be activated!! Promotes racemization!!!
Urea,
Side product
Organic
solvent

## Slide 51
Fine-pharma chemistry
Major biotransformations at industrial scale 1.

## Slide 52: In some cases biocatalyst is the ONLY option

## Slide 53
Use of whole cells for the production of acrylamide
time
Cell density
Production of acrylamide by hydration of acrylonitrile using whole bacterial cells (Pseudomonas chloraphis, Rhodococcus rhodochrous).
industrial scale > 30,000 tonnes / year
Yields >99%
formation of by-products ( acrylic acid ) completely avoided

## Slide 54
Ampicillin
Penicillina G
Natural product (secondary methabolite) abtained through fermentation: not used any longer for terapeutic use
Allergenic, degraded when administered by os, narrow spectrum
Antibiotici beta-lattamici: penicilline
Semisiynthetic antiobitic: next generation
Penicillin G amidase in the hydrolysis of Pen G to 6-APA (precursor of semi-sintetic beta-lactam antibiotics (41% of the whole antibiotic market)

## Slide 55
Penicillin G amidase in the hydrolysis of Pen G to 6-APA (precursor of semi-sintetic beta-lactam antibiotics
Penicillin G amidase:PGA
Market: 10 - 30 tons of immobilized/insoluble PGA consumed per year
Enzymatic process
Chemical process
T <-50°C

## Slide 56
Selective + Sustainable
Reduction of process costs
65% of energy saving
Reduction of wastes (1/5)
50% reduction of cost for beta-lactam antibiotics production
Why biocatalysis? The drivers
Economy
Regulations

## Slide 57: Annexes

## Slide 58: I dodici principi della chimica verde
1. La prevenzione alla produzione di rifiuti risulta essere più conveniente rispetto al trattare o detossificare i rifiuti dopo che essi siano stati formati.
2. I metodi di sintesi dovrebbero essere messi a punto in modo da poter permettere il massimo utilizzo dei materiali impiegati, consentendo così rese elevate dei prodotti desiderati.
3. Per quanto possibile, le metodologie di sintesi dovrebbero essere ideate per usare o generare sostanze che abbiano minima o nessuna tossicità per la salute umana e l’ambiente.
4. I prodotti chimici devono essere progettati per mantenere l’efficacia della funzione, riducendone la tossicità.
5. L’uso di sostanze ausiliarie deve essere reso innocuo o non necessario.
6. Il fabbisogno energetico dovrebbe essere valutato secondo l'impatto ambientale ed economico, riducendolo al minimo. I metodi di sintesi devono essere condotti a temperatura e pressione ambiente.

## Slide 59: I dodici principi della chimica verde
7. Una materia prima rinnovabile dovrebbe essere preferita ad una non rinnovabile, qualora questo sia tecnicamente ed economicamente possibile.
8. Bisognerebbe ridurre i prodotti secondari laddove possibile.
9. I catalizzatori (il più selettivi possibile) risultano essere migliori rispetto i classici reagenti stechiometrici.
10. I prodotti chimici devono essere progettati in modo tale che al termine della loro funzione non persistano nell’ambiente e diano prodotti di degradazione innocui.
11. Le metodologie analitiche devono essere sviluppate per impedire in tempo reale, durante i processi di controllo, la formazione di sostanze nocive.
12. Il tipo di sostanza e lo stato della sostanza, usati durante i processi chimici, devono essere scelti in modo da ridurre il rischio di incidenti, come rilasci, esplosioni ed incendi.

## Slide 60
L'utilizzo dei solventi organici costituisce un ulteriore problema nell'ambito della chimica verde: I solventi non sempre riescono ad essere riciclati. L'impiego di questi in processi costituiti da reazioni multi-stadio causa solitamente delle contaminazioni crociate
i solventi sono le sostanze che contribuiscono maggiormente all'ottenimento di valori elevati di E. Factor durante i processi di lavorazione
i solventi costituiscono, nelle sintesi chimiche, l'80% della massa totale delle sostanze coinvolte L'acqua è un buon solvente, essendo non tossica, non infiammabile, disponibile su larga scala ed economica. Nelle reazioni in cui vengono utilizzati i catalizzatori, grazie alla presenza dell'acqua, si possono associare dei sistemi bifasici acquosi. Il catalizzatore risiede nella fase acquosa, mentre il prodotto si trova nella fase organica. In questo modo il catalizzatore può essere recuperato e riciclato attraverso una semplice separazione di fase.
OBIETTIVO: USARE ACQUA O SISTEMI CONCENTRATI E POSSIBILMENTE «bulk» senza solvente