## Slide 1: Denavit-Hartenberg
D-H define the relative position and orientation of two consecutive links: uniquoness
In general, the frames can be arbitrarily chosen as long as they are attached to the link they are referred to

## Slide 2: Denavit-Hartenberg
Numerate the links
Numerate the joints
Choose axis z_i along the axis of Joint i+1 (verse is arbitrary)
Minimum distance line or common normal (red lines)
  (it is perpenduclar to both the z axis)
Locate the origin Oi at the intersection of axis z_i with
  the common normal to axes
Choose axis xi along the common normal
  with direction from Joint i to Joint i + 1
Choose axis yi and zi so as to complete a right-handed frame

## Slide 3: Denavit-Hartenberg

## Slide 4: Case in which the DH doesn’t provide a unique definition of the link frame
For Frame 0, only the direction of axis z0 is specified; then x0 can be arbitrarily chosen.
DH introduces a constraint:
zi-1 ┴ xi
To identify the frame it is necessary a previous kinematic joint (which is not present on the base)

## Slide 5
For Frame n, since there is no Joint n+ 1, zn is not uniquely defined while xn has to be normal to axis zn-1.
Typically, Joint n is revolute, and thus zn is to be aligned with the direction of zn_1.

## Slide 6
When two consecutive axes are parallel, the common normal between them is not uniquely defined.
When two consecutive axes intersect, the direction of xi is arbitrary
6
5
4
x4
x4

## Slide 7: Case with prismatic joint

## Slide 8: D-H parameters (4 parameters)
Coordinate transformation between Frame i and Frame i - 1
Translate the chosen frame by di along axis zi-1
and
rotate it by θi about axis zi_1

## Slide 9
Translate the chosen frame by ai along axis xi
and
rotate it by αi about axis xi

## Slide 10: Three-link planar arm
z
y
If an end-effetor is required

## Slide 11: Spherical Arm

## Slide 12: Anthropomorphic Arm

## Slide 13: Spherical wrist

## Slide 14: DLR robot (Kuka)

## Slide 16: Example: D-H applied to UR10