## Slide 1: Collaborative robotics
Robotics
a.a. 2020-2021

## Slide 2: Definition
Collaboration
The action of working with someone to produce or create something.
something

## Slide 3: Safety
Industrial robots are:
  Large, powerful
  Huge mechanical advantage compared to humans
  Dangerous
Historical solution:
  Cage

## Slide 4: Safety regulation
Robotics era
  1970 Occupational Health & Safety Act
USA: Robotic Industries Association (RIA)
  ANSI/RIA R15.06 robot safety standard (1986)
  Updated in 1992, 1999, withdrawn 2014
EU: International Standards Organization (ISO)
  Based on ANSI/RIA R15.06
  ISO 10218 first edition (1999)
USA:
  ANSI/RIA R15.06 adopts ISO 10218-1 and ISO 10218-2:2011
  ANSI/RIA R15.306-406-506 published

## Slide 5: Safety regulation
1970 | Occupational Health & Safety Act
1986 | Publication of ANSI/RIA R15.06 1986 robot safety standard
1992 | Publication of ANSI/RIA R15.06 1992
1999 | Publication of ANSI/RIA R15.06 1999
 | Publication of ISO 10218 First Edition – based on ANSI/RIA R15.06
2006 | Publication of ISO 10218-1 (collaborative applications)
2011 | Publication of ISO 10218-1 and ISO 10218-2: 2011 (introduction of cobot)
2012 | ANSI/ RIA R15.06 adopts ISO 10218-1 and ISO 10218-2:2011
2014 | ANSI/ RIA Tech Reports published (TR R15.306, .406, .506
2016 | Publication of ISO/TS 15066:2016 in addition to ISO 10218 for cobots

## Slide 6: Safety requirements
ANSI/RIA and ISO documents were different
  ANSI/RIA addressed how the robot was employed
  ISO addresses safety requirements for manufacturers
The prevailing idea was to keep the robot away from humans
  Early actuators were less controllable
  Less-capable sensing capabilities (both because of hardware and software)

## Slide 7: Modern Safety Regulation
ISO TC184/SC2 WG3 for Industrial Robots
Publication of ISO 10218-1 in 2006
  Dedicated to only the robot
  Considers safety-rated control software
  New types of safety sensors
  Results in many new possibilities
Publication of ISO 10218-2:2011
  Collaborative robots

## Slide 8: Safety principles
Collaborative robotics

## Slide 9: Risk
It can also be determined with a probabilistic approach:
  damage
  probability of the damage happening
Hazard
Exposure
Vulnerability
Risk
More or less:

## Slide 10: Hazards
Robots pose hazard because of:
  Inertia
    Mass , velocity , momentum (impact energy!)
  Structure
    Crush-hazard through pinching (e.g. joints/between links)
    Penetration-hazard (e.g. a sharp edge on the tool)
  Process forces
    Crush-hazard due to operations which require high forces (e.g. handling of heavy loads)

## Slide 11: Exposure
Being close to the robot
  This means being inside its workspace
  In case of mobile robots the workspace is boundless (!)
Robot workspace
Human workspace

## Slide 12: Vulnerability
Humans are vulnerable for:
  Blunt impacts (with energy > some level)
  Penetrating/cutting impacts
  Abrasion
  Crushing (applied forces)

## Slide 13: Risk reduction strategies
Collaborative Robotics

## Slide 14: Risk reduction strategies
How do we reduce risk?
  Lowering the hazards
  Lowering the exposure
  Lowering the vulnerability
Hazard
Exposure
Vulnerability
Risk
Or combinations...

## Slide 15: Exposure reduction
Hystorically the first one
Reduces or avoids exposure entirely
Use of fences\cages\cells
Addition of safeguards
Very effective
Severely limiting
Can be disregarded by the user
Introduces points of failure of the safeguards themselves
  Doors switches, etc.
  Vision systems, laser scanners, etc.
Increases downtime (need to stop the robot to perform operations in the cage)

## Slide 16: Vulnerability reduction
The idea is to render the human less vulnerable
Limited risk-limiting potential
The only possibility is using Personal Protective Equipment (PPE)
  Useful only to a certain extent
  Generally not sufficient by the safety regulations

## Slide 17: Hazard reduction
The modern approach is that of reducing the damaging potential of robots!
Several ways to achieve this:
  Padding
  Monitored stops
    Speed and separation monitoring
    Power and force limitations
  Perception and sensing
  etc.

## Slide 18: Exposure reduction
Collaborative Robotics

## Slide 19: Safeguarding systems
Devices that enforce safety around the robot
  Cell or cage
  Fences
  Gates
  Sensing systems

## Slide 20: Safeguarding systems
Doors with switches

## Slide 21: Safeguarding systems
Safety perimeter enforcing

## Slide 22: Safeguarding systems
Light curtains

## Slide 23: Safeguarding systems
Issues:
  Stop-time increases
    The robot needs to be completely stopped to enter the cell
    False alarms
  Severely limits collaborative tasks between the robot and the human
  People defeating the safeguarding system in order to perform maintenance etc.
    Leads the worker to be exposed to an unsafe robot
    Very high level of exposure + very high hazard!
  Complexity (and thus cost) can be high

## Slide 24: Hazard reduction
Collaborative Robotics

## Slide 25: Hazard reduction
This is the approach for collaborative robots
The idea is limiting the potential for the robot to do harm to the human

## Slide 26: Padding

## Slide 27: Sensorized padding

## Slide 28: Safe joint design

## Slide 29: Safety-rated Monitored Stop
Obstacle or operator in the workspace
  Stop-motion condition triggers and is enforced
  Drive power remains on
  Motion resumes normally when obstruction clears
  Robot motion resumes without intervention
  Protective stop delivered if stop condition violated
Applications
  Direct part loading or unloading
  Work-in-process inspections
  Standstill function in other collaborative operations

## Slide 30: Hand-guiding
The operator leads robot movement through direct manipulation of the end-effector
  Robot stops when operator arrives (safety-rated monitored stop)
  Operator grasps enabling device, activating motion
  Non-collaborative operation resumes when operator leaves workspace
Applications
  Robotic lift assist
  Highly variable applications (e.g. painting, assembly)
  Limited or small-batch production

## Slide 31: Dead-man Switch
Device that needs to be kept in a certain position actively
Upon release it deactivates the robot/robot cell
Some variations are force-sensitive switches
  Release is made:
  When force is too low (releasing)
  When force is too high (clutching)
Also 3-way switch (same principle as force)

## Slide 32: Speed and separation monitoring
The robot speed reduces when an obstruction is detected
  Separation distances are monitored (scanners, vision systems, proximity sensors)
  Robot speed directly correlates to separation distance
  Zones dictate allowable speed
  Stop condition given if direct contact proximity is attained (Safety-rated monitored stop)
Applications
  Simultaneous tasks
  Direct operator interface

## Slide 33: Speed and separation monitoring
Video warning-critical zones
Video real-time zones
Video protected space + speed monitoring

## Slide 34: Power and Force Limiting
This is the case of the UR10!
Where incidental contact initiated by robot are limited in energy to not cause operator harm
Forces robot can exert are limited
Robot system design eliminates
  pinch points
  sharp edges, etc.
Robot complies and reacts when contact is made
Applications
Small components or highly variable applications
Conditions requiring frequent operator presence
Machine tending
Loading/unloading

## Slide 35: Power and Force Limiting
There were limitations in force:
  ISO 10218-1:2006 Power 80 W, force 150 N
  ISO 10218-1:2011 Removed
Rationale:
  It depends too much where force is applied!
  Examples:
    1 N in an eye is still too much (underestimation)
    200 N of distributed force without pinch/crush is low (overestimation)
    149 N + pinch can cause harm! (underestimation)

## Slide 36: Pinch points elimination
Pinch points can cause harm even with small forces
Can exist even in-between joints in the robot itself

## Slide 37: Power and Force Limiting
Force limits depend by many things:
  Pinch/crush points
  Robot velocity (thus momentum)
  Robot mass (thus inertia)
  Robot pose (increasing surface impact area)
  Avoid sensitive body areas (head, neck, eyes)
The application, not the robot, is key!

## Slide 38: Cobots implementation
Collaborative Robotics

## Slide 39: Consequences of cobots implementation

## Slide 40: How far can we go?

## Slide 41: Absence of Intent Signalling
Humans are able to signal for intent:
  E.g. moving in a certain direction, hitting in some spot, etc.
  Cobots are not like this!
Solutions:
  Simulations
  Intent signalling: lights, displays, tactile (e.g. vibration), …

## Slide 42: Machine tending
Video CNC tending, Video CNC tending & defects detection

## Slide 43: Packaging
Video Packaging