## Slide 1: Mobile Robotics Part II.2
Robotics and Mechatronics
a.a. 2020-2021

## Slide 2: Relative Position sensing
Mobile Robotics

## Slide 3: Relative position sensors
Relative position sensors
  They provide a signal proportional to the displacement measured between a part and a reference position
  Linear
    Linear potentiometers, linear encoders
  Angular
    Potentiometers, rotary encoders, resolvers

## Slide 4: Principle
Transducer
Physical quantity
Digital signal
Position:
Linear
Angular
Digital signal
Transduction

## Slide 5: Encoders type
Incremental
  Measures single increments
  Requires definition of a reference
Absolute
  Measures the position relative to a reference
  Immediate measure
  Reference is intrinsic

## Slide 6: Incremental encoders Structure and function
One or more slits array
Measurement of single increments
No intrinsic “memory”
Rotary incremental encoder

## Slide 7: Incremental encoders Principle
Emitter
Photodiode
Motion
time
Value
1
3
2
4…
Counts/steps
Signal
Linear incremental encoder

## Slide 8: Incremental encoders Reference
Requirement: reference
Options:
  Additional slit with the zero-reference
  Limits sensors directly on the joint

## Slide 9: Incremental encoders Direction determination (1)
Single slit array (quadrature enc.)
  Detects steps
  Does not differentiate direction
Double slit arrays
  Detect steps
  Detects direction
No difference detected
Emitters
Photodiode A
A
B
Photodiode B
A
B
0
0
0
1
1
1
1
0
0
0
0
1
1
1
…

## Slide 10: Incremental encoders Direction determination (2)
Emitters
Photodiode A
A
B
Photodiode B
A
B
0
0
0
1
1
1
1
0
0
0
0
1
1
1
…
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0

## Slide 11: Incremental encoders Operation
Sensor A
Sensor B
Comparison table
Step
Direction
Integrator
A
B
Current position:
where:
if clockwise, if anti-cw,
step

## Slide 12: Absolute encoders Structure and function

## Slide 13: Absolute encoders Principle
1
1
1
0
1
1
0
1
0
0
0
0
0°
45°
90°
135°
Position is ENCODED in the disk
0°
45°
90°
135°

## Slide 14: Absolute encoders Operation
Sensor track 1
Sensor track 2
Decoder
Sensor track 3
Sensor track n
…
Current position
Track 1 | Track 2 | Track 3 | Position
1 | 1 | 1 | 0°
0 | 1 | 1 | 45°
0 | 1 | 0 | 90°
0 | 0 | 0 | 135°
Track 3
Track 2
Track 1

## Slide 15: Encoder technologies
Mobile Robotics

## Slide 16: Incremental encoders Technologies
Electro-mechanical
Optical
Magnetic (Hall-effect)

## Slide 17: Incremental encoders Electro-mechanical
Typically used in electronics for hand-operated controls
Cheap component
Low accuracy due to limited number of contacts
Low durability due to wear

## Slide 18: Incremental encoders Optical
Typically used for high-fidelity measurements, high performance CNC machining, measurement systems, etc.
High accuracy with glass scales, etching etc.
High durability due to contactless operation
Expensive component

## Slide 19: Incremental encoders Magnetic (Hall-effect)
Sensor A
Sensor B
A
B
Typically used for medium-fidelity measurements: motor control, robot axis control
Good accuracy with proper installation and high-quality magnetized materials
High durability due to contactless operation
Medium-price component
N
S
N
S
N
S
N
S
N
S
N
S
N
S

## Slide 20: Incremental encoders Rating
Angular resolution is usually measured in pulses per revolution, P/R

## Slide 21: Absolute encoders Technologies
Electro-mechanical (impractical in most cases)
Optical
Magnetic (Hall-effect)
Capacitive
Pros and cons are the same as for incremental encoders

## Slide 22: Absolute encoders Optical
Rotor often made of etched/printed glass
Expensive

## Slide 23: Absolute encoders Magnetic (Hall-effect)
Can have 2 or more polar expansions
More poles higher accuracy
Analog to digital signal
N
S
Sensor A
Sensor B
A
B

## Slide 24: Absolute encoders Capacitive
Innovative approach
Similar principle to that of Hall-effect encoders
Sensor A
Sensor B
A
B

## Slide 25: Encoders Comparison