## Slide 1: Robotics Part II
a.a. 2020-2021

## Slide 2: Mechanisms and degrees of freedom
Robotics

## Slide 3: Mechanisms
Mechanism
  Device that transforms input forces and movement into a desired set of output forces and movement
Input
Forces
Motion
Output
Forces
Motion
Mechanism

## Slide 4: Mechanisms
Example:
Input
Torque
Rotation
Output
Force
Alternative motion
Mechanism

## Slide 5: Kinematic pairs
A kinematic pair is a connection between two bodies that imposes constraints on their relative movement.
For example:
  Revolute pair
  Prismatic joint
Allowed motion
Constrained motions

## Slide 6: Kinematic pairs
Screw joint
  Rotation and translation are dependent

## Slide 7: Kinematic pairs
Cylindrical pair
  Allowed motions:
    Translation
    Rotation
Allowed motions

## Slide 8: Kinematic pairs
Spherical pair
  Allowed motions:
    All rotations
Allowed motions

## Slide 9: Kinematic pairs
Other type of kinematic pairs
  Cams, and others…

## Slide 10: Degrees of freedom
The number of degrees of freedom (DOF) of a mechanical system (mechanism) is the number of independent parameters that define its configuration.
Parameters that allow independent motion.
Independent parameter
Independent parameter 1
Independent parameter 2

## Slide 11: Degrees of freedom
A body (e.g. a link) in 3D space has 6 DOF
  Translation along X, Y, Z (3 DOF)
  Rotation along X, Y, Z (3 DOF)
A body in 2D space (a plane) has 3 DOF
  Translation along X, Y (2 DOF)
  Rotation along Z (1 DOF)

## Slide 12: Degrees of freedom
Class of a kinematic pair
Number of free degrees of freedom that the pair allows
The type of class changes in relation to space:
  In 3D space
  In 2D space

## Slide 13: Class of kinematic pairs
Revolute joint
  In 2D
    Constrained: x, y motions
    Free: rotation
  In 3D
    Constrained:
      x,y,z motions
      rotations around x, z
    Free:
      rotation around y

## Slide 14: Class of kinematic pairs
Prismatic joint
  In 2D
    Constrained:
      y motion
      rotation
    Free: x motion
  In 3D
    Constrained:
      x,z motions
      rotations around x, y, z
    Free:
      y motion

## Slide 15: Class of kinematic pairs
Screw joint
  In 3D
    Constrained:
      x,z motions
      rotations around x, z
      relation: y motion rotation around y
    Free:
      Linked y motion and rotation around y

## Slide 16: Class of kinematic pairs
Cylindrical pair
  In 3D
    Constrained:
      x,z motions
      rotations around x, z
    Free:
      y motion
      rotation around y

## Slide 17: Class of kinematic pairs
Spherical pair
  In 3D
    Constrained:
      x, y, z motions
    Free:
      rotations around x
      rotations around y
      rotations around z

## Slide 18: Class of kinematic pairs
Guided spherical pair
  In 3D
    Constrained:
      x, y, z motions
      rotations around z
    Free:
      rotations around x
      rotations around y

## Slide 19: Mobility
Mobility formula (also Chebychev–Grübler–Kutzbach criterion)
Gives the mobility of a mechanism: its n. of DOFs
  3D
  2D
  is the number of DOF of the mechanism
  is the number of links (including the frame link)
  is the number of class kinematic pairs in the mechanism

## Slide 20: Mobility
Example:
Frame link
Open chain: no Frame link

## Slide 21: Hidden joints
A joint is a connection between 2 links
Joint is composed of 2 joints:
  Joint
  Joint
Notes: This has no redundant constraints; in fact, once accepted that the mechanism is
stationary, take out each link and see that the resulting mechanism is mobile.
This means that no redundant constraint is present.

## Slide 22: Special case: Redundant constraints

## Slide 23: Redundant constraints

## Slide 24: Redundant constraints
The first link on the left provides no additional constraint.
Equivalent

## Slide 25: Redundant constraints

## Slide 26: Special case: ?
Notes: This has redundant AND hidden constraints!

## Slide 27: Special case: ?
Redundant constraint!
Hidden constraint!
Notes: This has redundant constraints!

## Slide 28: Special case

## Slide 29: Special case
What if:
There are 3+5=8 DOF:
  3 can be thought of as the manipulation DOF of the E.E.
  5 can be considered parameters for the kinematic chain

## Slide 30: Special case
Why is this important?
Kinematically redundant robots

## Slide 31: Mobility
Example:
Serial manipulator
6 links + base ()
6 rotational joints ()
1
3
4
5
6
7
2
1
2
3
4
5
6

## Slide 32: Mobility
Example:
Serial manipulator
6 links + linear rail + base ()
6 rotational joints ()
1 prismatic joint ()

## Slide 33: Mobility
Example:
Serial manipulator
3 links + base ()
2 rotational joints ()
1 screw joint ()

## Slide 34: Mobility
Example:
2D Parallel manipulator
5 links + frame()
6 rotational joints ()

## Slide 35: Mobility
Example:
Serial manipulator
4 links + base ()
6 spherical joints ()
?

## Slide 36: Mobility
3-DOF
3-DOF

## Slide 37: Mobility
Example:
Serial manipulator
4 links + base ()
3 guided spherical joints ()
3 spherical joints ()

## Slide 38: Exercises: planar mechanisms
2D
Notes: solutions:
2 (hidden), 1, 0 (redundant), 0 (redundant),
3, 1, 1, 1

## Slide 39: Exercises: planar mechanisms
2D
Notes: solutions:
2 (hidden), 1, 0 (redundant), 0 (redundant),
3, 1, 1, 1

## Slide 40: Exercises: planar mechanisms
2D
Notes: solutions:
2 (hidden), 1, 0 (redundant), 0 (redundant),
3, 1, 1, 1

## Slide 41: Exercise: Gough-Stewart platform (1)
Linear actuator
Platform
Class 2 or 3 joints
Video

## Slide 42: Exercise: Gough-Stewart platform (2)
3D
Notes: % Soluzione 1 (sferici + prismatiche)
m = 6*2+2;
c1 = 6*1;
c2 = 6*1;
c3 = 6*1;
K= 6

## Slide 43: Exercise: Gough-Stewart platform (3)
3D
Notes: % Soluzione 1 (sferici guidati + cilindriche)
m = 6*2+2;
c1 = 6*0;
c2 = 6*3;
c3 = 6*0;
K= 6

## Slide 44: Exercise: Delta robot (1)
Actuator
End-effector
Frame
Link
Spherical joint

## Slide 45: Exercise: Delta robot (2)
First let’s locate indeterminate links
Notes: % Soluzione 1 (SOVRABBONDANTE)
m = 3*3+2; % 3*(2 link + leva) + base + ee
c1 = 3*1; % 3 motori
c2 = 3*0;
c3 = 3*4; % 3*4 giunti sferici su leva
K = 9 (-6)
% Soluzione 2
m = 3*3+2; % 3*(2 link + leva) + base + ee
c1 = 3*1; % 3 motori
c2 = 3*2; % 3*2 giunti sferici guidati su leva
c3 = 3*2; % 3*2 giunti sferici su ee
K = 3
% Soluzione 3 (LINK EQUIVALENTE)
m = 3*2+2; % 3*(2 link + leva) + base + ee
c1 = 3*1; % 3 motori
c2 = 3*2;
c3 = 3*0; % 3*4 giunti sferici su leva
6*(m-1) - 5*c1 - 4*c2 - 3*c3
K = 3

## Slide 46: Exercise: Delta robot (3)
3D
Notes: % Soluzione 1 (SOVRABBONDANTE)
m = 3*3+2; % 3*(2 link + leva) + base + ee
c1 = 3*1; % 3 motori
c2 = 3*0;
c3 = 3*4; % 3*4 giunti sferici su leva
K = 9 (-6)
% Soluzione 2
m = 3*3+2; % 3*(2 link + leva) + base + ee
c1 = 3*1; % 3 motori
c2 = 3*2; % 3*2 giunti sferici guidati su leva
c3 = 3*2; % 3*2 giunti sferici su ee
K = 3
% Soluzione 3 (LINK EQUIVALENTE)
m = 3*2+2; % 3*(2 link + leva) + base + ee
c1 = 3*1; % 3 motori
c2 = 3*2;
c3 = 3*0; % 3*4 giunti sferici su leva
6*(m-1) - 5*c1 - 4*c2 - 3*c3
K = 3

## Slide 47: Mobility
Example:

## Slide 48: Mobility
Example:

## Slide 49: Mobility
Example:
Notes: m = 9
n(c1) = 11
k = 3(9-1) – 2*11 = 24 – 22 = 2