## Slide 1: RadFrac – Rigorous method for multicomponent distillation
Maurizio Fermeglia
Maurizio.fermeglia@units.it
Department of Engineering & Architecture
University of Trieste

## Slide 2: Agenda
Introduction to RadFrac in ASPEN+
Setup
Results
Plotting results
Design specifications
Efficiencies, trays and packings
Distillation shortcut methods
Example

## Slide 3: Objectives
Understand the requirements for designing a rigorous separation column, starting from shortcut methods
Enter the minimum input required for the RadFrac fractional model
Implement Design Specification
Introduce column efficiency and hydraulic calculations

## Slide 4: RadFrac in Aspen Plus
Vapor-Liquid or Vapor-Liquid-Liquid phase simulation of:
  Ordinary distillation
  Absorption, reboiled absorption
  Stripping, reboiled stripping
  Azeotropic distillation
  Reactive distillation
Configuration options:
  Any number of feeds
  Any number of side draws
  Total liquid draw off and pumparounds
  Any number of heaters
  Any number of decanters

## Slide 5: RadFrac Flowsheet Connectivity
Decanter
Vapor Distillate
Heat
Liquid distillate
Water distillate
Side products
Pseudo Streams
Feed
Product
Return
Heat
Bottoms
Bottom Stage or Reboiler Heat Duty
Heat
Heat
Heat
Pumparound
Feed
Top-Stage or Condenser Heat Duty
Boil-up
Reflux
1
N-stage
Legend:
Optional stream
Heat stream
Material Stream

## Slide 6: RadFrac Setup Configuration Sheet
Specify:
  Calculation Type: Equilibrium, Rate-Based
  Number of stages
  Condenser and reboiler configuration: Total, Partial, Kettle, Thermosyphon, etc…
  Valid Phases
  Convergence
  Column operating specifications: Distillate Rate, Reflux Ratio, Distillate to Feed Ration, Condenser/Reboiler Duty, etc.

## Slide 7: RadFrac Setup Streams Sheet
Specify:
  Feed stage location
  Feed stream convention: Above stage, On-Stage, On-Stage-Liquid, On-Stage-Vapor, Decanter (for VLL calculations only)
  Bottom and overhead product streams
  Side products

## Slide 8: Feed Convention
n-1
n
Pre-Flash
Vn
Ln-1
Lfeed
Ln
Ln-2
Vfeed
Vn-1
Vn+1
Feed to stage n
Ln-2
n-1
n
Vn
Ln-1
Ln
Vn-1
Vn+1
Feed to stage n
Above-Stage (default)
RadFrac introduces the material stream between adjacent stages – the liquid portion flows to the specified stage and the vapor portion flows to the stage above
On-Stage
On-Stage: RadFrac introduces both liquid and vapor portions of the feed flow to the stage specified
On-Stage Liquid and On-Stage-Vapor: similar to On-Stage, but no flash is ever performed with these specifications. Feed is treated as being entirely in the phase specified

## Slide 9: RadFrac Setup Pressure Sheet
Specify one of:
  Top/Bottom Pressure: Pressure in Stage 1/Condenser represents column pressure if no pressure drop is specified. It is possible to specify pressure drop information on a stage-wise or full column basis
  Pressure profile
  Section pressure drop:

## Slide 10: RadFrac Setup Pressure Sheet
Pressure profile:
  This option allows the user to specify pressures for any stage in the column
  Stage pressure not entered (Stage 3 in this case) are linearly interpolated or extrapolated from specified values
Section pressure drop:
  This option lets the user specify pressures drop across any range of stages in the column
  Top Stage pressure is required

## Slide 11: RadFrac Results
Profiles:
  Temperature, Pressure, Flows, Heat of each stage
  Composition variations
  K-values (ratio of volatilities, partial pressures, mole frac, … of a component between two phases in equilibrium)
Results sheets:
  Info on Condenser and Reboiler
  Mass and Energy Balance
  Split fraction of components

## Slide 12: Plotting RadFrac Results
Use the Plotting Tool from the Home tab of the ribbon to quickly generate plot results of a simulation:
  Assay data analysis
  Physical property analysis
  Data regression analysis
  Profiles for all separation models including RadFrac, MultiFrac and PetroFrac
  Sensitivity Analysis
Provide additional information if requested, such as phases, components, etc…

## Slide 13: Define RadFrac parameters
We need to define these parameters:
  Number of stages
  Type of condenser/reboiler
  Any two of the available operating specifications
  Feed stage
  Pressure

## Slide 14: Using Design Specification
Design specifications can be specified inside the RadFrac block
  using Design Specs and Vary forms (in Specifications)
One or more RadFrac inputs can be manipulated (Vary)
  to achieve specifications for one or more RadFrac performance parameters
RadFrac Vary variables must be a input to the block (usually on the Specifications sheet):
  More complex columns have additional options
  Examples: pump around heater, stage duty, side draw rate
The number of Specs should, in most cases, be equal to the number of varies
Design Specification sheet
Vary sheet

## Slide 15: Specifying Efficiencies in RadFrac
RadFrac assumes total equilibrium on each separation stage
For non-ideal separation, you can specify Efficiencies
For trayed columns: Nstages= Ntrays+2
  Matches real equipment
  Enter efficiencies to match plant performance
RadFrac accepts Vaporization and Murphree efficiencies
Entered on component, stage or section basis

## Slide 16: Specifying Efficiencies in RadFrac
Specify efficiencies on Vapor-Liquid sheet
  Stages and efficiencies not entered are linearly interpolated from specified values
Murphree efficiencies are preferred as vaporization efficiencies can alter the temperature profile and thus relative volatilities

## Slide 17: Sizing and Rating for Trays and Packing
Extensive capabilities to size, rate, and perform pressure drop calculations for trayed and packed columns
Calculations are based on vendor-recommended procedures when available.
Tray and packing calculations do NOT affect column separation by default.
Rating specifications are used when performing cost analysis

## Slide 18: RadFrac Convergence Notes
Ensure that column operating conditions are feasible
Check that physical property issues are properly addressed
If the column err/tol is decreasing fairly consistently, increasing the max number of iterations (RadFrac | Convergence | Convergence | Basic Sheet
Convergence without Design Specs and Vary to initialize the column before adding (or revealing) specs and varys
Provide Temperature estimates for some stages in the column using RadFrac | Convergence | Estimates | Temperature sheet (for absorbers)
Provide composition estimates for some sates in the column using RadFrac | Convergence | Estimates | L and V Composition sheet (for non-ideal systems)
Consider different convergence methods on RadFrac | Specifications | Setup | Configuration Sheet
Remember to reinitialize the simulation every time!
18

## Slide 19: Demo RadFrac: Set up a methanol tower
Components Methanol - water
Property Method: NRTL-RK
Feed Stream:
  Mole fractions: 60 mole% methanol, 40 mole% water
  Mass Flow: 100 kmol/hr
  Pressure: 1.1 bar
  Condition: saturated liquid (V/F=0)
Radfrac column:
  31 trays
  Feed tray: 20
  Total condenser, kettle reboiler
  Top stage pressure: 1.1 bar
  Pressure drop per stage: 0.0005 bar
  Distillate to feed ratio: 0.598
  Molar reflux ratio: 0.496
Results:
  Any Warning?
  Heat Duties?
  Plot the compositions and understand what is going on
  Did we achieve a good separation? If not try to increase distillate rate to 60 kmol/hr and more

## Slide 20: Demo RadFrac: Set up a methanol tower
Results
  Separation not good: purity meOH in D= 0.938, purity water in B= 0.902
  Concertation profiles are flat for many stages around feed stage
Increase D/F to 0.65  purity meOH in D= 0.923, purity water in B= 1
Increase D/F to 0.70  purity meOH in D= 0.857, purity water in B= 1
Decrease D/F to 0.55  purity meOH in D= 0.938, purity water in B= 0.813

## Slide 21: Demo RadFrac: Set up a methanol tower
Add design specifications
  Des spec 1  purity MeOH in DISTIL
  Des spec 2  purity Water in BOTTOM

## Slide 22: Demo RadFrac: Set up a methanol tower
Results
Temperature
Flow rates

## Slide 23: Demo RadFrac: Set up a methanol tower
Results: compositions