## Slide 1: Mobile Robotics Part II.3
Robotics and Mechatronics
a.a. 2020-2021

## Slide 2: MAPPING
Mobile Robotics

## Slide 3: Environment mapping
Creation of a virtual map of the environment surrounding the robot
Contains information on:
  Obstacles
  Terrain geometry
  Locations and Points of Interest (POI) (e.g. goal)
  Position of the robot itself
Crucial for definition of traversability paths
Obstacles
Terrain
geometry
Robot position
POI

## Slide 4: Environment mapping
Map representation
  Metric framework
    2D or 3D space
    Records raw objects at precise coordinates
    Example:
      2D matrix
      Each pixel either contains an object (black) or doesn’t (white)
  Topological framework
    Records objects and places identifiers
    Records relations between objects/places
    Map is a graph

## Slide 5: Environment mapping
Type of map:
  Continuous
    Features are determined by mathematically defined objects
      Polygons, lines, points etc.
      High accuracy
      High computational cost
  Discrete
    Based on the decomposition of the environment in discrete elements
      Grids: occupancy grid
      Lower accuracy
      Large datasets

## Slide 6: Continuous maps
Geometric map
2D
Polygons as objects/walls

## Slide 7: Discrete maps
Occupancy grid-based map

## Slide 8: Discrete maps
Variable-cell occupancy grid-based map

## Slide 9: Discrete maps
Occupancy-grid

## Slide 10: Example of occupancy grid mapping

## Slide 11: Environment mapping
Rules:
  Precision of map precision of goals
  Precision of map accuracy of the sensors
  Complexity of map computational cost

## Slide 12: Position determination
Determination of the position/positions of the robot with respect to the environment.
  Position and orientation , i.e. with respect to the inertial frame
  Probability or accuracy information

## Slide 13: Position determination
Belief representation:
  Single unique position?
  Set of possible positions?
  How are they ranked?
Single-hypothesis
  The robot identifies one single unique position
  a certain probability distribution
Multiple-hypothesis
  The position is described in a fuzzy way
  This allows a better description of the degree of uncertainty

## Slide 14: Position determination
Single-hypothesis
Multiple-hypothesis
Continuous environment
Discrete environment

## Slide 15: Position determination
Reality
Occupancy grid-based map
Line-based map
Topological map
Continuous geometric map
Non-metric
Discrete geometric map

## Slide 16: Navigation
Mobile Robotics

## Slide 17: Navigation
Definition
  Determination of position and orientation relative to the environment,
  The planning and execution of the maneuvers required to get from point A to point B.

## Slide 18: Map-based Navigation

## Slide 19: Behavior-based navigation

## Slide 20: Position determination
Example: Odometry
Example: triangulation
Idiothetic sources
  Related to self-motion
  Uses proprioceptive sensors
    Number of wheel rotations,
    IMU
    Also called odometry or dead reckoning
Allothetic sources
  Related to external references
  Uses exteroceptive sensors
    Objects/obstacles
    Landmarks
    Terrain geometry
    Points of interest

## Slide 21: Example: odometry
Odometry
  We know at every instant
  We can calculate the configuration at time :
  Same thing can be done with an IMU, by knowing, which are the accelerations in the local frame of reference
Initial position

## Slide 22: Odometric error
Error adds up linearly (drift)
  Step 0 error:
  Step 1 error:
  Step n error:
Mitigation
  Fusion with other sensors, e.g. GPS/geographic locations etc.
Worst case scenario

## Slide 23: S.L.A.M. Simultaneous Localization and Mapping
The computational problem of simultaneously mapping the environment and localizing the robot within
Very computationally intensive
Implemented in varying ad-hoc architectures in the whole industry
  E.g. Autonomous cars

## Slide 24: Reactive navigation
Line following
  A somewhat «legacy» technology
    No mapping required,
    Limited position determination required,
    Simple sensors (IR or magnetic if the line is magnetized)
    Virtually zero flexibility
  Can be coupled to other more advanced form of navigation
Video logistics
Video carts

## Slide 25: Path planning
Aim: producing a continuous path between two points, A (start) and B (goal).
Several possible paths:
Approaches:
  Search algorithms
  Fields
A
B
Obstacles

## Slide 26: Path planning
A path-planning or navigation problem can be represented as a graph
  Weights can be assigned to the single branches to account for distance, slope, terrain, …
The aim is to find the shortest or best path through the nodes, from A to B
A
B
Nodes
A
B

## Slide 27: Path planning
Determination of the nodes
  Grid-based search
  Edge visibility graph
Search for optimal path This is achieved by graph exploration through efficient search algorithms:
  Dijkstra, A*, ...

## Slide 28: Edge visibility graph
The process is repeated for every visible edge
The result is a graph connecting point A to B

## Slide 29: Path planning
Example of graph navigation in matrix form
4 | 3 | 2 | 1 | 0
5 |  |  | 2 | 1
6 | 5 | 4 | 3 | 2
 |  |  | 4 | 3
8 | 7 | 6 | 5 | 4
A
B
Distance matrix
Step 1 Define matrix
Step 2 Find minimum distance path by selecting the lowest neighbor
Exact
Optimal

## Slide 30: Path planning
A larger example
  1000x1000 grid
  Long computation
B
A

## Slide 31: Path planning
Artificial potential fields
  Point A is starting point
  Obstacles are repulsors
  Goal B is an attractor
B
A

## Slide 32: Path planning
Potential where
Gradient
Path follows easily
Potential
Gradient

## Slide 33: Example of artificial potential fields

## Slide 34: The “real world” issue
Mobile Robotics

## Slide 35: «The Real World»
Issues in the real world
  Geometry of the terrain
    Loss of contact with the ground
    Slopes
  Terrain yield
    Traction loss
    Sinking
  Position determination accuracy

## Slide 36: Terrain geometry
Loss of contact
  Up to this moment we have dealt with flat ground
    Simultaneous contact with all wheels
  Discontinuities loss of contact
  Possible solutions
    Three wheeled systems
    Suspension systems
    Rocker-bogie

## Slide 37: Terrain geometry
Rocker-bogie
  Based on the Whippletree mechanism
  Advantages:
    Distributes loads equally on the wheels
    Allows contact even on complex geometries

## Slide 38: Bogie example

## Slide 39: Terrain geometry
Slopes
  The actuation motors limit the maximum slope angle
    Thus:
  The maximum slope angle is

## Slide 40: Terrain Yield
Traction loss
  Bad for odometry: introduces errors (drift)
    Consider using exteroceptive sensors
  Can prevent overcoming slopes
    Lower friction coefficient limits acting between wheels and ground
  Solutions:
    Keep ground pressure under control
      contact surface

## Slide 41: Terrain Yield
Sinking
  Can happen in 2 occasions
  Very high wheel pressure and/or very loose soil
  Due to digging by slipping wheels
The demise of JPL’s Spirit rover, in 2010