## Slide 1: Robot Operating System ROS
Mobile Robots
a.a. 2020-2021

## Slide 2: Our fleet
At the University of Trieste Robotics Laboratory all the mobile robots are ROS-Enabled
Rover
Turtlebot3 Waffle-Pi
MP-500
MPO-500
And eventually:
UR10
Kuka LBR

## Slide 3: Introduction
ROS: Robot Operating System
A set of libraries to build robot applications
  Hardware control (actuators, sensors, ...)
  Software control (navigation, mapping, ...)
Features
  Wide variety of platforms
  Flexible
  Distributed
  Exploits Modularity
  Open Source

## Slide 4: History
Originally developed in 2007 at the Stanford Artificial Intelligence Laboratory and continued at Willow Garage (now Clearpath Robotics)
Since 2013 managed by OSRF (Open Source Robotics Foundation)

## Slide 5: ROS Ecosystem

## Slide 6: Main Features
Operating system side
  Provides core functionality
  Low-level hardware control
  Messaging between processes
Packages
  Contributed by the user base
  Implement common robot functionality:
  SLAM, path planning, perception, vision, manipulation, autonomous navigation, etc.

## Slide 7: Philosophy
Distributed
  Peer-to-peer
  Numerous small programs which exchange messages
Package-based
  Packages provide all the specific functionalities.
  Client libraries: C++, Python, Java, C#, lisp, MATLAB, ...
Thin
  ROS itself is only a layer that wraps around stand-alone libraries
  It allows there to exchange information between them
Free and Open-source

## Slide 8: ROS elements
Nodes
Messages and Topics
Services
ROS Master
Parameters

## Slide 9: ROS Terminology
A ROS network comprises different parts of a robot system (such as a planner or a camera interface) that communicate over ROS. The network can be distributed over several machines.
A ROS master coordinates the different parts of a ROS network. It is identified by a Master URI (Uniform Resource Identifier) that specifies the hostname or IP address of the machine where the master is running.
A ROS node is an entity that contains a collection of related ROS capabilities (such as publishers, subscribers and services). A ROS network can have many ROS nodes.
Publishers, subscribers, and services are different kinds of ROS entities that process data. They exchange data using messages.
A publisher sends messages to a specific topic (such as "odometry"), and subscribers to that topic receive those messages. There can be multiple publishers and subscribers associated with a single topic.

## Slide 10: Example
Face detection
Obstacle detection
Map building
Laser-scanner
Camera
Image message
Image message
Point cloud
Point cloud
Obstacle position/size
Nodes
Messages
Motor Driver
Bool message
Obstacle Avoidance
Velocity message

## Slide 11: ROS structure
The master node coordinates all other nodes
All nodes register with the master at startup

## Slide 12: ROS structure

## Slide 13: ROS nodes
Single-purposed executable programs
  Sensor drivers, actuator drivers, mapper, planner, User Interfaces, …
Individually compiled, executed, and managed
Nodes are written using a ROS client library
  roscpp – C++ client library
  rospy – python client library
Nodes can publish or subscribe to a Topic
Nodes can also provide or use a Service

## Slide 14: ROS Topics
A stream of messages with a defined type
  Example:
  Laser range-finder sends data on a topic called scan, with message type: “LaserScan”
Nodes communicate with each other by publishing messages to topics
Publish/Subscribe model:
  N-to-N broadcasting

## Slide 15: ROS Topics
Example:
Left camera
Stereoscopy
3D Processing
Path-planner
Right camera
Topic: /vision
Topic: /map
Camera nodes publish image data to topic /vision
Stereo node subscribes to topic /vision
Stereo node publishes 3D data of map to topic /map
Path-planner node subscribes to topic /map
Eventually, the path-planner commands the motors...

## Slide 16: Messages
Many kind of different messages;
They represent the data structure of the passed data;
Defined in a file .msg;
Compiled togheter with the parent package or as standalone msg package
Message
Standard
Derived
Custom
e.g. Bool, float, int, char, etc.
e.g. Vector, Twist, Odometry, etc.
e.g. pippo, pluto, etc.

## Slide 17: Message - Example
The topic /cmd_vel, common to every mobile platform, uses Twist as message type.
Twist is derived

## Slide 18: ROS Services
Used for request/response communication
1 to 1 communication

## Slide 19: ROS Services - Usage
Perform small tasks once in a while: e.g. reset sensors, perform calibration, taking pictures of something of interest;
Save collected data;
Emergengy stop.

## Slide 20: Topics / Services
Client-server communication
N-N broadcast communication
Node
Node
Service
Node
Node
Node
Node
Topic
Publication
Subscription
Comparison:

## Slide 21
Actions
Used as services but for very large demanding tasks/actions.
Uses 3 messages: Goal Message, Feedback Message, Result Message.
Example:
Planner
Robot
Go to pose
Progress
Final pose

## Slide 22: Parameter Server
Shared dictionary in the ROS network.
Nodes store and load parameters at runtime
Runs inside the ROS Master
Mainly used for systems configuration.
Possible to start the Nodes by passing parameters one by one;
Possible to load a configuration file loading multiple parameters

## Slide 23: Ros Package
Main unit of how the software is organized in ROS;
Extensive use of C++, Python and XML language;
Contains:
  Nodes;
  Messages/Services/Actions definitions;
  Configuration files;
  Launch files;
  Instructions for the compiler;
  Package Manifest (metadata, version, dependecies etc.).

## Slide 24: Rviz
3D visualization tool for ROS
  Allows visualization of robot frame
  Frames of reference
  Maps
  Path/trajectories
  Objects
  Sensor data
  Vision output
Video RVIZ

## Slide 25: Gazebo
Dynamic simulator for robotic systems in general;
Allows modeling of the robot and the scenario either in its GUI or via code;
Modeling of the robot through URDF and SDF files (files describing how the robot is composed – Links, Joints, Bodies, Sensors etc.);
Explicit definition of physical properties: friction, gravity, contacts etc;
Extendable with custom plugins, for example extend robot model with additional sensors.

## Slide 26: Gazebo - Example
Trajectory tracking with one and a fleet of mobile robots in a custom and cluttered environment;
Two ROS Package created
Simulation/world setup and robots spawning
Trajectory Tracking Controller

## Slide 27: Gazebo – Example (Rosgraph)
Use of namespaces (prefix) makes the script scalable to n independent robots.
Case of multiple robots

## Slide 28: ROS Package Example Custom Teleop Node
Source Code
Use of rospy client
Control a mobile platform using the keyword;
Usable on any kind of mobile platform;
Can control either simulated ones or real ones
Launch File

## Slide 29: Summary Example
Based on the Turtlebot3, the navigation stack, mapping (Gmapping), SLAM
roslaunch turtlebot3_gazebo turtlebot3_world_mio.launch #Simulation environment
roslaunch teleop_mio teleop.launch #Teleop
rosservice call /gazebo/reset_simulation #Reset simulation
roslaunch turtlebot3_slam turtlebot3_slam.launch #SLAM & Mapping
rosrun map_server map_saver -f test_map/test_map #Save map
roslaunch turtlebot3_gazebo turtlebot3_world_mio.launch #Simulation environment
roslaunch turtlebot3_navigation turtlebot3_navigation.launch map_file:=$HOME/test_map/test_map.yaml #Planner

## Slide 30: Rover
Developed a ROS-Enabled prototype of a 4 wheel steering rover.
Main Nodes:
  Robot Core Node: compute odometry, update motors command, receive and apply teleoperating commands after applying inverse kinematics, receive motors operating modes, extract and update IMU, provide informations about sensors, motors and joint state.
  Lidar Node: Aquire readings in form of distance and angles and publish them on /scan topic.
  Matlab Remote Node: Contains teleop, SLAM, mapping, planning, inverse kinematics and many other features.
  Camera Node: takes images from the camera and publish them in the corresponding topic.
  Diagnosis Node: Collect states of different systems and publish them on its topic.

## Slide 31: Rover - Rosgraph
Camera Node
LiDar Scanner Node
Master Node
Rover Core Node

## Slide 32: Rover – Custom Message Definition

## Slide 33: How to start - Solutions
ROS Developement Studio: online programming and testing. No installation required link;
Create a virtual machine on your Windows laptop and install Ubuntu in it. Oracle VM Virtual Box. Then refer to the next step;
ROS: installation of the software required. Better to use Ubuntu
  Homepage: descriptions, tutorials etc.
  Installation guide: last ROS version ROS Noetic Ninjemys.
If you are courious and you want to start on developing ROS applications:
Enjoy and have fun!

## Slide 34: Thank you for your attention
For any question feel free to contact us.
Contacts:
sseriani@units.it
matteo.caruso@phd.units.it