## Slide 1
The gravitational field of the Earth reflects the kind of mass distribution within our planet and is closely linked to the shape of the Earth. The gravitational attraction between two objects (point) with mass M and M0 at a distance r is given by
GRAVITY FIELD: introduction
Experimental determination of G was extremely difficult, and was first achieved more than a century after the publication of Principia by Lord Charles Cavendish (1731–1810). From a set of painstaking measurements of the force of attraction between two spheres of lead, Cavendish in 1798 determined the value of G to be 6.754·10-11 m3 kg-1 s-2. A modern value is 6.674·10-11 m3 kg-1 s-2
It has not yet been possible to determine G more precisely, due to experimental difficulty. Although other physical constants are now known with a relative standard uncertainty of much less than 1·10-6, the gravitational constant is known to only 1·10-6
where G=6.67x10-11 m3kg-1s-2 is the universal gravitational constant.

## Slide 2
is the acceleration of an object in free fall directly into M.
The gravity due to the various masses is the vectorial sum in the measurement point rm of gravity due to the individual masses at the points rs
NB: In physics r is usually directed from the mass M to observer, so in expressions above it would take a minus sign. In geophysics it is however convenient to define the acceleration of gravity towards the center of the Earth as positive.
The force for unit mass

## Slide 3
A way to represents indirectly the gravitational field is its potential, that for a point mass is
GRAVITATIONAL POTENTIAL
The gravity is obtained by its gradient:
For example:
NB: For physicists it would take a minus sign.
The gravitational field is conservative.

## Slide 4
Considering the gravitational flow through a spherical surface centered on a point mass. For symmetry the gravity is the same in each point on the surface:
For any surface the result is the same. This is represents the Gauss law and is equivalent to
Considering the flow for volume unit, the divergence, that is the Gauss theorem:
We have:
From which, replacing
we obtain the Poisson equation:
Gauss law

## Slide 5
The Gauss law implies that the gravitational potential outside of an extended body (sphere) with total mass M is equal to that due to a point mass placed at the center of gravity of the extended body. Therefore, if the Earth were perfectly spherical and non-rotating with a density distribution depending only on the radius ρ = ρ (r), the external gravitational potential would simply
Newtonian potential
with the distance r between the center of the Earth and the mass of Earth M. Gravity would be equal on each point on the Earth's surface. The value of the gravitational acceleration on the Earth's surface varies, however - although less than a hundredth - with an average value of about 9.8 ms-2 (981 cms-2 = 980 gal). The Earth, in fact, differs from spherical to one three-hundredth. It is flattened at the poles and bulging in the equatorial zones, very similar to an ellipsoid of rotation. The flattening of the Earth is given by
where a and b are polar and equatorial radius, respectively. The most recent value of f is given by f = 1 / 298,247. The radius of the ellipsoid of rotation is given (to the first term in f) from
where ϕ is latitude, a=6378.14km ,b=6356.75 km.

## Slide 6
Also the deviation of the external gravitational field of the Newtonian potential is of the order of the three hundredth and less still. Before the advent of artificial satellites had failed (with earthly measures) to determine the first correction J2 of the Newtonian gravitational field
DEVIATION IN SFERIC SIMMETRY
with
C= the inertial moment respect to the polar axes
Ᾱ= is the average inertial moment respect to the equatorial axes
is the second Legendre’s polynomial and Θ is the colatitude : Θ=π/2-ϕ
The present value is J2= 1082.65x10-6
J2 measures the deviation of the real gravitational field of the Earth from spherical symmetry. Its contribution makes you that an artificial satellite revolves around the Earth on an orbital plane that rotates in turn retrograde, fixed prejudice to its inclination to the equatorial plane of the Earth: regression orbit.

## Slide 7
The gravitational potential can be developed in spherical functions, the so-called eigenfunctions of the sphere (sums of sines and cosines, grouped in a certain way, of the latitude and longitude variables).
General case
with Pnm (cosΘ) associated Legendre polynomials (of order n than cosΘ and sinΘ) and Jn, Anm, Bnm are the gravitational moments (to be determined experimentally). Note that the terms of first order in Θ (n = 1) do not appear, having chosen the center of gravity of the Earth as origin of the reference system! By the early '60s were known a ten zonal moment Jn (generating secular perturbations in the orbits of artificial satellites) and a ten tesseral moment Anm, Bnm create instead periodic variations of short duration.

## Slide 9
The figure of the Earth
The best mathematical approximation to the figure is an oblate ellipsoid, or spheroid. The precise determination of the dimensions of the Earth (e.g., its polar and equatorial radii) is the main objective of the science of geodesy. It requires an exact knowledge of the Earth’s gravity field, the description of which is the goal of gravimetry.
Modern analyses of the Earth’s shape are based on precise observations of the orbits of artificial Earth satellites. These data are used to define a best-fitting oblate ellipsoid, called the International Reference Ellipsoid
In 1980 the International Association of Geodesy adopted a Geodetic Reference System (GRS80)

## Slide 11
For an Earth exactly in hydrostatic equilibrium (i.e. no shear stress), the gravitational potential would be
EARTH DEVIATION FROM THE HYDROSTATIC EQUILIBRIUM
with only zonal numbers equal J2N. Furthermore, the values of J2N should grow rapidly as n increases with
If so, the following corrective term after J2 would be J4. By measures from satellites it has however come to the conclusion that all the gravitational moments, starting with J3, are about the same order and equal to some units per 10-6: the order of the square of the flattening, f2. Also the decrease of the moments as n increases very slowly. The deviation of the Earth hydrostatic equilibrium is therefore the order of the square of flattening! It follows that in the Earth, in addition to the hydrostatic stress, also act tangential stresses, which are of the order of a few MPa. The shape of the earth differs from the hydrostatic one: the thickness of the layer in equilibrium is ≈f2a = 70m

## Slide 12
The precession of the Earth’s axis is the interaction between the Earth's rotation ωT and the revolution around the sun ωS, which take place according to two axes inclined by approximately 23.5 ° relative to one another. The non-parallelism between the two axes, together with the Earth flattering, generates a bend/twist moment which would tend to make them parallel, giving rise to the phenomenon of precession (T≈26000 years!)

## Slide 13
For the study of the internal structure of the Earth is of great interest the average value of the moment of inertia
INERTIAL MOMENT
that together with the average Earth density
and seismological data, allows to determine the density distribution within the Earth.

## Slide 14
For a planet at constant density (homogeneous sphere) the dimensionless moment of inertia result
If the density inside the planet grows from the outside inwards, I* assumes values lower than 0.4; vice versa if the density decreases with depth, it will have a value greater than 0.4. Based on the observations for the Earth is I* = 0.33076, which corresponds to a considerable concentration of the land mass in the central areas of the planet.
Causes of growth of the density with depth: 1. Compression due to overlying layers 2. Increase with the depth of the heavy elements 3. Possible phase transitions at high pressure Causes of decrease in density with depth: 1. Temperature increase towards the interior of the Earth 2. Fusion (partial) separation of the components with the lower-density
Clearly they are more effective the causes of growth of density with depth.
In case of strong reversals of density, on the region of low density would act the so-called “Archimedes buoyancy" that brings back the regions with high density under those low density.

## Slide 15
ROTATIONAL POTENTIAL AND TOTAL POTENTIAL
For the Earth that rotates around its axes with angular velocity ω, we must also consider the centrifugal force in a point at distance r from the rotational axes ω by:
The force field is conservative and the its potential is:

## Slide 16
Gravity
Newton’s first law of motion states that every object continues in its state of rest or of uniform motion in a straight line unless compelled to change that state by forces acting on it.
The continuation of a state of motion is by virtue of the inertia of the body. A framework in which this law is valid is called an inertial system.
Motion in a circle implies that a force is active that continually changes the state of rectilinear motion. Newton recognized that the force was directed inwards, towards the center of the circle, and named it the centripetal (meaning “center-seeking”) force.
Arguing that the curved path of a projectile near the surface of the Earth was due to the effect of gravity, which caused it constantly to fall toward the Earth, Newton postulated that, if the speed of the projectile were exactly right, it might never quite reach the Earth’s surface.
Newton suggested that the Moon was held in orbit around the Earth by just such a centripetal force, which originated in the gravitational attraction of the Earth
Centripetal acceleration

## Slide 17
Gravity
The mathematical form of the centripetal acceleration for circular motion with constant angular velocity  about a point can be derived as follows: define orthogonal Cartesian axes x and y relative to the center of the circle. The linear velocity v at any point where the radius vector makes an angle θ=(t) with the x-axis has components:
The x- and y-components of the acceleration are obtained by differentiating the velocity components with respect to time. This gives:
These are the components of the centripetal acceleration, which is directed radially inwards and has the magnitude 2r

## Slide 18
Gravity
The passenger in a car going round a corner experiences a tendency to be flung outwards. He is restrained in position by the frame of the vehicle, which supplies the necessary centripetal acceleration to enable the passenger to go round the curve in the car.
The inertia of the passenger’s body causes it to continue in a straight line and pushes him outwards against the side of the vehicle.
This outward force is called the centrifugal force. It arises because the car does not represent an inertial reference frame.
The centrifugal force feels real enough to the passenger in the car, but it is called a pseudo-force, or inertial force. In contrast to the centripetal force, which arises from the gravitational attraction, the centrifugal force does not have a physical origin, but exists only because it is being observed in a non-inertial reference frame.
Centrifugal acceleration

## Slide 19
The gravitational acceleration acting on a body will be less than that acting on a body located on the Earth not rotating
The total gravitational potential is the sum of the field potential of the Newtonian’s force and of the centrifugal force
The concavity of the force lines of the total field is directed towards the axis of rotation and the equipotential surfaces have the ellipsoid shape closed

## Slide 20
REFERENCE ELLIPSOID
The Earth should have the shape of a rotational ellipsoid if it were a fluid mass with density that increases with depth and rotating around the polar axis. Also its surface, being liquid, is necessarily equipotential surface. This ellipsoid is called reference ellipsoid and represents the equipotential surface of an Earth sferoidal model with real lateral variation of the density and with a centrifugal potential. The gravitational force is everywhere perpendicular to its surface and can be calculated mathematically. The formula adopted by the International Association of Geodesy in 1967 is
where ge=978.03185 gal, a=5.278895∙10-3, β=2.3462∙10-5
About the 40% of the gravity variation with the latitude is due to the difference between ellipsoid and sphere (that is to flattering), instead the 60% is due to Earth’ rotation. The maximum error in the formula is 4μgal. The gravity calculated with this formula is called normal gravity.

## Slide 24
THE GEOID
The Earth is not a perfect sphere nor rotational ellipsoid. For example mountains and oceanic trenches represent variations of many kilometers. The equipotential surface that delimit the Earth mass is called geoid and differ less from the reference ellipsoid. Over the oceanic, the geoid coincides with the sea level. On the continentals the geoid can be visualized by the average level on which could arrange the water in a network of narrow canals dug across continents. The geoid is a reference surface for the navigation, survey and altimetry. In a point the vertical is not direct versus the centre of the Earth , but is perpendicular to local equipotential surface and, if close to level sea, it is perpendicular to the geoid.
The figure of the geoid derived from satellite data, in particular from radar altimetry measurements. These measurement have defined the marine geoid with an accuracy about 10 cm. The satellite and gravimetric measurements are in agree about of 50 cm indicating that the theory and assumptions are correct.

## Slide 25
gn = 9.80665 ms-2 (980.665 cms-2 = 980.665 gal).

## Slide 26
Geoid
The geoid can be elevated above ellipsoid by:
hill or mountain with center of gravity outside ellipsoid causes upward attraction;
B) mass excess below ellipsoid

## Slide 28
Satellite Geodesy
Modern satellite technology has greatly improved determination of the Earth’s ellipsoid.
Since the early 1960s knowledge of the geoid: features of the gravity field on a scale larger than 1000 km are discerned more effectively by studying perturbations of satellite orbits than would be possible from surface observations. With progressive improvements, satellite techniques have been used to distinguish increasingly fine features, although for exploration of local anomalies surface observations on land must still be used, sometimes in combination with satellite data

## Slide 37
The gaps between the geoid and International Ellipsoid are about 10 m and not more than 70 m , in agree with the deviations from idrostatic equilibrium are of the order of f2.
A geoid negative anomaly is in a region with a deficit of mass (depression in the ocean floor), instead a positive anomaly in a region with an excess of mass (mountain on the ocean floor).
The anomaly Δh is linked to the anomaly of the gravitational potential measured on the ellipsoid:
where g is the gravitational acceleration on the ellipsoid.
The deviations are due to the inhomogeneous in the Earth stratification and also are not in hydrostatic equilibrium.
Erosion, tectonic movements, accumulation and melting ice are the cause of slow and continuous variations of the shape of the geoid.

## Slide 38
Geoid ondulation: displacement between the geoid and the ellipsoid

## Slide 42
Just two years after its launch, the ESA's GOCE satellite has gathered enough data to create a map of the Earth's gravitational field, with a precision never before achieved. The scientific community now has access to more accurately model 'geoid' ever produced, which will allow us to better understand the functioning of our planet.
The map created by Goce shows the points of the Earth where there are gravitational alterations: in red, areas with gravitational pull above average, in blue ones where the gravitational pull is lower.

## Slide 46
Geoid (meters), from GRACE satellite data

## Slide 47
Gravity anomalies (mGal), from GRACE satellite data

## Slide 48
Gravity anomalies (mGal), from GRACE satellite data