## Slide 1
differences in density of materials (rocks) in Earth’s interior
produces small differences in local gravity field (anomalies)
can be measured with a gravimeter (attraction of spring to mass)
dense material
attracts
and extends spring
void (cave) has no
mass to attract
spring
mass uniform
and spring
is neutral

## Slide 2
MISURE DI GRAVITA’

## Slide 3
Gli strumenti adatti ad una rapida miisura della gravità sono da ricercare nei metodi statici, che prevedono l’osservazione di un Sistema in equilibrio. I gravimetri statici consentono soltanto misure relative della gravità (differenza rispetto una misura g iniziale). Le misure sono rapide e possono accuratezze elevate (mgal).

## Slide 4
GRAVIMETRO ASSOLUTO
Uno dei gravimetric assoluti più accurate (10 mgal) è quello dell’Istituto Metrologico Colonnetti di Torino, che si basa sulla caduta libera simmetrica: un corpo viene lanciato in alto e ricade. Per determinare g bisogna misurare due tempi ed una lunghezza.

## Slide 6
Absolute measurement of gravity
The measurement of an absolute value of gravity is difficult and requires complex apparatus and a lengthy period of observation !

## Slide 14
mg
dz

## Slide 15
mg
dz
GRAVIMETRO LINEARE
Il principio è quello del dinamometro: un massa m sospesa ad una molla con costante k. Nella condizione di equilibrio avremo:
Se la gravità varia:
Da cui:
E il rapporto dà la sensibilità dello strumento. Spostando la massa dalla condizione di euilibrio e applicando la legge di Newton:

## Slide 16
L’equazione differenziale è quella del moto armonico con periodo:
=
Si vede che la sensibilità è direttamente proporzionale al quadrato del periodo. Costruttivamente è difficile ottenere T>1 s, per cui se si vuole misurare
occorre valutare
e si ha bisogno di ingrandimenti fortissimi! Pertanto tali gravimetri sono stati abbandonati.

## Slide 17
I gravimetri astatici sono strumenti di grande precisione e già nel 1850 avevano la sensibilità di 10 mgal.
Essi sono costituiti essenzialmente da un braccio che può ruotare attorno ad un punto O nel piano P(x,z) e porta all'estremo libero una massa m; il braccio è mantenuto in posizione orizzontale da una molla fissata ad un asse verticale passante per O. L'equilibrio del sistema dipende dai momenti delle forze in gioco rispetto ad O : uno dovuto alla g agente su m;
un’altro dovuto alla reazione elastica della molla di bilanciamento.
Gravimetri astatici

## Slide 18
Sia φ l'angolo nel piano P(x,z) compreso tra il braccio b e il piano orizzontale passante per O .
Supponiamo che per effetto di g si raggiunga l’equilibrio per una rotazione del braccio di un angolo φ; in queste condizioni ovviamente le forze in gioco sono in equilibrio e quindi il momento totale delle forze in gioco M deve essere nullo; in termini di modulo:
M(g, φ) = 0 .

## Slide 19
Il momento totale è dato dalla componente stabilizzante (elastica) e quella labilizzante (gravitazionale):
M = Me - Mg

## Slide 20
0

## Slide 21
Mentre il momento della fase d’inerzia, essendo accelerazione tangenziale , sarà dato da:
Da cui si ricava che l’equazione del moto sarà:
Che dà ancora un moto armonico di periodo:

## Slide 22
E pertanto anche in questo caso la sensibilità è proporzionale al quadrato del periodo.
Per ottenere periodi grandi e sensibilità elevate basterà realizzare:

## Slide 27
La Coste - Romberg

## Slide 28
La Coste - Romberg

## Slide 29
Askania

## Slide 30
Relative measurement of gravity
Gravimeters for general surveying use are capable of registering changes in gravity with an accuracy of 0.1 gu. A new generation of more efficient zero-length springs has been developed. Microprocessor-controlled instruments are now available which are, within limits, selflevelling, and which allow observations to be made rapidly. Also available for more specialized surveys are gravimeters capable of detecting gravity changes as small as 1 microgal (10-8ms-2) !!!.

## Slide 31
Gravity survey
The goal of gravity surveying is to locate and describe subsurface structures from the gravity effects caused by their anomalous densities.
Most commonly, gravimeter measurements are made at a network of stations, spaced according to the purpose of the survey.
In environmental studies a detailed high-resolution investigation of the gravity expression of a small area requires small distances of a few meters between measurement stations.
In regional gravity surveys, as used for the definition of hidden structures of prospective commercial interest, the distance between stations may be several kilometers.
A microgravity survey (50 m spaced lines and 20 m spaced stations)
If the area surveyed is not too large, a suitable site is selected as base station (or reference site), and the gravity differences between the surveyed sites and this site are measured.

## Slide 32
In order to obtain a reduced gravity value accurate to ±1mgal, the reduction procedure described in the following section indicates that the gravimeter must be read to a precision of ±0.1 mgal, the latitude of the station must be known to ±10 m and the elevation of the station must be known to ±10mm.
The latitude of the station must consequently be determined from maps at a scale of 1 : 10 000 or smaller, or by the use of electronic position-fixing systems.
Uncertainties in the elevations of gravity stations probably account for the greatest errors in reduced gravity values on land;
The optimal equipment at present is the global positioning system (GPS), whose constellation of 24 satellites is now complete and an unadulterated signal is broadcast. Signals from these can be monitored by a small, inexpensive receiver.
Use of differential GPS, that is, the comparison between GPS signals between a base set at a known elevation and a mobile field set, can provide elevations to an accuracy of some 25mm.

## Slide 33
Before the results of a gravity survey can be interpreted it is necessary to correct for all variations in the Earth’s gravitational field which do not result from the differences of density in the underlying rocks. This process is known as gravity reduction or reduction to the geoid
In practice, it is not possible to measure gravity on the ellipsoid at the place where the reference value is known. The elevation of a measurement station may be hundreds of meters above or below the ellipsoid. Moreover, the gravity station may be surrounded by mountains and valleys that perturb the measurement.
let P and Q represent gravity stations at different elevations in hilly terrain The theoretical value of gravity is computed at the points R on the reference ellipsoid below P and Q. Thus, we must correct the measured gravity before it can be compared with the reference value.

## Slide 34
0.1 mGal
Marea terrestre

## Slide 35
0.1 mGal
Marea terrestre

## Slide 36
A shortcoming of gravimeters is the phenomenon of drift. This refers to a gradual change in reading with time, observable when the instrument is left at a fixed location.
Drift results from the imperfect elasticity of the springs, which undergo anelastic creep with time. Drift can also result from temperature variations which, unless counteracted in some way, cause expansion or contraction of the measuring system and thus give rise to variations in measurements that are unrelated to changes in gravity.
The effect is small in modern gravimeters and can be compensated by making a drift correction. This is obtained by repeated occupation of some measurement stations at intervals during the day Gravity readings at other stations are adjusted by comparison with the drift curve. In order to make this correction the time of each measurement must be noted.

## Slide 37
Deriva strumentale

## Slide 38
Per interpretare i valori di gravità gm, che vengono misurati sulla superficie terrestre, in termini di anomalie locali o regionali, bisogna prima rimuovere certi effetti, comuni a tutte le misure. Supponendo che gli effetti di deriva e calibrazione dello strumento, nonchè delle maree terrestri siano già stati (se necessario) rimossi, le correzioni (dette anche riduzioni) da applicare sono:
Correzioni di latitudine (gravità normale)
Correzione di aria libera (di Faye)
Correzione della piastra (di Bouguer)
Correzione topografica
Correzione isostatica

## Slide 39
Alessandro Germak (INRIM, 2007)

## Slide 40
Alessandro Germak (INRIM, 2007)

## Slide 41
Alessandro Germak (INRIM, 2007)

## Slide 42
La correzione si ottiene sottraendo dal valore misurato gm il valore della gravità normale gϕ
Correzione di latitudine
Se la zona della campagna gravimetrica è limitata, si può usare una correzione al primo ordine ottenuta derivando la formula della gravità normale:
Pertanto:
ove Δl è lo scostamento in direzione N-S da un punto appropriato in cui la gravità normale è g0. Avremo:
Possiamo pertanto esprimere i contributi della gravità nel punto di misura come:
Ove con ε1 indico il contributo di altri fattori. Pertanto:
rappresenta una prima anomalia residua ottenuta (che però non ha nome in quanto di poca utilità).

## Slide 43
Correzione di aria libera (di Faye)

## Slide 44
Poichè la gravità varia come 1/r2, necessita correggere il dato misurato per la differenza di altitudine del punto (stazione) di misura rispetto al geoide. La correzione viene detta di aria libera in quanto non tiene conto delle masse interposte tra la stazione ed il geoide. Essa viene determinata con grande approssimazione, trascurando la componente centrifuga.
Correzione di aria libera (di Faye)
Pertanto la correzione per l’altitudine sarà:
In seconda approssimazione i contributi alla gravità nel punto di misura saranno:
In cui le correzioni per l’altitudine va sottratta se il punto di misura è al di sopra del geoide.
Corregendo i dati solamente per la latitudine e l’altitudine si ottiene un’anomalia (ε2 che però chiamiamo gFA) che risulta utile nelle investigazioni locali e regionali:
e viene chiamata anomalia dell’aria libera (free-air anomaly).

## Slide 45
Tiene conto dell’attrazione delle masse interposte tra la stazione di misura ad altezza h ed il geoide, che è stato ignorato nella correzione ad aria libera. Tale effetto può essere approssimato con quello di una piastra (circolare con raggio a →∞) di altezza h e densità uguale alla densità media degli strati sottostanti (NB: non nota in generale, per cui nel caso di campi regionali si assume ρ=2.67 g/cm3).
Correzione della piastra (di Bouguer)

## Slide 46
Correzione della piastra (di Bouguer)

## Slide 47
Tiene conto dell’attrazione delle masse interposte tra la stazione di misura ad altezza h ed il geoide, che è stato ignorato nella correzione ad aria libera. Tale effetto può essere approssimato con quello di una piastra (circolare con raggio a →∞) di altezza h e densità uguale alla densità media degli strati sottostanti (NB: non nota in generale, per cui nel caso di campi regionali si assume ρ=2.67 g/cm3). Calcoliamo il contributo alla gravità nel punto di misura di un elementino di massa
Correzione della piastra (di Bouguer)

## Slide 48
Pertanto l’approssimazione successiva alla gravità nel punto di misura sarà:
La correzione è positiva poichè la piastra attrae con una massa extra il punto di misura rispetto al geoide. La correzione ΔgB risulta (per ρ=2.67 g/cm3) di circa 0.112 mgal/m.
L’ anomalia risultante (ε3) viene detta anomalia di Bouguer semplice.
Per ottenere l’anomalia di Bouguer in mare si sostituisce all’acqua di densità 1 g/cm3 materiale di densità =2.67 g/cm3 e quindi si somma l’attrazione addizionale (dovuta al contrasto di densità 1.67 g/cm3) del materiale
alla gravità in aria libera. La formula da una correzione di 0.070 mgal/m.
Poichè l’anomalia in aria libera è di solito molto piccola, si ottiene una forte anomalia di Bouguer positiva nella maggior parte delle regioni oceaniche. Pertanto, con dati marini, non ci sono vantaggi nell’usare le anomalie di Bouguer rispetto a quelle in aria libera.

## Slide 49
Se la stazione di misura non è situata su un altopiano, ma in mezzo a montagne e valli, occorre aggiungere alla correzione di Bouguer quella dovuta alla topografia. Da notare che la topografia riduce il valore delle misure: infatti aggiunge all’attrazione verso l’alto (colline), ovvero provoca una mancanza di attrazione verso il basso (valli). Per calcolare le correzioni si suddivide la zona circostante la stazione di misura secondo prismi a sezione di settore circolare con una base alla quota di misura ed altezza corrispondente alla quota media del settore
Correzione topografica

## Slide 51
Se la stazione di misura non è situata su un altopiano, ma in mezzo a montagne e valli, occorre aggiungere alla correzione di Bouguer quella dovuta alla topografia. Da notare che la topografia riduce il valore delle misure: infatti aggiunge all’attrazione verso l’alto (colline), ovvero provoca una mancanza di attrazione verso il basso (valli). Per calcolare le correzioni si suddivide la zona circostante la stazione di misura secondo prismi a sezione di settore circolare con una base alla quota di misura ed altezza corrispondente alla quota media del settore
Il calcolo dell’attrazione gravitazionale è analogo a quello della piastra infinita solo il limite di integrazione per r’ varia da a1 ad a2 per cui
Correzione topografica
Per cui, variando il limite di integrazione in ϕ tra 0 ed α, avremo

## Slide 53
Ovviamente la correzione ΔgT da applicare sarà la somma delle correzioni dovute ad ogni prisma entro un determinato raggio dalla stazione.
L’approssimazione successiva alla gravità nel punto di misura sarà pertanto
Dicesi anomalia di Bouguer (completa) l’anomalia (ε4) che si ottiene da quella in aria libera correggendola per l’effetto della piastra e della topografia:
Se la Terra non avesse variazioni di densità laterali, tutte le misure di gravità, corrette per gli effetti visti sopra, sarebbero identiche. Pertanto le differenze residue riscontrabili ε4 costituiscono un’anomali di gravità gB che è il risultato di variazioni laterali di densità.

## Slide 57
A gravity anomaly results from the inhomogeneous distribution of density in the Earth. Suppose that the density of rocks in a subsurface body is ρ and the density of the rocks surrounding the body is 0. The difference =-0 is called the density contrast of the body with respect to the surrounding rocks.
If the body has a higher density than the host rock, it has a positive density contrast; a body with lower density than the host rock has a negative density contrast. Over a high-density body the measured gravity is augmented; after reduction to the reference ellipsoid and subtraction of the normal gravity a positive gravity anomaly is obtained.
Likewise a negative anomaly results over a region of low density. The presence of a gravity anomaly indicates a body or structure with anomalous density; the sign of the anomaly is the same as that of the density contrast and shows whether the density of the body is higher or lower than normal
The appearance of a gravity anomaly is affected by the dimensions, density contrast and depth of the anomalous body. The horizontal extent of an anomaly is often called its apparent “wavelength.” The wavelength of an anomaly is a measure of the depth of the anomalous mass. Large, deep bodies give rise to broad (long-wavelength), low amplitude anomalies, while small, shallow bodies cause narrow (short-wavelength), sharp anomalies.

## Slide 58
Usually a map of Bouguer gravity anomalies contain superposed anomalies from several sources. The long-wavelength anomalies due to deep density contrasts are called regional anomalies. They are important for understanding the large-scale structure of the Earth’s crust under major geographic features, such as mountain ranges, oceanic ridges and subduction zones. Short-wavelength residual anomalies are due to shallow anomalous masses that may be of interest for commercial exploitation.
Geological knowledge is essential for interpreting the residual anomalies. In eroded shield areas, like Canada or Scandinavia, anomalies with very short wavelengths may be due to near-surface mineralized bodies. In sedimentary basins, short- or intermediate-wavelength anomalies may arise from structures related to reservoirs for petroleum or natural gas.
The separation of anomalies of regional and local origin is an important step in the interpretation of a gravity map. The analysis may be based on selected profiles across some structure, or it may involve the two dimensional distribution of anomalies in a gravity map.
Numerous techniques have been applied to the decomposition of a gravity anomaly into its constituent parts. They range in sophistication from simple visual inspection of the anomaly pattern to advanced mathematical analysis.

## Slide 59
The simplest way of representing the regional anomaly on a gravity profile is by visually fitting the large-scale trend with a smooth curve. The value of the regional gravity given by this trend is subtracted point by point from the Bouguer gravity anomaly.
This method allows the interpreter to fit curves that leave residual anomalies with a sign appropriate to the interpretation of the density distribution.

## Slide 60
This approach may be adapted to the analysis of agravity map by visually smoothing the contour lines: bouguer gravity curve sharply around a local abnormality.
The values of the regional and original Bouguer gravity are interpolated from the corresponding maps at points spaced on a regular grid. The regional value is subtracted from the Bouguer anomaly at each point and the computed residuals are contoured to give a map of the local gravity anomaly.
The experience and skill of the interpreter are important factors in the success of visual methods !

## Slide 61
In an alternative method the regional trend is represented by a straight line or, more generally, by a smooth polynomial curve. If x denotes the horizontal position on a gravity profile, the regional gravity gR may be written:
The polynomial is fitted by the method of least squares to the observed gravity profile. This gives optimum values for the coefficients gn.
The method also has drawbacks: the higher the order of the polynomial, the better it fits the observations. The ludicrous extreme is when the order of the polynomial is one less than the number of observations; the curve then passes perfectly through all the data points, but the regional gravity anomaly has no meaning geologically. !
The interpreter’s judgement is important in selecting the order of the polynomial, which is usually chosen to be the lowest possible order that represents most of the regional trend.

## Slide 62
Polynomial fitting can also be applied to gravity maps. It is assumed that the regional anomaly can be represented by a smooth surface, g(x, y), which is a low order polynomial of the horizontal position coordinates x and y. In the simplest case the regional anomaly is expressed as a first-order polynomial, or plane. To express changes in the gradient of gravity a higher-order polynomial is needed. For example, the regional gravity given by a second-order polynomial is written:
As in the analysis of a profile, the optimum values of the coefficients gx1, gy1, etc., are determined by least-squares fitting. The residual anomaly is again computed point by point by subtracting the regional from the original data

## Slide 63
The gravity anomaly along a profile can be analyzed with techniques developed for investigating time series. Instead of varying with time, as the seismic signal does in a seismometer, the gravity anomaly g(x) varies with position x along the profile. For a spatial distribution the wave number, k=2/, is the counterpart of the frequency of a time series.
If it can be assumed that its variation is periodic, the function g(x) can be expressed as the sum of a series of discrete harmonics. Each harmonic is a sine or cosine function whose argument is a multiple of the fundamental wave number. The expression for g(x) is called a Fourier series.
The breakdown of a complex anomaly (or time series) in terms of simpler periodic variations of different wavelengths is called Fourier analysis and is a powerful method for resolving the most important components of the original signal.

## Slide 64
The two-dimensional variation of a mapped gravity anomaly can be expressed in a similar way with the aid of double Fourier series. As in the simpler one dimensional case of a gravity anomaly on a profile, the expression of two-dimensional gravity anomalies by double Fourier series is analogous to summing weighted sinusoidal functions. These can be visualized as corrugations of the x–y plane, with each corrugation weighted according to its importance to g(x, y).

## Slide 65
The observed gravity can then be manipulated using the techniques of Fourier transform. These techniques involve intensive computations and are ideally suited to digital data-processing with powerful computers.
The two-dimensional Fourier transform of a gravity map makes it possible to digitally filter the gravity anomalies. A filter is a spatial function of the coordinates x and y. When the function g(x, y) representing the gravity data is multiplied by the filter function, a new function is produced.
The nature of the filter applied in the Fourier domain can be chosen to eliminate certain wavelengths. For example, it can be designed to cut out all wavelengths shorter than a selected wavelength and to pass longer wavelengths: this is called a low-pass filter; it passes long wavelengths that have low wave numbers. The irregularities in a Bouguer gravity anomaly map are removed
Alternatively, the filter in the Fourier domain can be designed to eliminate wavelengths longer than a selected wavelength and to pass shorter wavelengths. The application of such a high-pass filter enhances the short-wavelength (high wave number)
Wavelength filtering can be used to emphasize selected anomalies.