## Slide 1
MICROSCOPIA OTTICA IN BIOLOGIA CELLULARE [675SM]
15th March 2023:
Contrasting techniques with laboratory
Agnes Thalhammer
agnes.thalhammer@units.it

## Slide 2
CONTRASTING TECHNIQUES
Brightfield
Darkfield
Phase Contrast
Polarization Contrast
Differential Interference Contrast (DIC)
Fluorescence Contrast

## Slide 3
CONTRAST GENERATION FOR TRANSMITTED LIGHT
Brightfield | >>> | absorbance
Darkfield | >>> | diffraction
Phase Contrast | >>> | Phase shift
Differential Interference Contrast (DIC) Microscopy
>>> Phase shift / Polarization / Interference

## Slide 4: ABSORPTION
Absorption
Control
No blue/green light
red filter

## Slide 5
DIFFRACTION

## Slide 6
BRIGHTFIELD
Piece of artificially grown skin
(www.igb.fhg.de/.../dt/PI_BioTechnica2001.dt.html )
Cross section of sunflower root
(http://www.zum.de/Faecher/Materialien/beck/12/bs12-5.htm)
Principle:
Light is transmitted through the sample and absorbed by it.
Application:
Only useful for specimens that can be contrasted via dyes
Very little contrast in unstained specimens
With a bright background, the human eye requires local intensity fluctuations of at least 10 to 20% to be able to recognize objects.

## Slide 7
BRIGHTFIELD
Bright Field is the most universal technique used in light microscope.
Usually used in samples with colorimetric staining or good contrast; dark sample absorbing light on bright background
Particularily useful on samples with intrinsic colour (e.g. chloroplasts)
AI programs using mashine-learning techniques on stained samples to be able to identify cells/organelles etc.. without staining in Bright Field.

## Slide 8
DARKFIELD
Principle:
The illuminating rays of light are directed through the sample from the side by putting a dark disk into the condenser that hinders the main light beam to enter the objective. Only light that is scattered by structures in the sample enters the objective.
Application:
Diatoms and other unstained or colourless specimens
Darkfield
Symbiotic Diatom colony
(www1.tip.nl/~t936927/making.html)
Brightfield

## Slide 9
DARKFIELD
Fine structures can often not be seen in front of a bright background.

## Slide 10
DARKFIELD
Dark background against which objects are brilliantly illuminated.
This is accomplished by a special condenser that transmits a hollow cone of light.
Most of the light directed through the condenser does not enter the objective, the field is dark.
However, some of the light rays will be scattered if the medium contains objects.
The diffracted light will enter the objective & reach the eye, thus the object will appear bright in an dark background.
Best for observing pale objects, unstained cells

## Slide 11
DARKFIELD

## Slide 12
PHASE CONTRAST
Principle:
Incident light is out of phase with transmitted light as it was slowed down
while passing through different parts of the sample. when the phases of the light are synchronized by an interference lens, a new image with greater contrast is seen.
I
I0
aligned
not aligned
Phase stops

## Slide 13
PHASE CONTRAST
I
I0
aligned
not aligned
Phase stops
Phase contrast in practice
Application: Phase contrast is the most commonly used contrasting technique All tissue culture microscopes and many time-lapse microscopes are set up for phase contrast.
wrong phase stop
brightfield
right phase stop

## Slide 14
PHASE CONTRAST
I
I0
aligned
not aligned
Phase stops

## Slide 15
PHASE CONTRAST
I
I0
aligned
not aligned
Phase stops
THEORY & APPL. LIGHT MICROSCOPY

## Slide 16
POLARISATION
I
I0
aligned
not aligned
Phase stops
light vibrates in
all planes that contain the light ray
(i.e., all planes perpendicular to the propagation direction
plane of vibration
vibration direction
propagation
direction
© Jane Selverstone, University of New Mexico, 2003

## Slide 17
1) Light passes through the lower polarizer
west (left)
Plane polarized light
Unpolarized light
east
(right)
Only the component of light vibrating in E-W direction can pass through lower polarizer –
light intensity decreases
Though polarized, still white light!
POLARISATION
© Jane Selverstone, University of New Mexico, 2003

## Slide 18
2) Insert the upper polarizer
west (left)
east (right)
Now what happens? What reaches your eye?
Why would anyone design a microscope that
prevents light from reaching your eye???
south
(front)
north
(back)
Black!! (“extinct”)
© Jane Selverstone, University of New Mexico, 2003
POLARISATION

## Slide 19
© Jane Selverstone, University of New Mexico, 2003
3) Now insert a thin section
west (left)
Light vibrating E-W
How does this work??
Unpolarized light
east (right)
Light vibrating in many planes and with many wavelengths
Light and colors reach eye!
POLARISATION

## Slide 20
Polarizer
Analyzer
Lambda plate
Principle:
Polarized light is used for illumination. Only when the vibration direction of the polarized light is altered by a sample placed into the light path, light can pass through the analyzer. The sample appears light against a black background. A lambda plate can be used to convert this contrast into colours.
Application:
Polarization contrast is used to look at materials with birefringent properties, in which the refractive index depends on the vibration direction of the incident light, e.g. crystals or polymers.
POLARISATION CONTRAST

## Slide 21
Dinosaur Bone
Glutaric Acid Crystallites
Brightfield
Polarization contrast
Polarization contrast with Lambda plate

## Slide 22
NOMARSKI IMAGE
Result is extinction (shadow) on one side of specimen and reinforcement (bright) on the other
Shear of image
False relief 3D image
Consider wavefront diagrams

## Slide 24
BIREFRINGENCE
Birefringent materials have different indices of refraction for light polarized parallel or perpendicular to the optical axis.
Two beams with orthogonal polarization are produced if illumination is at an angle to optical axis

## Slide 25
The idea:
Use two beams and interference to measure the path length difference between adjacent points in the sample
Differential Interference Contrast (DIC)
OPL
ns
nm

## Slide 26
WOLLASTON / NOMARSKI PRISMS
Two pieces of cemented calcite/quartz
Produce orthogonally polarized beams propagating at different angles
Placed at a back focal plane, this produces the two beams that will probe the OPL difference of our sample
.
f

## Slide 27
THE DIFFERENTIAL INTERFERENCE CONTRAST (DIC) MICROSCOPE
Tube lens
Projection Eyepiece
Camera
Imaging path
Field iris
Illumination
path
Collector
Light source
Objective
Sample
Condenser lens Aperture iris
Field lens
Polarizer (analyzer)
Wollaston
Wollaston Polarizer

## Slide 28
© Jane Selverstone, University of New Mexico, 2003
HOW DIC GENERATES CONTRAST
Both beams see same OPL
Emerge in phase
Regenerate initial polarization
No light makes it through analyzer
X

## Slide 29
© Jane Selverstone, University of New Mexico, 2003
Beams see different OPL
Right beam is phase retarded
Generate elliptical
polarization
Light makes it through analyzer
HOW DIC GENERATES CONTRAST

## Slide 30
X
Both beams see same OPL
Emerge in phase
Regenerate initial polarization
No light makes it through analyzer
HOW DIC GENERATES CONTRAST

## Slide 31
THEORY & APPL. LIGHT MICROSCOPY

## Slide 32
Contrast is directional
Contrast highlights edges
One end brighter, other is dimmer
giving a pseudo – 3D image

## Slide 33
Analyzer
Polarizer
THE DIFFERENTIAL INTERFERENCE CONTRAST (DIC) MICROSCOPE

## Slide 34
Analyzer
Condenser Nomarski prism
Polarizer
THE DIFFERENTIAL INTERFERENCE CONTRAST (DIC) MICROSCOPE

## Slide 35
SHEAR IN IMAGE
Degree of shear is set by wollaston combination
Bias of shear adjustable by shifting upper wollaston position to retard one beam more or less relative to other
Cannot be used for quantitative measurements of dry mass
But extremely useful for observing living cells

## Slide 36
THEORY & APPL. LIGHT MICROSCOPY

## Slide 37
THEORY & APPL. LIGHT MICROSCOPY

## Slide 38
THEORY & APPL. LIGHT MICROSCOPY

## Slide 39
COMPARISON OF NOMARSKI AND PHASE CONTRAST OPTICS
Phase Contrast | Nomarski
Cheaper | More expensive
Easier to set up | Fussy alignment
Uses less than full aperture of objective | Uses full aperture — closest to theoretical limit
Phase Halo — surrounds specimen and other changes | Shadow Effect — contrast greatest at shear direction maximum

## Slide 40
COMPARISON OF NOMARSKI AND PHASE CONTRAST OPTICS
Phase Contrast | Nomarski
Insensitive to birefringence in specimen or slides | Optics disrupted by birefringence
Extremely large depth of field — sensitive to artifacts far out of plane of specimen | Extremely shallow depth of field — useful for optical sectioning of specimen
Doesn’t work well with stained specimens | Works well with stained specimens; optics can be adjusted to enhance contrast

## Slide 41
THEORY & APPL. LIGHT MICROSCOPY
DIC
Phase
DIC IS HIGHER RESOLUTION THAN PHASE CONTRAST

## Slide 42
THEORY & APPL. LIGHT MICROSCOPY

## Slide 43
THEORY & APPL. LIGHT MICROSCOPY

## Slide 44
THEORY & APPL. LIGHT MICROSCOPY

## Slide 45
THEORY & APPL. LIGHT MICROSCOPY
HeLa Cell Culture
Heliozoans
(Actinophrys sol)

## Slide 46
THEORY & APPL. LIGHT MICROSCOPY
https://en.wikipedia.org/wiki/Polarized_light_microscopy#/me dia/File:Paper_Micrograph_Bright.png

## Slide 47
CONTRASTING TECHNIQUES - A SUMMARY
Brightfield - absorption
Light transmitted through sample. Only useful for colored samples. Very little contrast in unstained ones
Darkfield - scattering
Light directed from the side - only scattered light enters the microscope lenses -> sample appears as an illuminated object
Phase Contrast - phase interference
Incident light is out of phase with transmitted light. phases of the light are synchronized by an interference lens -> new image with greater contrast
Polarization Contrast – polarization
Polarized light for illumination. vibration direction of the polarized light is altered by a sample - light can pass through analyzer. The sample appears light against a black background.
Differential Interference Contrast (DIC) – polarization + phase interference
Also known as Nomarski microscopy. Synchronizing of the different phases of incident and transmitted light is done by a set of special condenser lens mounted below the stage of a microscope
Fluorescence Contrast