## Slide 1
Digital Signal Controller
TMS320F2833x
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 5: Digital Input / Output
Notes: <number>
1

## Slide 2
A(19-0)
D(31-0)
32x32 bit
Multiplier
Sectored
Flash
Program Bus
Data Bus
RAM
Boot
ROM
32-bit
Auxiliary
Registers
3
32-bit
Timers
Real-Time
JTAG
Emulation
CPU
Register Bus
R-M-W
Atomic
ALU
PIE Interrupt Manager
eQEP
12-bit ADC
Watchdog
CAN 2.0B
I2C
SCI
SPI
GPIO
ePWM
eCAP
FPU
McBSP
DMA
6 Ch.
XINTF
DMA Bus
F2833x Block Diagram
Notes: <number>

## Slide 3
XINTF Zone 6 (1Mw)
XINTF Zone 7 (1Mw)
0x000000
0x000400
0x000800
M1 SARAM (1Kw)
M0 SARAM (1Kw)
Data Program
PIE Vectors
(256 w)
PF 0 (6Kw)
XINTF Zone 0 (4Kw)
reserved
PF 1 (4Kw)
PF 2 (4Kw)
PF 3 (4Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
L4 SARAM (4Kw)
L5 SARAM (4Kw)
L6 SARAM (4Kw)
L7 SARAM (4Kw)
reserved
0x000D00
0x002000
0x006000
0x007000
0x008000
0x009000
0x00A000
0x00C000
0x000E00
0x005000
0x00B000
0x00D000
0x00E000
0x00F000
0x004000
0x010000
0x010000
0x100000
0x200000
reserved
Data Program
FLASH (256Kw)
0x300000
0x33FFF8
0x340000
PASSWORDS (8w)
reserved
User OTP (1Kw)
0x380800
ADC calibration data
0x380080
0x380090
reserved
0x380400
reserved
0x3F8000
Boot ROM (8Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
reserved
0x3F9000
0x3FA000
0x3FB000
0x3FC000
0x3FE000
0x3FFFFF
DMA Accessible:
L4, L5, L6, L7,
XINTF Zone 0, 6, 7
Dual Mapped:
L0, L1, L2, L3
CSM Protected:
L0, L1, L2, L3,
FLASH, ADC CAL,
OTP
0x3FFFC0
BROM Vectors (64w)
TMS320F2833x Memory Map

## Slide 4
•
•
•
01
00
MUX Control Bits *
00 = GPIO
01 = Peripheral 1
10 = Peripheral 2
11 = Peripheral 3
Peripheral
1
I/O DAT
Bit (R/W)
In
Out
I/O DIR Bit
0 = Input
1 = Output
GPxMUX1
GPxMUX2
GPxDIR
GPxDAT
GPxSET
GPxCLEAR
GPxTOGGLE
•
•
10
11
Peripheral
2
Peripheral
3
Pin
Internal Pull-Up
0 = enable (default GPIO 12-31)
1 = disable (default GPIO 0-11)
GPxPUD
Input Qualification
(GPIO 0-63 only)
GPxQSEL1
GPxQSEL2
GPxCTRL
* See device datasheet for pin function selection matrices
F2833x GPIO Pin Block Diagram

## Slide 5
GPIO Port A Mux1
Register (GPAMUX1)
[GPIO 0 to 15]
GPIO Port A
Direction Register
(GPADIR)
[GPIO 0 to 31]
GPIO Port A
GPIO Port B
Internal Bus
GPIO Port A Mux2
Register (GPAMUX2)
[GPIO 16 to 31]
GPIO Port B Mux1
Register (GPBMUX1)
[GPIO 32 to 47]
GPIO Port B Mux2
Register (GPBMUX2)
[GPIO 48 to 63]
GPIO Port B
Direction Register
(GPBDIR)
[GPIO 32 to 63]
GPIO Port C
GPIO Port C Mux1
Register (GPCMUX1)
[GPIO 64 to 79]
GPIO Port C Mux2
Register (GPCMUX2)
[GPIO 80 to 87]
GPIO Port C
Direction Register
(GPCDIR)
[GPIO 64 to 87]
Input
Qual
Input
Qual
F2833x GPIO Grouping Overview

## Slide 6: F2833x GPIO Pin Assignment
GPAMUX1 - Bits | 00 | 01 | 10 | 11
1,0 | GPIO0 | EPWM1A | - | -
3,2 | GPIO1 | EPWM1B | ECAP6 | MFSRB
5,4 | GPIO2 | EPWM2A | - | -
7,6 | GPIO3 | EPWM2B | ECAP5 | MCLKRB
9,8 | GPIO4 | EPWM3A | - | -
11,10 | GPIO5 | EPWM3B | MFSRA | ECAP1
13,12 | GPIO6 | EPWM4A | EPWMSYNCI | EPWMSYNC0
15,14 | GPIO7 | EPWM4B | MCLKRA | ECAP2
17,16 | GPIO8 | EPWM5A | CANTXB | /ADCSOCA0
19,18 | GPIO9 | EPWM5B | SCITXDB | ECAP3
21,20 | GPIO10 | EPWM6A | CANRXB | /ADCSOCB0
23,22 | GPIO11 | EPWM6B | SCIRXDB | ECAP4
25,24 | GPIO12 | /TZ1 | CANTXB | SPISIMOB
27,26 | GPIO13 | /TZ2 | CANRXB | SPISOMIB
29,28 | GPIO14 | /TZ3_/XHOLD | SCITXDB | SPICLKB
31,30 | GPIO15 | /TZ4_/XHOLDA | SCIRXDB | /SPISTEB
GPIO - A Multiplex Register GPAMUX1

## Slide 7: F2833x GPIO Pin Assignment
GPAMUX2 - Bits | 00 | 01 | 10 | 11
1,0 | GPIO16 | SPISIMOA | CANTXB | /TZ5
3,2 | GPIO17 | SPISOMIA | CANRXB | /TZ6
5,4 | GPIO18 | SPICLKA | SCITXDB | CANRXA
7,6 | GPIO19 | /SPISTEA | SCIRXDB | CANTXA
9,8 | GPIO20 | EQEP1A | MDXA | CANTXB
11,10 | GPIO21 | EQEP1B | MDRA | CANRXB
13,12 | GPIO22 | EQEP1S | MCLKXA | SCITXDB
15,14 | GPIO23 | EQEP1I | MFSXA | SCIRXDB
17,16 | GPIO24 | ECAP1 | EQEP2A | MDXB
19,18 | GPIO25 | ECAP2 | EQEP2B | MDRB
21,20 | GPIO26 | ECAP3 | EQEP2I | MCLKXB
23,22 | GPIO27 | ECAP4 | EQEP2S | MFSXB
25,24 | GPIO28 | SCIRXDA | /XZCS6 | /XZCS6
27,26 | GPIO29 | SCITXDA | XA19 | XA19
29,28 | GPIO30 | CANRXA | XA18 | XA18
31,30 | GPIO31 | CANTXA | XA17 | XA17
GPIO - A Multiplex Register GPAMUX2

## Slide 8: F2833x GPIO Pin Assignment
GPBMUX1 - Bits | 00 | 01 | 10 | 11
1,0 | GPIO32 | SDAA | EPWMSYNCI | /ADCSOCA0
3,2 | GPIO33 | SCLA | EPWMSYNCO | /ADCSOCB0
5,4 | GPIO34 | ECAP1 | XREADY | XREADY
7,6 | GPIO35 | SCITXDA | XR/W | XR/W
9,8 | GPIO36 | SCIRXDA | /XZCS0 | /XZCS0
11,10 | GPIO37 | ECAP2 | /XZCS7 | /XZCS7
13,12 | GPIO38 | - | /XWE0 | /XWE0
15,14 | GPIO39 | - | XA16 | XA16
17,16 | GPIO40 | - | XA0/XWE1 | XA0/XWE1
19,18 | GPIO41 | - | XA1 | XA1
21,20 | GPIO42 | - | XA2 | XA2
23,22 | GPIO43 | - | XA3 | XA3
25,24 | GPIO44 | - | XA4 | XA4
27,26 | GPIO45 | - | XA5 | XA6
29,28 | GPIO46 | - | XA6 | XA6
31,30 | GPIO47 | - | XA7 | XA7
GPIO - B Multiplex Register GPBMUX1

## Slide 9: F2833x GPIO Pin Assignment
GPBMUX2 - Bits | 00 | 01 | 10 | 11
1,0 | GPIO48 | ECAP5 | XD31 | XD31
3,2 | GPIO49 | ECAP6 | XD30 | XD30
5,4 | GPIO50 | EQEP1A | XD29 | XD29
7,6 | GPIO51 | EQEP1B | XD28 | XD28
9,8 | GPIO52 | EQEP1S | XD27 | XD27
11,10 | GPIO53 | EQEP1I | XD26 | XD26
13,12 | GPIO54 | SPISIMOA | XD25 | XD25
15,14 | GPIO55 | SPISOMIA | XD24 | XD24
17,16 | GPIO56 | SPICLKA | XD23 | XD23
19,18 | GPIO57 | /SPISTEA | XD22 | XD22
21,20 | GPIO58 | MCLKRA | XD21 | XD21
23,22 | GPIO59 | MFSRA | XD20 | XD20
25,24 | GPIO60 | MCLKRB | XD19 | XD19
27,26 | GPIO61 | MFSRB | XD18 | XD18
29,28 | GPIO62 | SCIRXDC | XD17 | XD17
31,30 | GPIO63 | SCITXDC | XD16 | XD16
GPIO - B Multiplex Register GPBMUX2

## Slide 10: F2833x GPIO Pin Assignment
GPCMUX1 - Bits | 00 or 01 | 10 or 11
1,0 | GPIO64 | XD15
3,2 | GPIO65 | XD14
5,4 | GPIO66 | XD13
7,6 | GPIO67 | XD12
9,8 | GPIO68 | XD11
11,10 | GPIO69 | XD10
13,12 | GPIO70 | XD9
15,14 | GPIO71 | XD8
17,16 | GPIO72 | XD7
19,18 | GPIO73 | XD6
21,20 | GPIO74 | XD5
23,22 | GPIO75 | XD4
25,24 | GPIO76 | XD3
27,26 | GPIO77 | XD2
29,28 | GPIO78 | XD1
31,30 | GPIO79 | XD0
GPIO - C Multiplex Register
GPCMUX2 - Bits | 00 or 01 | 10 or 11
1,0 | GPIO80 | XA8
3,2 | GPIO81 | XA9
5,4 | GPIO82 | XA10
7,6 | GPIO83 | XA11
9,8 | GPIO84 | XA12
11,10 | GPIO85 | XA13
13,12 | GPIO86 | XA14
15,14 | GPIO87 | XA15
17,16 | - | -
19,18 | - | -
21,20 | - | -
23,22 | - | -
25,24 | - | -
27,26 | - | -
29,28 | - | -
31,30 | - | -

## Slide 11
Qualification available on ports A & B (GPIO 0 - 63) only
Individually selectable per pin
  no qualification (peripherals only)
  sync to SYCLKOUT only
  qualify 3 samples
  qualify 6 samples
Port C pins are fixed as ‘sync to SYSCLKOUT’
Input
Qualification
pin
to GPIO and peripheral modules
SYSCLKOUT
T
T
T
samples taken
T = qualification period
F2833x GPIO Input Qualification

## Slide 12
0x00 no qualification (SYNC to SYSCLKOUT)
0x01 QUALPRD = TSYSCLKOUT * 2
0x02 QUALPRD = TSYSCLKOUT * 4
… … …
0xFF QUALPRD = TSYSCLKOUT * 510
00 = sync to SYSCLKOUT only
01 = qual to 3 samples
10 = qual to 6 samples
11 = no sync or qual (for peripheral only; GPIO same as 00)
GPAQSEL1 / GPAQSEL2 / GPBQSEL1 / GPBQSEL2
16 pins configured per register
0
31
QUALPRD0
QUALPRD1
QUALPRD2
QUALPRD3
GPACTRL / GPBCTRL
31 24 16 8 0
B: GPIO63-56 GPIO55-48 GPIO47-40 GPIO39-32
A: GPIO31-24 GPIO23-16 GPIO15-8 GPIO7-0
F2833x GPIO Input Qualification Registers

## Slide 13
Register Description
GPACTRL GPIO A Control Register [GPIO 0 – 31]
GPAQSEL1 GPIO A Qualifier Select 1 Register [GPIO 0 – 15]
GPAQSEL2 GPIO A Qualifier Select 2 Register [GPIO 16 – 31]
GPAMUX1 GPIO A Mux1 Register [GPIO 0 – 15]
GPAMUX2 GPIO A Mux2 Register [GPIO 16 – 31]
GPADIR GPIO A Direction Register [GPIO 0 – 31]
GPAPUD GPIO A Pull-Up Disable Register [GPIO 0 – 31]
GPBCTRL GPIO B Control Register [GPIO 32 – 63]
GPBQSEL1 GPIO B Qualifier Select 1 Register [GPIO 32 – 47]
GPBQSEL2 GPIO B Qualifier Select 2 Register [GPIO 48 – 63]
GPBMUX1 GPIO B Mux1 Register [GPIO 32 – 47]
GPBMUX2 GPIO B Mux2 Register [GPIO 48 – 63]
GPBDIR GPIO B Direction Register [GPIO 32 – 63]
GPBPUD GPIO B Pull-Up Disable Register [GPIO 32 – 63]
GPCMUX1 GPIO C Mux1 Register [GPIO 64 – 79]
GPCMUX2 GPIO C Mux2 Register [GPIO 80 – 87]
GPCDIR GPIO C Direction Register [GPIO 64 – 87]
GPCPUD GPIO C Pull-Up Disable Register [GPIO 64 – 87]
C2833x GPIO Control Registers

## Slide 14
Register Description
GPADAT GPIO A Data Register [GPIO 0 – 31]
GPASET GPIO A Data Set Register [GPIO 0 – 31]
GPACLEAR GPIO A Data Clear Register [GPIO 0 – 31]
GPATOGGLE GPIO A Data Toggle [GPIO 0 – 31]
GPBDAT GPIO B Data Register [GPIO 32 – 63]
GPBSET GPIO B Data Set Register [GPIO 32 – 63]
GPBCLEAR GPIO B Data Clear Register [GPIO 32 – 63]
GPBTOGGLE GPIO B Data Toggle [GPIO 32 – 63]
GPCDAT GPIO C Data Register [GPIO 64 – 87]
GPCSET GPIO C Data Set Register [GPIO 64 – 87]
GPCCLEAR GPIO C Data Clear Register [GPIO 64 – 87]
GPCTOGGLE GPIO C Data Toggle [GPIO 64 – 87]
C2833x GPIO Data Registers

## Slide 15
PLL
XCLKIN
Watchdog
Module
VCOCLK
OSCCLK
•
C28x
Core
CLKIN
SYSCLKOUT
HISPCP
LOSPCP
HSPCLK
LSPCLK
•
•
DIV CLKIN
0 0 0 0 OSCCLK / n * (PLL bypass)
0 0 0 1 OSCCLK x 1 / n
0 0 1 0 OSCCLK x 2 / n
0 0 1 1 OSCCLK x 3 / n
0 1 0 0 OSCCLK x 4 / n
0 1 0 1 OSCCLK x 5 / n
0 1 1 0 OSCCLK x 6 / n
0 1 1 1 OSCCLK x 7 / n
1 0 0 0 OSCCLK x 8 / n
1 0 0 1 OSCCLK x 9 / n
1 0 1 0 OSCCLK x 10 / n
(PLL bypass)
HSPCLK
LSPCLK
Input Clock Fail Detect Circuitry
PLL will issue a “limp mode” clock (1-4 MHz) if input clock is removed after PLL has locked.
An internal device reset will also be issued (XRSn pin not driven).
SysCtrlRegs.PLLSTS.bit.DIVSEL
•
SysCtrlRegs.PLLCR.bit.DIV
ADC
SCI, SPI, I2C,
McBSP
All other peripherals clocked by SYSCLKOUT
crystal
X2
XTAL OSC
X1
1/n
MUX
DIVSEL n
0x /4 *
10 /2
11 /1
* default
Note: /1 mode can only be used when PLL is bypassed
F2833x Clock Module

## Slide 16
H/LSPCLK Peripheral Clock Frequency
0 0 0 SYSCLKOUT / 1
0 0 1 SYSCLKOUT / 2 (default HISPCP)
0 1 0 SYSCLKOUT / 4 (default LOSPCP)
0 1 1 SYSCLKOUT / 6
1 0 0 SYSCLKOUT / 8
1 0 1 SYSCLKOUT / 10
1 1 0 SYSCLKOUT / 12
1 1 1 SYSCLKOUT / 14
2 - 0
15 - 3
HSPCLK
reserved
SysCtrlRegs.HISPCP
2 - 0
15 - 3
LSPCLK
reserved
SysCtrlRegs.LOSPCP
ADC
SCI / SPI /
I2C / McBSP
NOTE:
All Other Peripherals Clocked By SYSCLKOUT
F2833x Clock Scaling

## Slide 17
15
14
13
11
10
9
8
12
7
6
5
4
3
2
1
0
SysCtrlRegs.PCLKCR0
SysCtrlRegs.PCLKCR1
SysCtrlRegs.PCLKCR3
15
14
13
11
10
9
8
12
7
6
5
4
3
2
1
0
15 - 14
13
12
10
9
8
7 - 0
11
ECANB
ENCLK
ECANA
ENCLK
SCIB
ENCLK
SCIA
ENCLK
SPIA
ENCLK
MA
ENCLK
MB
ENCLK
I2CA
ENCLK
ADC
ENCLK
TBCLK
SYNC
SCIC
ENCLK
EQEP2
ENCLK
EQEP1
ENCLK
ECAP4
ENCLK
ECAP3
ENCLK
ECAP2
ENCLK
ECAP1
ENCLK
ECAP5
ENCLK
ECAP6
ENCLK
EPWM6
ENCLK
EPWM5
ENCLK
EPWM4
ENCLK
EPWM3
ENCLK
EPWM2
ENCLK
EPWM1
ENCLK
CPUTIMER0
ENCLK
CPUTIMER1
ENCLK
CPUTIMER2
ENCLK
DMA
ENCLK
XINTF
ENCLK
GPIOIN
ENCLK
reserved
reserved
reserved
reserved
reserved
reserved
reserved
reserved
reserved
Module Enable Clock Bit
0 = disable (default) 1 = enable
F2833x Clock Control Unit

## Slide 18
Resets the F2833x if the CPU crashes
  Watchdog counter runs independent of CPU
  If counter overflows, a reset or interrupt is triggered (user selectable)
  CPU must write correct data key sequence to reset the counter before overflow
Watchdog must be serviced or disabled within 4.37ms after reset (assuming a 30 MHz OSCCLK)
This time period translates into 645000 instructions, if CPU runs at 150MHz!
Watchdog Timer

## Slide 19
6 - Bit
Free -
Running
Counter
CLR
/2
/4
/8
/16
/32
/64
OSCCLK
System
Reset
101
100
011
010
001
000
111
110
•
•
•
•
8 - Bit Watchdog
Counter
CLR
One-Cycle
Delay
Watchdog
Reset Key
Register
55 + AA
Detector
•
1 0 1
•
•
•
•
/
/
3
3
WDCR . 2 - 0
WDCR . 6
WDPS
WDDIS
WDCR . 7
WDFLAG
WDCNTR . 7 - 0
WDKEY . 7 - 0
WDCR . 5 - 3
WDCHK 2-0
Bad WDCR Key
/512
Output
Pulse
WDRST
WDINT
SCSR .1
WDENINT
•
•
•
SCSR . 0
WDOVERRIDE
Good Key
Watchdog Timer Module

## Slide 20
WDFLAG
WDDIS
7
6
5 - 3
2 - 0
WDPS
WDCHK
Logic Check Bits
Write as 101 or reset immediately triggered
WD Prescale
Selection Bits
Watchdog Disable Bit
Write 1 to disable
(Functions only if WD OVERRIDE
bit in SCSR is equal to 1)
reserved
15 - 8
WD Flag Bit
Gets set when the WD causes a reset
  Writing a 1 clears this bit
  Writing a 0 has no effect
Watchdog Timer Control Register
Register: SysCtrlRegs.WDCR

## Slide 21: Resetting the Watchdog
WDKEY write values:
  0x55 - counter enabled for reset on next 0xAA write
  0xAA - counter set to zero if reset enabled
Writing any other value has no effect
Watchdog should not be serviced solely in an ISR
  If main code crashes, but interrupt continues to execute, the watchdog will not catch the crash
  Could put the 0x55 WDKEY in the main code, and the 0xAA WDKEY in an ISR; this catches main code crashes and also ISR crashes
reserved
7 - 0
15 - 8
WDKEY

## Slide 22: WDKEY Write Results
Sequential
Step
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Value Written
to WDKEY
AAh
AAh
55h
55h
55h
AAh
AAh
55h
AAh
55h
23h
AAh
55h
AAh
Result
No action
No action
WD counter enabled for reset on next AAh write
WD counter enabled for reset on next AAh write
WD counter enabled for reset on next AAh write
WD counter is reset
No action
WD counter enabled for reset on next AAh write
WD counter is reset
WD counter enabled for reset on next AAh write
No effect; WD counter not reset on next AAh write
No action due to previous invalid value
WD counter enabled for reset on next AAh write
WD counter is reset

## Slide 23: System Control and Status Register
WD Override (protect bit)
Protects WD from being disabled
0 = WDDIS bit in WDCR has no effect (WD cannot be disabled)
1 = WDDIS bit in WDCR can disable the watchdog
This bit is a clear-only bit (write 1 to clear)
The reset default of this bit is a 1
0
1
2
15 - 3
WDOVERRIDE
WDENINT
WDINTS
reserved
WD Enable Interrupt
WD Interrupt Status
(read only)
0 = active
1 = not active
0 = WD generates a DSP reset
1 = WD generates a WDINT interrupt
Register: SysCtrlRegs.SCSR

## Slide 24
Low Power
Mode
CPU Logic
Clock
Peripheral
Logic Clock
Watchdog
Clock
PLL /
OSC
Normal Run
IDLE
STANDBY
HALT
on
off
off
off
on
on
off
off
on
on
on
off
on
on
on
off
See device datasheet for power consumption in each mode
Low Power Modes

## Slide 25
1 - 0
7 - 2
14 - 8
LPM0
WDINTE
QUALSTDBY
reserved
Low Power Mode Selection
00 = Idle (default)
01 = Standby
1x = Halt
Wake from STANDBY
GPIO signal qualification *
000000 = 2 OSCCLKs
000001 = 3 OSCCLKs
111111 = 65 OSCCLKS (default)
.
.
.
.
.
.
.
.
.
15
Watchdog Interrupt wake device from STANDBY
0 = disable (default)
1 = enable
Low Power Mode Entering
1. Set LPM bits
2. Enable desired exit interrupt(s)
3. Execute IDLE instruction
4. The Power down sequence of the hardware
depends on LP mode
* QUALSTDBY will qualify the GPIO wakeup signal in series with the GPIO port qualification. This is useful when GPIO port qualification is not available or insufficient for wake-up purposes.
Register: SysCtrlRegs.LPMCR0
Low Power Mode Control Register 0

## Slide 26
IDLE
STANDBY
HALT
RESET
or
XNMI
yes
yes
yes
Any Enabled Interrupt
yes
no
no
yes
yes
no
Exit
Interrupt
Low Power
Mode
Watchdog
Interrupt
GPIO Port A Signal
yes
yes
yes
Low Power Mode Exit

## Slide 27
Wake device from
HALT and STANDBY mode
(GPIO Port A)
0 = disable (default)
1 = enable
0
GPIO2
GPIO14
GPIO8
GPIO11
GPIO5
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
GPIO0
GPIO1
GPIO4
GPIO3
GPIO9
GPIO6
GPIO10
GPIO7
GPIO12
GPIO13
GPIO15
16
GPIO18
GPIO30
GPIO24
GPIO27
GPIO21
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
GPIO16
GPIO17
GPIO20
GPIO19
GPIO25
GPIO22
GPIO26
GPIO23
GPIO28
GPIO29
GPIO31
Register: SysCtrlRegs.GPIOLPMSEL
GPIO Low Power Wakeup Select

## Slide 28: Lab 5_1: “Binary Counter” at 4 LEDs
Display the 4 least significant bits of a counter variable at LED LD1(GPIO9), LD2(GPIO11), LD3(GPIO34) and LD4(GPIO49) of the Peripheral Explorer Board.
Increment variable “counter” every 100 milliseconds
Use a software delay loop to generate the interval of 100 milliseconds
Objective:
Project - Files :
C - source file “Lab5_1.c”
Start assembly code file: “DSP2833x_CodeStartBranch.asm”
2. Register Variable Definition File: “DSP2833x_GlobalVariableDefs.c”
3. Linker Command File:
“28335_RAM_lnk.cmd”
“DSP2833x_Headers_nonBIOS.cmd”
4. Runtime Library “rts2800_fpu32.lib”
0000
0001
0010
1111
…
Notes: <number>

## Slide 29
“DSP2833x_GlobalVariableDefs.c”
Definition of global variables for all memory mapped peripheral registers based on predefined structures
Master Header File is “DSP2833x_Device.h”
Example GpioDataRegs:
    volatile struct GPIO_DATA_REGS GpioDataRegs;
This structure variable combines all registers, which belong to this peripheral group, e.g.:
    GpioDataRegs.GPADAT
Each register is declared as a union to allow 32-bit - (“all”) and single bit field - accesses (“bit”), e.g.:
    GpioDataRegs.GPADAT.bit.GPIO9 = 1;
    GpioDataRegs.GPADAT.all = 0x0000FFFF;
Steps to be done are:
  Add “DSP2833x_GlobalVariableDefs.c” to project
  Include “DSP2833x_Device.h” into your C-code
Notes: <number>

## Slide 30
“Lab 5_1 Register usage”
Registers involved in LAB 5_1:
Core Initialisation:
  Watchdog - Timer - Control : WDCR
  PLL Clock Register : PLLCR
  High Speed Clock Pre-scaler : HISPCP
  Low Speed Clock Pre-scaler : LOSPCP
  Peripheral Clock Control : PCLKCRx
  System Control and Status : SCSR
Access to LED‘s (GPIO9, GPIO11,GPIO34,GPIO49):
  GPA and GPB Multiplex Register:
    GPAMUX1, GPAMUX2, GPBMUX1, GPBMUX2
  GPA and GPB Direction Register:
    GPADIR and GPBDIR
  GPA and GPB Data Register:
    GPASET, GPACLEAR, GPBSET, GPBCLEAR
Notes: <number>

## Slide 31: Lab Exercise 5_2
Modify the C -source – code to:
  switch 4 LEDs at GPIO9, GPIO11, GPIO34 and GPIO49 sequentially on and off
  use a software time delay from Lab5_1
GPIO9 GPIO11 GPIO34 GPIO49
Step 1
Step 3
Step 2
Step 4
Step 5
Step 6

## Slide 32: Lab 5_3: Digital Input (GPIO 15...12)
  a 4 bit hex encoder connected to GPIO15…GPIO12
  4 LED‘s connected to GPIO9, GPIO11, GPIO34 and GPIO49
  read the status of encoder and display it at the LEDs
Objective:
Project - Files :
1. C - source file: “Lab5_3.c”
2. Register Definition File: “DSP2833x_GlobalVariableDefs.c”
3. Linker Command File:
“28335_RAM_lnk.cmd”
4. Runtime Library: “rts2800_fpu32.lib”
Notes: <number>

## Slide 33: Lab 5_4: Digital In- and Output
Mix between Lab5_1 and LAB5_3:
    change the loop – speed of Lab5_1 depending of the status of the hex – encoder.
    If hex – encoder reads “0000”, set the time period for the LED update to approximately 100 ms.
    If hex - encoder reads “1111”, set the time period for the LED update to approximately 1.6 seconds.
    Adjust the period for all other encoder values accordingly.

## Slide 34: Lab 5_5: Start - /Stop Control
Add a start/stop function to Lab5_4:
Peripheral Explorer Board Pushbuttons:
    PB1 (GPIO17) to start/restart control code
    PB2 (GPIO48) to stop/suspend control code
If PB1 is pushed, LED counting should start / resume
If PB2 is pushed, LED counting should stop.