## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 7: PWM and Capture F2833x
Digital Signal Controller
TMS320F2833x

## Slide 2: ePWM Block Diagram
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
TZSEL . 15 - 0
EPWMxA
EPWMxB
SYSCLKOUT
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK

## Slide 3: ePWM Time-Base Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
SYSCLKOUT
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Trip
Zone
TZSEL . 15 - 0
EPWMxA
EPWMxB
TZy

## Slide 4: ePWM Phase Synchronization
SyncIn
SyncOut
CTR=zero
CTR=CMPB
X
En
o
o
o
o
o
o
o
=120°
Phase

EPWM2A
EPWM2B
SyncIn
SyncOut
CTR=zero
CTR=CMPB
X
En
o
o
o
o
o
o
o
=240°
Phase

EPWM3A
EPWM3B
SyncIn
SyncOut
CTR=zero
CTR=CMPB
X
En
o
o
o
o
o
o
o
=0°
Phase

EPWM1A
EPWM1B
=120°
=120°
=240°
Ext. SyncIn
(optional)
To eCAP1
SyncIn

## Slide 5: ePWM Time-Base Count Modes
TBCTR
TBCTR
TBCTR
TBPRD
TBPRD
TBPRD
Count Up Mode
Count Down Mode
Count Up and Down Mode
Asymmetrical
Waveform
Asymmetrical
Waveform
Symmetrical
Waveform

## Slide 6: ePWM Time-Base Module Registers
Name Description Structure
TBCTL Time-Base Control EPwmxRegs.TBCTL.all =
TBSTS Time-Base Status EPwmxRegs.TBSTS.all =
TBPHS Time-Base Phase EPwmxRegs.TBPHS =
TBCTR Time-Base Counter EPwmxRegs.TBCTR =
TBPRD Time-Base Period EPwmxRegs.TBPRD =

## Slide 7: ePWM Register TBCTL
Upper Register:
FREE_SOFT
PHSDIR
CLKDIV
HSPCLKDIV
15 - 14
13
12 - 10
9 - 7
TBCLK = SYSCLKOUT / (HSPCLKDIV * CLKDIV)
TB Clock Prescale
000 = /1 (default)
001 = /2
010 = /4
011 = /8
100 = /16
101 = /32
110 = /64
111 = /128
High Speed TB
Clock Prescale
000 = /1
001 = /2 (default)
010 = /4
011 = /6
100 = /8
101 = /10
110 = /12
111 = /14
Emulation Halt Behavior
00 = stop after next CTR inc/dec
01 = stop when:
Up Mode; CTR = PRD
Down Mode; CTR = 0
Up/Down Mode; CTR = 0
1x = free run (do not stop)
Phase Direction
0 = count down after sync
1 = count up after sync
(HSPCLKDIV is for legacy compatibility)

## Slide 8: ePWM Register TBCTL
Lower Register:
CTRMODE
SWFSYNC
SYNCOSEL
PRDLD
PHSEN
6
5 - 4
3
1 - 0
2
Software Force Sync Pulse
0 = no action
1 = force one-time sync
Sync Output Select
(source of EPWMxSYNC0 signal)
00 = EPWMxSYNCI
01 = CTR = 0
10 = CTR = CMPB
11 = disable SyncOut
Counter Mode
00 = count up
01 = count down
10 = count up and down
11 = stop – freeze (default)
Period Shadow Load
0 = load on CTR = 0
1 = load immediately
Phase Reg. Enable
0 = disable
1 = CTR = TBPHS on
EPWMxSYNCI signal

## Slide 9: ePWM Register TBSTS
CTRDIR
CTRMAX
SYNCI
reserved
15 - 3
0
2
1
Counter Max Latched
0 = max value not reached
1 = CTR = 0xFFFF (write 1 to clear)
External Input Sync Latched
0 = no sync event occurred
1 = sync has occurred (write 1 to clear)
Counter Direction
0 = CTR counting down
1 = CTR counting up

## Slide 10: Lab 7_1: Generate a 1 KHz Signal at ePWM1A
Generate a 1 KHz square wave signal at ePWM1A with a duty cycle of 50 %
Measure it with an oscilloscope or
Connect the signal to an external buzzer or loudspeaker
Registers involved:
  TBPRD: define signal frequency
  TBCTL: setup operating mode and time prescale
  AQCTLA: define signal shape for ePWM1A
Objective:

## Slide 11: Lab 7_2: Generate a 3 phase system
Generate three 1 KHz square wave signals at ePWM1A, 2A and 3A with duty cycles of 50 % and a phase shift of 120° and 240° between the signals
Measure all three signals with an oscilloscope
Registers involved:
  TBPRD: define signal frequency
  TBCTL: setup operating mode and time prescale
  AQCTLA: define signal shape for ePWM1A
  TBPHS: definition of the phase shift for 2A and 3A
Objective:

## Slide 12: What is Pulse Width Modulation?
PWM is a scheme to represent a signal as a sequence of pulses
  fixed carrier frequency
  fixed pulse amplitude
  pulse width proportional to instantaneous signal amplitude
  PWM energy ≈ original signal energy
t
Original Signal
T
t
PWM representation

## Slide 13: Why use PWM with Power Switching Devices?
Desired output currents or voltages are known
Power switching devices are transistors
  Difficult to control in proportional region
  Easy to control in saturated region
PWM is a digital signal  easy for DSP to output
PWM approx.
of desired signal
DC Supply
Desired
signal to
system
?
DC Supply
Unknown Base Signal
Base Signal known with PWM
PWM
Notes: <number>
Relationship between PWM gate signal and PWM modulated motor phase current is essentially 1 to 1 since transistor is operated in the saturated region. If PWM representation of desired phase current is known, gate signal is identical.
To produce a real sinusoidal phase current, the transistor would have to be operated in the proportional region, i.e. Icollector = *Ibase (NPN transistor terminology!). The needed gate signal would be difficult to determine. In addition, power loss and high temperature problems can occur since the transistor will be dissipating power.

## Slide 14: ePWM Compare Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
SYSCLKOUT
EPWMxSYNCI
EPWMxSYNCI
TBCLK
Trip
Zone
TZSEL . 15 - 0
EPWMxA
EPWMxB
TZy

## Slide 15: ePWM Compare Event Waveforms
TBCTR
TBCTR
TBCTR
TBPRD
TBPRD
TBPRD
Count Up Mode
Count Down Mode
Count Up and Down Mode
Asymmetrical
Waveform
Asymmetrical
Waveform
Symmetrical
Waveform
CMPA
CMPA
CMPA
CMPB
CMPB
CMPB





















= compare events are fed to the Action Qualifier Module

## Slide 16: ePWM Compare Module Registers
Name Description Structure
CMPCTL Compare Control EPwmxRegs.CMPCTL.all =
CMPA Compare A EPwmxRegs.CMPA =
CMPB Compare B EPwmxRegs.CMPB =

## Slide 17: ePWM Compare Control Register EPwmxRegs.CMPCTL
6
5
4
1 - 0
LOADBMODE
LOADAMODE
reserved
3 - 2
SHDWBMODE
SHDWAMODE
CMPA and CMPB Operating Mode
0 = shadow mode;
double buffer w/ shadow register
1 = immediate mode;
shadow register not used
CMPA and CMPB Shadow Load Mode
00 = load on CTR = 0
01 = load on CTR = PRD
10 = load on CTR = 0 or PRD
11 = freeze (no load possible)
SHDWBFULL
15 - 10
9
8
SHDWAFULL
7
reserved
reserved
CMPA and CMPB Shadow Full Flag
(bit automatically clears on load)
0 = shadow not full
1 = shadow full

## Slide 18: ePWM Action Qualifier Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
SYSCLKOUT
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Trip
Zone
TZSEL . 15 - 0
EPWMxA
EPWMxB
TZy

## Slide 19: ePWM Action Qualifier Actions
Z

Z

Z
X
Z
T
CA

CA

CA
X
CA
T
CB

CB

CB
X
CB
T
P

P

P
X
P
T
SW

SW

SW
X
SW
T
Do Nothing
Clear Low
Set High
Toggle
S/W
Force
EPWM
Output
Actions
Time-Base Counter equals:
Zero
CMPA
CMPB
TBPRD

## Slide 20: Independent Modulation on EPWMA / B
Z

P
X
CB
X
CA

Z

P
X
CB
X
CA

Z

P
X
Z

P
X
CB

CA
X
Z

P
X
CB

CA
X
Z

P
X
TBCTR
TBPRD




EPWMA
EPWMB

## Slide 21: Moving Pulse on EPWMA
CA

CB

CA

CB

Z
T
Z
T
Z
T
TBCTR
TBPRD




EPWMA
EPWMB

## Slide 22: Independent Modulation on EPWMA / B
TBCTR
TBPRD








CA

CA

CA

CA

CB

CB

CB

CB

EPWMA
EPWMB

## Slide 23: ePWM Action Qualifier Module Registers
Name Description Structure
AQCTLA AQ Control Output A EPwmxRegs.AQCTLA.all =
AQCTLB AQ Control Output B EPwmxRegs.AQCTLB.all =
AQSFRC AQ S/W Force EPwmxRegs.AQSFRC.all =
AQCSFRC AQ Cont. S/W Force EPwmxRegs.AQCSFRC.all =

## Slide 24: Action Qualifier Control Register EPwmxRegs.AQCTLy (y = A or B)
ZRO
CBU
CAD
CAU
PRD
1 - 0
CBD
15 - 12
reserved
3 - 2
5 - 4
7 - 6
9 - 8
11 - 10
00 = do nothing (action disabled)
01 = clear (low)
10 = set (high)
11 = toggle (low  high; high  low)
Action when
CTR = CMPB
on DOWN Count
Action when
CTR = CMPB
on UP Count
Action when
CTR = CMPA
on DOWN Count
Action when
CTR = CMPA
on UP Count
Action when
CTR = 0
Action when
CTR = PRD

## Slide 25: Action Qualifier SW Force Register EPwmxRegs.AQSFRC
ACTSFA
RLDCSF
OTSFB
ACTSFB
OTSFA
1 - 0
15 - 8
reserved
2
4 - 3
5
7 - 6
AQSFRC Shadow Reload Options
00 = load on event CTR = 0
01 = load on event CTR = PRD
10 = load on event CTR = 0 or CTR = PRD
11 = load immediately (from active reg.)
One-Time S/W Force on Output B / A
0 = no action
1 = single s/w force event
Action on One-Time S/W Force B / A
00 = do nothing (action disabled)
01 = clear (low)
10 = set (high)
11 = toggle (low  high; high  low)

## Slide 26: Continuous SW Force Register EPwmxRegs.AQCSFRC
CSFA
CSFB
1 - 0
15 - 4
reserved
3 - 2
Continuous S/W Force on Output B / A
00 = forcing disabled
01 = force continuous low on output
10 = force continuous high on output
11 = forcing disabled

## Slide 27: Lab 7_3: 1 KHz Signal with variable pulse width at ePWM1A
Generate a 1 KHz square wave signal at ePWM1A with a variable duty cycle between 0 and 100%
Measure the pulse with an oscilloscope
Registers involved:
  TBPRD: define signal frequency
  TBCTL: setup operating mode and time prescale
  CMPA: setup the pulse width for ePWM1A
  AQCTLA: define signal shape for ePWM1A
Objective:

## Slide 28: Lab 7_4: a pair of complementary 1 KHz signals at ePWM1A and ePWM1B
Generate a 1 KHz square wave signal at ePWM1A with a variable duty cycle between 0 and 100%
Generate a complementary signal at ePWM1B
Measure the pulses with an oscilloscope
Registers involved:
  TBPRD: define signal frequency
  TBCTL: setup operating mode and time prescale
  CMPA: setup the pulse width for ePWM1A / 1B
  AQCTLB: define signal shape for ePWM1B
  AQCTLA: define signal shape for ePWM1A
Objective:

## Slide 29: Lab 7_5: Independent Modulation of ePWM1A and ePWM1B
TBCTR
TBPRD








CA

CA

CA

CA

CB

CB

CB

CB

EPWMA
EPWMB

## Slide 30: Voltage source inverter components
Power
Switching
Devices
Three phase
outputs to drive the motor
terminals


Upper & lower
devices can not
be turned on
simultaneously
(dead band)
PWM signal is
applied between
gate and source
DC bus
capacitor




Notes: <number>

## Slide 31: Motivation for Dead-Band
to power switching device
supply rail
gate signals are
complementary PWM
Transistor gates turn on faster than they shut off
Short circuit if both gates are on at same time!

## Slide 32: ePWM Dead-Band Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
SYSCLKOUT
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Trip
Zone
TZSEL . 15 - 0
EPWMxA
EPWMxB
TZy

## Slide 33: ePWM Dead-Band Module Block Diagram
Rising Edge Delay
In Out
(10-bit counter)
Falling Edge Delay
In Out
(10-bit counter)



0
1



0
1



0
1



1
0






PWMxA - IN
PWMxB - IN
PWMxB
PWMxA
S1
S0
S2
S3
FED
RED
OUT-MODE
POLSEL



0
1



0
1
S4
S5
IN-MODE

## Slide 34: ePWM Dead-Band Module Registers
Rising Edge Delay = TTBCLK x DBRED
Falling Edge Delay = TTBCLK x DBFED
Name Description Structure
DBCTL Dead-Band Control EPwmxRegs.DBCTL.all =
DBRED 10-bit Rising Edge Delay EPwmxRegs.DBRED =
DBFED 10-bit Falling Edge Delay EPwmxRegs.DBFED =

## Slide 35: ePWM Dead Band Control Register
Polarity Select
00 = active high
01 = active low complementary (RED)
10 = active high complementary (FED)
11 = active low
Out-Mode Control
00 = disabled (DBM bypass)
01 = PWMxA = no delay
PWMxB = FED
10 = PWMxA = RED
PWMxB = no delay
11 = RED & FED (DBM fully enabled)
OUT_MODE
POLSEL
1 - 0
15 - 6
reserved
3 - 2
IN_MODE
5 - 4
In-Mode Control
00 = PWMxA is source for RED and FED
01 = PWMxA is source for FED
PWMxB is source for RED
10 = PWMxA is source for RED
PWMxB is source for FED
11 = PWMxB is source for RED and FED

## Slide 36: Lab 7_6: Dead Band Unit for ePWM1A and ePWM1B
Add a delay time for rising edges on a pair of complementary signals ePWM1A and ePWM1B
Active High Complementary (AHC) Mode
Input signal to Dead-Band Unit is ePWM1A
Dead Band Unit will generate ePWM1A and ePWM1B
Use Lab7_4 as starting point
New Registers involved:
  DBRED: Dead Band Unit Rising Edge Delay
  DBFED: Dead Band Unit Falling Edge Delay
  DBCTL: Dead Band Unit Control Register
Objective:

## Slide 37: ePWM Chopper Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
SYSCLKOUT
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Trip
Zone
TZSEL . 15 - 0
EPWMxA
EPWMxB
TZy

## Slide 38: Purpose of the PWM Chopper Module
Allows a high frequency carrier signal to modulate the PWM waveform generated by the Action Qualifier and Dead-Band modules
Used with pulse transformer-based gate drivers to control power switching elements

## Slide 39: ePWM Chopper Waveform
EPWMxA
EPWMxB
CHPFREQ
EPWMxA
EPWMxB
OSHT
EPWMxA
Programmable
Pulse Width
(OSHTWTH)
Sustaining
Pulses
With One-Shot Pulse on EPWMxA and/or EPWMxB

## Slide 40: ePWM Chopper Module Registers
Name Description Structure
PCCTL PWM-Chopper Control EPwmxRegs.PCCTL.all =

## Slide 41: ePWM Chopper Control Register EPwmxRegs.PCCTL
CHPEN
CHPDUTY
CHPFREQ
OSHTWTH
0
15 - 11
reserved
4 - 1
7 - 5
10 - 8
Chopper Enable
0 = disable (bypass)
1 = enable
One-Shot Pulse Width
0000 = 8 / SYSCLKOUT 1000 = 72 / SYSCLKOUT
0001 = 16 / SYSCLKOUT 1001 = 80 / SYSCLKOUT
0010 = 24 / SYSCLKOUT 1010 = 88 / SYSCLKOUT
0011 = 32 / SYSCLKOUT 1011 = 96 / SYSCLKOUT
0100 = 40 / SYSCLKOUT 1100 = 104 / SYSCLKOUT
0101 = 48 / SYSCLKOUT 1101 = 112 / SYSCLKOUT
0110 = 56 / SYSCLKOUT 1110 = 120 / SYSCLKOUT
0111 = 64 / SYSCLKOUT 1111 = 128 / SYSCLKOUT
Chopper Clk Freq.
000 = SYSCLKOUT/8  1
001 = SYSCLKOUT/8  2
010 = SYSCLKOUT/8  3
011 = SYSCLKOUT/8  4
100 = SYSCLKOUT/8  5
101 = SYSCLKOUT/8  6
110 = SYSCLKOUT/8  7
111 = SYSCLKOUT/8  8
Chopper Clk Duty Cycle
000 = 1/8 (12.5%)
001 = 2/8 (25.0%)
010 = 3/8 (37.5%)
011 = 4/8 (50.0%)
100 = 5/8 (62.5%)
101 = 6/8 (75.0%)
110 = 7/8 (87.5%)
111 = reserved

## Slide 42: Lab 7_7: Chopper Mode Signals add ePWM1A and ePWM1B
The pair of complementary signals ePWM1A and ePWM1B will be modulated by a chopper frequency of 2.344 MHz
Chopper Mode Duty Cycle = 50%
One shot pulse width = 800 ns
Use Lab7_5 as starting point
Objective:

## Slide 43: ePWM Trip-Zone Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
SYSCLKOUT
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Trip
Zone
TZSEL . 15 - 0
EPWMxA
EPWMxB
TZy

## Slide 44: Trip-Zone Module Features
Trip-Zone has a fast, clock independent logic path to high-impedance the EPWMxA/B output pins
Interrupt latency may not protect hardware when responding to over current conditions or short-circuits through ISR software
Supports: #1) one-shot trip for major short circuits or over current conditions
#2) cycle-by-cycle trip for current limiting operation
DSP
core
P
W
M
O
U
T
P
U
T
S
EPWMxTZINT
EPWM1A
TZ6
TZ5
TZ4
TZ3
TZ2
TZ1
Over
Current
Sensors
Cycle-by-Cycle
Mode
One-Shot
Mode
EPWM1B
EPWM2A
EPWM2B
EPWM3A
EPWM3B
EPWM4A
EPWM4B
EPWM5A
EPWM5B
EPWM6A
EPWM6B

## Slide 45: ePWM Trip-Zone Module Registers
Name Description Structure
TZCTL Trip-Zone Control EPwmxRegs.TZCTL.all =
TZSEL Trip-Zone Select EPwmxRegs.TZSEL.all =
TZEINT Enable Interrupt EPwmxRegs.TZEINT.all =
TZFLG Trip-Zone Flag EPwmxRegs.TZFLG.all =
TZCLR Trip-Zone Clear EPwmxRegs.TZCLR.all =
TZFRC Trip-Zone Force EPwmxRegs.TZFRC.all =

## Slide 46: ePWM Trip-Zone Control Register EPwmxRegs.TZCTL
TZA
TZB
1 - 0
15 - 4
reserved
3 - 2
TZ1 to TZ6 Action on EPWMxB / EPWMxA
00 = high impedance
01 = force high
10 = force low
11 = do nothing (disable)

## Slide 47: ePWM Trip-Zone Select Register EPwmxRegs.TZSEL
OSHT1
OSHT5
OSHT4
OSHT3
OSHT2
8
OSHT6
15 - 14
reserved
9
10
11
12
13
CBC1
CBC5
CBC4
CBC3
CBC2
0
CBC6
7 - 6
reserved
1
2
3
4
5
Cycle-by-Cycle Trip Zone
(event cleared when CTR = 0;
i.e. cleared every PWM cycle)
0 = disable as trip source
1 = enable as trip source
One-Shot Trip Zone
(event only cleared under S/W
control; remains latched)
0 = disable as trip source
1 = enable as trip source

## Slide 48: ePWM Trip-Zone Enable Interrupt Register EPwmxRegs.TZEINT
OST
CBC
reserved
15 - 3
0
2
1
reserved
Cycle-by-Cycle
Interrupt Enable
0 = disable
1 = enable
One-Shot
Interrupt Enable
0 = disable
1 = enable

## Slide 49: Lab 7_8: Over Current Protection with Trip Zone Signals TZx
Trip Zone Signal TZ6 is connected to GPIO17, push – button PB1at Peripheral Explorer Board
Active Signal PB1 will force ePWM1A and ePWM1B to low
Use Lab7_5 as starting point
New registers in this lab:
  TZCTL: Trip Zone Control
  TZSEL: Trip Zone Select
  TZEINT: Trip Zone Enable Interrupt
  TZCLR: Trip Zone Clear Interrupt Flags
Objective:

## Slide 50: ePWM Event-Trigger Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Shadowed
Compare
Register
Shadowed
Period
Register
Clock
Prescaler
Shadowed
Compare
Register
CMPA . 15 - 0
CMPB . 15 - 0
TBCTR . 15 - 0
TBPRD . 15 - 0
TBCTL . 12 - 7
AQCTLB . 11 - 0
AQCTLA . 11 - 0
DBCTL . 4 - 0
PCCTL . 10 - 0
SYSCLKOUT
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Trip
Zone
TZSEL . 15 - 0
EPWMxA
EPWMxB
TZy

## Slide 51: ePWM Event-Trigger Interrupts and SOC
TBCTR
TBPRD








EPWMA
EPWMB
CMPB
CMPA
CTR = 0
CTR = PRD
CTRU = CMPA
CTRD = CMPA
CTRU = CMPB
CTRD = CMPB

## Slide 52: ePWM Event-Trigger Module Registers
Name Description Structure
ETSEL Event-Trigger Selection EPwmxRegs.ETSEL.all =
ETPS Event-Trigger Pre-Scale EPwmxRegs.ETPS.all =
ETFLG Event-Trigger Flag EPwmxRegs.ETFLG.all =
ETCLR Event-Trigger Clear EPwmxRegs.ETCLR.all =
ETFRC Event-Trigger Force EPwmxRegs.ETFRC.all =

## Slide 53: ePWM Event-Trigger Selection Register EPwmxRegs.ETSEL
15
11
7 - 4
2 - 0
INTEN
INTSEL
reserved
3
SOCBSEL
SOCASEL
SOCAEN
SOCBEN
10 - 8
14 - 12
Enable SOCB / A
0 = disable
1 = enable
EPWMxSOCB / A Select
000 = reserved
001 = CTR = 0
010 = CTR = PRD
011 = reserved
100 = CTRU = CMPA
101 = CTRD = CMPA
110 = CTRU = CMPB
111 = CTRD = CMPB
Enable EPWMxINT
0 = disable
1 = enable
EPWMxINT Select
000 = reserved
001 = CTR = 0
010 = CTR = PRD
011 = reserved
100 = CTRU = CMPA
101 = CTRD = CMPA
110 = CTRU = CMPB
111 = CTRD = CMPB

## Slide 54: ePWM Event-Trigger Prescale Register EPwmxRegs.ETPS
15 - 14
11 - 10
7 - 4
1 - 0
INTCNT
INTPRD
reserved
2 - 3
SOCBPRD
SOCAPRD
SOCACNT
SOCBCNT
9 - 8
13 - 12
EPWMxSOCB / A Counter
(number of events have occurred)
00 = no events
01 = 1 event
10 = 2 events
11 = 3 events
EPWMxSOCB / A Period
(number of events before SOC)
00 = disabled
01 = SOC on first event
10 = SOC on second event
11 = SOC on third event
EPWMxINT Counter
(number of events have occurred)
00 = no events
01 = 1 event
10 = 2 events
11 = 3 events
EPWMxINT Period
(number of events before INT)
00 = disabled
01 = INT on first event
10 = INT on second event
11 = INT on third event

## Slide 55: Lab 7_9: Sine Wave PWM signal at ePWM1A
Generate a sine wave modulated pulse sequence at ePWM1A
ePWM1A carrier frequency is 500 KHz
Sine wave frequency is 976 Hz
Objective:

## Slide 56: eCAP Block Diagram – Capture Mode
32-Bit
Time-Stamp
Counter
Capture 1
Register
Event
Prescale
Polarity
Select 1
Polarity
Select 2
Polarity
Select 3
Polarity
Select 4
Capture 2
Register
Capture 3
Register
Capture 4
Register
Event Logic
ECAPx
pin
SYSCLKOUT
TSCTR . 31 - 0
CAP1 . 31 - 0
CAP2 . 31 - 0
CAP3 . 31 - 0
CAP4 . 31 - 0
ECCTL . 13 - 9
ECCTL . 0
ECCTL . 2
ECCTL . 4
ECCTL . 6
CAP1POL
CAP2POL
CAP3POL
CAP4POL
PRESCALE

## Slide 57: Capture Units (eCAP)
The eCAP module timestamps transitions on a capture input pin
Timer
Timestamp
Values
Trigger
pin

## Slide 58: Some Uses for the Capture Units
Problem: At low speeds, calculation of speed based on a measured position change at fixed time intervals produces large estimate errors
Alternative: Estimate the speed using a measured time interval at fixed position intervals
Signal from one
quadrature
encoder channel
Low speed velocity estimation from incr. encoder:
Measure the time width of a pulse
vk 
x
tk - tk-1
vk 
t
xk - xk-1
x
Auxiliary PWM generation
Notes: <number>
LOW SPEED VELOCITY ESTIMATION
First box: Traditional way to estimate the velocity (using a QEP)
Second box: When you’re moving really slow you can’t use the above equation. The captures can allow you to estimate the velocity at low speeds.
Refer to App Note SPRA363 “USING THE CAPTURE UNITS FOR LOW SPEED VELOCITY ESTIMATION ON A TMS320C240” for more details

## Slide 59: eCAP Block Diagram – APWM Mode
32-Bit
Time-Stamp
Counter
Period
Register
(CAP3)
Period
Register
(CAP1)
Compare
Register
(CAP4)
Compare
Register
(CAP2)
PWM
Compare
Logic
ECAP
pin
Shadowed
Shadowed
SYSCLKOUT
TSCTR . 31 - 0
CAP1 . 31 - 0
CAP2 . 31 - 0
CAP3 . 31 - 0
CAP4 . 31 - 0
immediate
mode
shadow
mode
shadow
mode
immediate
mode

## Slide 60: eCAP Module Registers
Name Description Structure
ECCTL1 Capture Control 1 ECapxRegs.ECCTL1.all =
ECCTL2 Capture Control 2 ECapxRegs.ECCTL2.all =
TSCTR Time-Stamp Counter ECapxRegs.TSCTR =
CTRPHS Counter Phase Offset ECapxRegs.CTRPHS =
CAP1 Capture 1 ECapxRegs.CAP1 =
CAP2 Capture 2 ECapxRegs.CAP2 =
CAP3 Capture 3 ECapxRegs.CAP3 =
CAP4 Capture 4 ECapxRegs.CAP4 =
ECEINT Enable Interrupt ECapxRegs.ECEINT.all =
ECFLG Interrupt Flag ECapxRegs.ECFLG.all =
ECCLR Interrupt Clear ECapxRegs.ECCLR.all =
ECFRC Interrupt Force ECapxRegs.ECFRC.all =

## Slide 61: eCAP Control Register 1 ECapxRegs.ECCTL1
CAPLDEN
FREE_SOFT
PRESCALE
15 - 14
13 - 9
8
Upper Register:
Emulation Control
00 = TSCTR stops immediately
01 = TSCTR runs until equals 0
1X = free run (do not stop)
Event Filter Prescale Counter
00000 = divide by 1 (bypass)
00001 = divide by 2
00010 = divide by 4
00011 = divide by 6
00100 = divide by 8
11110 = divide by 60
11111 = divide by 62
CAP1 – 4 Load
on Capture Event
0 = disable
1 = enable

## Slide 62: eCAP Control Register 1 ECapxRegs.ECCTL1
Lower Register:
CTRRST4
CAP4POL
7
3
0
2
CTRRST3
CAP3POL
CTRRST2
CAP2POL
CTRRST1
CAP1POL
1
4
5
6
Counter Reset on Capture Event
0 = no reset (absolute time stamp mode)
1 = reset after capture (difference mode)
Capture Event Polarity
0 = trigger on rising edge
1 = trigger on falling edge

## Slide 63: eCAP Control Register 2 ECapxRegs.ECCTL2
Upper Register:
SWSYNC
APWMPOL
CAP_APWM
10
8
15 - 11
reserved
9
APWM Output Polarity
(valid only in APWM mode)
0 = active high output
1 = active low output
Capture / APWM mode
0 = capture mode
1 = APWM mode
Software Force
Counter Synchronization
0 = no effect
1 = TSCTR load of current
module and other modules
if SYNCO_SEL bits = 00

## Slide 64: eCAP Control Register 2 ECapxRegs.ECCTL2
Lower Register:
SYNCO_SEL
SYNCI_EN
7 - 6
3
0
2 - 1
TSCTRSTOP
REARM
STOP_WRAP
CONT_ONESHT
4
5
Sync-Out Select
00 = sync-in to sync-out
01 = CTR = PRD event
generates sync-out
1X = disable
Counter Sync-In
0 = disable
1 = enable
Time Stamp
Counter Stop
0 = stop
1 = run
Re-arm
(capture mode only)
0 = no effect
1 = arm sequence
Stop Value for One-Shot Mode/
Wrap Value for Continuous Mode
(capture mode only)
00 = stop/wrap after capture event 1
01 = stop/wrap after capture event 2
10 = stop/wrap after capture event 3
11 = stop/wrap after capture event 4
Continuous/One-Shot
(capture mode only)
0 = continuous mode
1 = one-shot mode

## Slide 65: eCAP Interrupt Enable Register ECapxRegs.ECEINT
CTR=CMP
CTR=PRD
7
3
0
2
CTROVF
CEVT4
CEVT3
CEVT2
CEVT1
1
4
5
6
reserved
15 - 8
reserved
0 = disable as interrupt source
1 = enable as interrupt source
CTR = CMP
Interrupt Enable
CTR = PRD
Interrupt Enable
CTR = Overflow
Interrupt Enable
Capture Event 3
Interrupt Enable
Capture Event 1
Interrupt Enable
Capture Event 4
Interrupt Enable
Capture Event 2
Interrupt Enable

## Slide 66: What is an Incremental Quadrature Encoder?
A digital (angular) position sensor
slots spaced  deg. apart
photo sensors spaced /4 deg. apart
light source (LED)
shaft rotation
Ch. A
Ch. B
Quadrature Output from Photo Sensors

/4
Incremental Optical Encoder

## Slide 67: How is Position Determined from Quadrature Signals?
Ch. A
Ch. B
(00)
(11)
(10)
(01)
(A,B) =
00
01
11
10
Quadrature Decoder
State Machine
increment
counter
decrement
counter
Position resolution is /4 degrees
Illegal Transitions; generate phase error interrupt

## Slide 68: eQEP Block Diagram
Quadrature
Decoder
EQEPxA/XCLK
EQEPxB/XDIR
EQEPxI
EQEPxS
Position/Counter
Compare
Quadrature
Capture
32-Bit Unit
Time-Base
QEP
Watchdog
SYSCLKOUT
Generate the direction and clock for the position counter in quadrature count mode
Generate a sync output and/or interrupt on a position compare match
Measure the elapsed time between the unit position events; used for low speed measurement
Generate periodic interrupts for velocity calculations
Monitors the quadrature clock to indicate proper operation of the motion control system
Quadrature -clock mode
Direction -count mode

## Slide 69: eQEP Connections
Ch. A
Ch. B
Index
Quadrature
Decoder
EQEPxA/XCLK
EQEPxB/XDIR
EQEPxI
EQEPxS
Position/Counter
Compare
Quadrature
Capture
32-Bit Unit
Time-Base
QEP
Watchdog
SYSCLKOUT
Strobe
from homing sensor