## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 12: Inter Integrated Circuit F2833x
32-Bit-Digital Signal Controller
TMS320F2833x

## Slide 2: Inter Integrated Circuit(I2C, IIC)
Philips I2C-bus specification compliant, version 2.1
Data transfer rate from 10 kbps up to 400 kbps
Each device can be considered as a Master or Slave
Master initiates data transfer and generates clock signal
Device addressed by Master is considered a Slave
Multi-Master mode supported
Standard Mode – send exactly n data values (specified in register)
Repeat Mode – keep sending data values (use software to initiate a stop or new start condition)
Serial Clock (SCL)
2833x
I2C
2nd - I2C
Controller
I2C
EPROM
TMP101
I2C
Pull-up
Resisters
VDD
Serial Data (SDA)
Notes: <number>

## Slide 3: I2C Block Diagram
TX FIFO
RX FIFO
I2CDXR
I2CDRR
I2CXSR
I2CRSR
Clock
Circuits
SDA
SCL

## Slide 4: I2C Clock Generation
÷
÷
SYSCLKOUT
IPSC
ICCL, ICCH
I2C – Clock Module
SCL (*)
I2C Module Clock
(*) SCL is output in master – mode only

## Slide 5: I2C Operating Modes
Operating Mode Description
Slave-receiver mode Module is a slave and receives data from a master
(all slaves begin in this mode)
Slave-transmitter mode Module is a slave and transmits data to a master
(can only be entered from slave-receiver mode)
Master-receiver mode Module is a master and receives data from a slave
(can only be entered from master-transmit mode)
Master-transmitter mode Module is a master and transmits to a slave
(all masters begin in this mode)

## Slide 6: I2C Data Validity

## Slide 7
I2C Serial Data Formats
S
Slave Address
R/W
ACK
Data
Data
ACK
ACK
P
1
7
1
1
n
1
n
1
1
7-Bit Addressing Format
S
11110AA
R/W
ACK
AAAAAAAA
Data
ACK
ACK
P
1
7
1
1
8
1
n
1
1
10-Bit Addressing Format
S
Data
ACK
Data
Data
ACK
ACK
P
1
n
1
n
1
n
1
1
Free Data Format
R/W = 0 – master writes data to addressed slave
R/W = 1 – master reads data from the slave
n = 1 to 8 bits
S = Start (high-to-low transition on SDA while SCL is high)
P = Stop (low-to-high transition on SDA while SCL is high)

## Slide 8: I2C Arbitration
Arbitration procedure invoked if two or more master-transmitters simultaneously start transmission
  Procedure uses data presented on serial data bus (SDA) by competing transmitters
  First master-transmitter which drives SDA high is overruled by another master-transmitter that drives SDA low
  Procedure gives priority to the data stream with the lowest binary value
1
0
1
0
0
1
0
1
1
0
0
1
0
1
SCL
SDA
Data from device #1
Data from device #2
Device #1 lost arbitration and switches to slave-receiver mode
Device #2 drives SDA

## Slide 9: I2C Interrupts
Interrupt Source | Description
XRDYINT | Transmit ready condition: The data transmit register (I2CDXR) is ready to accept new data because the previous data has been copied from I2CDXR to the transmit shift register (I2CXSR).
RRDYINT | Receive ready condition: The data receive register (I2CDRR) is ready to be red because data has been copied from the receive shift register (I2CRSR) to I2CDRR.
ARDYINT | Register-access ready condition: The I2C module registers are ready to be accessed because the previously programmed address, data, and command values have been used.
NACKINT | No-acknowledgment condition: The I2C module is configured as a master-transmitter and did not received acknowledgment from the slave-receiver.
ALINT | Arbitration-lost condition: The I2C module has lost an arbitration contest with another master-transmitter.
SCDINT | Stop condition detected: A STOP condition was detected on the I2C bus.
AASINT | Addressed as slave condition: The I2C has been addressed as a slave device by another master on the I2C bus.
I2CFIFO | see FIFO - Registers

## Slide 10: I2C Registers
Register Name | Description
I2COAR | I2C own address register
I2CIER | I2C interrupt enable register
I2CSTR | I2C status register
I2CCLKL | I2C clock low-time divide register
I2CCLKH | I2C clock high-time divide register
I2CCNT | I2C data count register
I2CDRR | I2C data receive register
I2CSAR | I2C slave address register
I2CDXR | I2C data transmit register
I2CMDR | I2C mode register
I2CISRC | I2C interrupt source register
I2CEMDR | I2C extended mode register
I2CPSC | I2C prescaler register
I2CFFTX | I2C FIFO transmit register
I2CFFRX | I2C FIFO receive register

## Slide 11: I2C Mode Register (I2CMDR) I2caRegs.I2CMDR
8
15
9
10
11
12
13
14
TRX
FREE
STP
STT
MST
NACKMOD
reserved
NACKMOD
(receiver mode only)
0 = I2C sends ACK
1 = I2C sends NACK
XA
FREE
0 = I2C stop on EMULCK
1 = no I2C stop on EMUL
STT
0 = no START
1 = generate a START
STP
0 = no STOP
1 = generate a STOP
MST
0 = Slave Mode
1 = Master Mode
TRX
0 = Receiver Mode
1 = Transmitter Mode
XA
0 = 7 Bit Address
1 = 10 Bit Address

## Slide 12: I2C Mode Register (I2CMDR) I2caRegs.I2CMDR
7
2 - 0
3
4
5
6
IRS
STB
FDF
BC
RM
RM
0 = no repeat mode
1 = repeat mode
DLB
DLB
0 = no loopback
1 = loopback mode
IRS
0 = I2C in RESET
1 = I2C enabled
STB
0 = no START byte mode
1 = START byte mode
FDF
0 = no free data format
1 = free data format
BC
0 = 8 bit per data
1 = 1 bit per data
2 = 2 bit per data
…
7 = 7 bit per data

## Slide 13: I2C Interrupt Enable Register I2caRegs.I2CIER
0
7
1
2
3
4
5
6
NACK
AAS
RRDY
SCD
ARDY
reserved
XRDY
AL
8
15
9
10
11
12
13
14
reserved
reserved
reserved
reserved
reserved
reserved
reserved
reserved
1 = enable interrupt source 0 = disable
AAS: an I2C - master has addressed the DSC as slave
SCD: Stop condition detected
XRDY: Transmit data ready for new data
RRDY: Receive data available
ARDY: I2C register access ready
NACK: No – Acknowledge received
AL: Arbitration lost during competition

## Slide 14: I2C Status Register I2caRegs.I2CSTR
0
7
1
2
3
4
5
6
NACK
reserved
RRDY
SCD
ARDY
reserved
XRDY
AL
8
15
9
10
11
12
13
14
AAS
SDIR
RSFULL
NACKSNT
XSMT
reserved
BB
AD0
SDIR: 1 = I2C is addressed as a slave transmitter; 0 = as receiver
NACKSNT: 1 = a NACK was sent as receiver from I2C
BB: 1 = Bus is busy, a START has been sent
RSFULL: 1 = Overrun of the receiver detected
XSMT: 0 = underflow of transmit shift register detected
AAS: 1 = I2C was addressed a s slave
AD0: 1 = a general call (address 0) has been detected
SCD: 1 = a STOP condition has been detected
XRDY: 1 = Transmit register I2CDXR ready for new data
RRDY: 1 = Receive data available in I2CDRR
ARDY: 1 = a previous cycle has completed
NACK: 0 = ACK received; 1 = NACK received
AL: 1 = Arbitration lost during competition by 2 masters

## Slide 15: I2C Interrupt Source Register I2caRegs.I2CISRC
2 - 0
15 - 3
INTCODE
reserved
INTCODE | Event
000 | None
001 | Arbitration lost
010 | No-acknowledgment
011 | Registers ready to be accessed
100 | Receive data ready
101 | Transmit data ready
110 | Stop condition detected
111 | Addressed as slave
Note: A CPU read of INTCODE will clear this field. If another lower priority interrupt is pending and enabled, the value corresponding to that interrupt will then be loaded. Otherwise, the value will stay cleared.

## Slide 16: I2C Clock Register I2caRegs.I2CPSC
7 - 0
15 - 8
IPSC
reserved
TI2C_MASTER_CLOCK = TI2C_MODULE_CLOCK * [ (ICCL +d ) + (ICCH + d ) ]
Note: should be 7…12 MHz
I2caRegs.I2CCLKL
0
15
ICCH
I2caRegs.I2CCLKH
0
15
ICCL
I2C module clock frequency = SYSCLKOUT / (IPSC + 1)

## Slide 17: I2C Master Clock
IPSC | Value for d
0 | 7
1 | 6
greater than 1 | 5
(A):

## Slide 18: I2C Slave Address Register I2caRegs.I2CSAR
9 - 0
15 - 10
SAR
reserved
SAR: next slave address that will be transmitted
  Bits 6…0 in 7 Bit - Address - Mode (XA = 0 in I2CMDR)
  Bits 9…0 in 10 Bit - Address _ Mode (XA = 1)

## Slide 19: I2C Own Address Register I2caRegs.I2COAR
9 - 0
15 - 10
OAR
reserved
OAR: F2833x address in case of slave mode
  Bits 6…0 in 7 Bit - Address - Mode (XA = 0 in I2CMDR)
  Bits 9…0 in 10 Bit - Address _ Mode (XA = 1)

## Slide 20: I2C Data Count Register I2caRegs.I2CCNT
0
15
ICDC
ICDC: Data Count Value
ICDC indicates the number of data bytes to transfer or receive.
0x0000: The start value loaded to the internal data counter is 65536.
00001-0xFFFF: The start value loaded to internal data counter is 1-65535.

## Slide 21: I2C Data Receive Register I2caRegs.I2CDRR
7 - 0
15 - 8
DATA
reserved
I2C Data Transmit Register I2caRegs.I2CDXR
7 - 0
15 - 8
DATA
reserved

## Slide 22: I2C Transmit FIFO Register I2caRegs.I2CFFTX
7
4 - 0
5
6
TXFFINTCLR
TXFFIENA
TXFFIL
TXFFINT
15
12 – 8
13
14
TXFFST
I2CFFEN
TXFFRST
reserved
I2CFFEN: 1 = enable TXFIFO - mode
TXFFRST: 0 = reset TXFIFO; 1 = enable TX – FIFO - operation
TXFFST: Filling level of TXFIFO (0 – 16 )
TXFFINT: TXFIFO Interrupt flag
1 = TX FIFO interrupt condition has occurred.
0 = TX FIFO interrupt condition has not occurred.
cleared by writing a 1 into bit TXFFINTCLR
TXFFINTCLR: 1 = clear flag TXFFINT
TXFFIENA: 1 = enabled. TXFFINT generates an interrupt when set.
TXFFIL: TX FIFO Interrupt level. If TXFFST is equal or less than
TXFFIL, the flag TXFFINT is set.

## Slide 23: I2C Receive FIFO Register I2caRegs.I2CFFRX
7
4 - 0
5
6
RXFFINTCLR
RXFFIENA
RXFFIL
RXFFINT
15
12 – 8
13
14
RXFFST
reserved
RXFFRST
reserved
RXFFRST: 0 = reset RXFIFO; 1 = enable RX – FIFO - operation
RXFFST: Filling level of RXFIFO (0 – 16 )
RXFFINT: RXFIFO Interrupt flag
1 = RX FIFO interrupt condition has occurred.
0 = RX FIFO interrupt condition has not occurred.
cleared by writing a 1 into bit RXFFINTCLR
RXFFINTCLR: 1 = clear flag RXFFINT
RXFFIENA: 1 = enabled. RXFFINT generates an interrupt when set.
RXFFIL: RX FIFO Interrupt level. If RTXFFST is equal or greater
than RXFFIL, the flag RXFFINT is set.

## Slide 24: I2C Summary
Compliance with Philips I2C-bus specification (version 2.1)
7-bit and 10-bit addressing modes
Configurable 1 to 8 bit data words
Data transfer rate from 10 kbps up to 400 kbps
Transmit FIFO and receive FIFO

## Slide 25: Temperature Sensor TMP101
Digital Interface: I2C Serial 2-Wire
Resolution: 9- to 12-Bits, User-Selectable
  9 – Bit: 0.5 °C; 12 – Bit:0.0625 °C
Accuracy:
  ±2.0°C from −25°C to +85°C (max)
  ±3.0°C from −55°C to +125°C (max)
Low quiescent current of 45μA, 0.1μA Standby
Power supply range: 2.7V to 5.5V
Tiny SOT23-6 package

## Slide 26: Temperature Sensor TMP100

## Slide 27: Temperature Sensor TMP100
00
10
01
11
Pointer:

## Slide 28: Temperature Sensor TMP100

## Slide 29: TMP100 Configuration Register
0
7
1
2
3
4
5
6
TM
R1
F0
R0
POL
OS/ALERT
F1
SD
OS/ALERT: write 1: single temperature conversion
write 0: continuous temperature conversion
read 1: temperature above THIGH
read 0: temperature below TLOW
R1, R0: Resolution 9 bit (0,0) … 12 bit (1,1)
F1,F0: activate ALERT after number of consecutive faults (1,2,4,6)
POL: Polarity of ALERT (0 or 1)
TM: write 0: Comparator Mode
(ALERT stays active as long as condition is true)
write 1: Interrupt Mode
( ALERT is cleared by a read instruction of any reg)
SD: write 1: shutdown
write 0: active mode

## Slide 30: TMP101 Write Timing

## Slide 31: TMP101 Read Timing