## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 17: IQ – Math library
32-Bit-Digital Signal Controller
TMS320F2833x

## Slide 2: Fractional Representation
S IIIIIIII
fffffffffffffffffffffff
0
31
32 bit mantissa
Advantage  Precision same for all numbers in an IQ format
Disadvantage  Limited dynamic range compared to floating point
-2I + 2I-1 + … + 21 + 20 . 2-1 + 2-2 + … + 2-Q
“IQ” – Format
“I”  INTEGER – Fraction
“Q”  QUOTIENT – Fraction

## Slide 3: IQ – Range and Resolution
4-bit number:
Format | Most Negative | Most Positive | Resolution (step size)
I1Q3 | 1.000 -1 | 0.111 +0.875 | 0.001 0.125
I2Q2 | 10.00 -2 | 01.11 +1.75 | 00.01 0.25
I3Q1 | 100.0 -4 | 011.1 +3.5 | 000.1 0.5
I4Q0 | 1000 -8 | 0111 +7 | 0001 1
Trade - Off between Range and Resolution
Note: Integer Format (I4Q0) is a subset of IQ-Math

## Slide 4: F28x Signal Processing Libraries
Signal Processing Libraries & Applications Software Literature #
ACI3-1: Control with Constant V/Hz SPRC194
ACI3-3: Sensored Indirect Flux Vector Control SPRC207
ACI3-3: Sensored Indirect Flux Vector Control (simulation) SPRC208
ACI3-4: Sensorless Direct Flux Vector Control SPRC195
ACI3-4: Sensorless Direct Flux Vector Control (simulation) SPRC209
PMSM3-1: Sensored Field Oriented Control using QEP SPRC210
PMSM3-2: Sensorless Field Oriented Control SPRC197
PMSM3-3: Sensored Field Oriented Control using Resolver SPRC211
PMSM3-4: Sensored Position Control using QEP SPRC212
BLDC3-1: Sensored Trapezoidal Control using Hall Sensors SPRC213
BLDC3-2: Sensorless Trapezoidal Drive SPRC196
DCMOTOR: Speed & Position Control using QEP without Index SPRC214
Digital Motor Control Library (F/C280x) SPRC215
Communications Driver Library SPRC183
DSP Fast Fourier Transform (FFT) Library SPRC081
DSP Filter Library SPRC082
DSP Fixed-Point Math Library SPRC085
DSP IQ Math Library SPRC087
DSP Signal Generator Library SPRC083
DSP Software Test Bench (STB) Library SPRC084
C28x FPU Fast RTS Library SPRC664
C2833x C/C++ Header Files and Peripheral Examples SPRC530
Available from TI Website  http://www.ti.com/c2000
Notes: We don’t have a lot of time in this section, so quickly point out the web address, and hit home this important location for their next step!!!
This shows them where to get additional info.
Highlight the DMC applications area, the designer notebook pages, and the development tools section.

## Slide 5: So how do we really use all this fraction stuff?
Takes many days/weeks to convert (one way process)
Fixed-Point Algorithm
(ASM, C, C++)
Fixed-Point DSP
Can be easily ported to floating-point device
Floating-Point DSP
Floating-Point
Algorithm
(C or C++)
Natural development starts with simulation in floating-point
Simulation
Platform
(i.e. MatLab)
The Fixed-Point Development Dilemma

## Slide 6: Traditional 16-bit “Q” Math Approach y = mx + b
s Q15
ss Q30
sssssssssssss Q15
s Q15
s Q15
s Q15
ss Q30
sI Q30
ssssssssssssI Q15
M
X
B
Y
<< 15
Align Binary
Point For Add
Y = ((i32) M * (i32) X + (i32) B << Q) >> Q;
in C:
>> 15
Align Binary
Point For Store

## Slide 7: Traditional 32-bit “Q” Math Approach y = mx + b
Y = ((i64) M * (i64) X + (i64) B << Q) >> Q;
in C:
Note: Requires support for 64-bit integer data type in compiler
<< 24
Align Decimal
Point for Add
I8 Q24
M
X
B
Y
I8 Q24
I8 Q24
I16 Q48
ssssssssssssssssssI8 Q24
ssssI8 Q48
I16 Q48
sssssssssssssssssI16 Q24
I8 Q24
>> 24
Align Decimal
Point for Store

## Slide 8: 32-bit IQmath Approach y = mx + b
I8 Q24
I16 Q48
M
X
B
Y
>> 24
Align Decimal
Point Of Multiply
I8 Q24
I8 Q24
sssssssssssssssssI16 Q24
I8 Q24
I8 Q24
Y = ((i64) M * (i64) X) >> Q + B;
in C:

## Slide 9: IQmath Approach Multiply Operation
Y = ((i64) M * (i64) X) >> Q + B;
_IQmpy(M,X) == ((i64) M * (i64) X) >> Q
Redefine the multiply operation as follows:
Y = _IQmpy(M,X) + B;
This simplifies the equation as follows:
MOVL XT,@M
IMPYL P,XT,@X ; P = low 32-bits of M*X
QMPYL ACC,XT,@X ; ACC = high 32-bits of M*X
LSL64 ACC:P,#(32-Q) ; ACC = ACC:P << 32-Q
; (same as P = ACC:P >> Q)
ADDL ACC,@B ; Add B
MOVL @Y,ACC ; Result = Y = _IQmpy(M*X) + B
; 7 Cycles
C28x compiler supports “_IQmpy” intrinsic; assembly code generated:

## Slide 10: IQmath Approach It looks like floating-point!
float Y, M, X, B;
Y = M * X + B;
Floating-Point
long Y, M, X, B;
Y = ((i64) M * (i64) X + (i64) B << Q)) >> Q;
Traditional
Fix-Point Q
_iq Y, M, X, B;
Y = _IQmpy(M, X) + B;
“IQmath”
In C
iq Y, M, X, B;
Y = M * X + B;
“IQmath”
In C++
“IQmath” code is easy to read!

## Slide 11: IQmath Approach GLOBAL_Q simplification
#define GLOBAL_Q 18 // set in “IQmathLib.h” file
_iq Y, M, X, B;
Y = _IQmpy(M,X) + B; // all values are in Q = 18
GLOBAL_Q
User selects “Global Q” value for the whole application
based on the required dynamic range or resolution, for example:
The user can also explicitly specify the Q value to use:
_iq20 Y, M, X, B;
Y = _IQ20mpy(M,X) + B; // all values are in Q = 20
0.000 000 06
-128.000 000 00
127.999 999 94
24
0.000 001
-2048.000 000
2047.999 999
20
0.000 000 004
-8.000 000 000
7.999 999 996
28
Resolution
Min Val
Max Val
GLOBAL_Q

## Slide 12: IQmath Provides Compatibility Between Floating-Point and Fixed-Point
All “IQmath” operations have an equivalent floating-point operation
Compile & Run
on Fixed-Point
F282xx
Y = _IQmpy(M, X) + B;
#if MATH_TYPE == IQ_MATH
#if MATH_TYPE == FLOAT_MATH
Y = (float)M * (float)X + (float)B;
1) Develop any mathematical function
2) Select math type in IQmathLib.h
3) Compiler automatically converts to:
Floating-Point Math Code
Fixed-Point Math Code
Compile & Run
on Floating-Point
F283xx *
* Can also compile floating-point code on any floating-point compiler (e.g., PC, Matlab, fixed-point w/ RTS lib, etc.)

## Slide 13: IQmath Library: Math & Trig Functions
Accuracy of functions/operations approx ~28 to ~31 bits
IQsin(A),IQcos(A)
IQsinPU(A),IQcosPU(A)
IQasin(A),IQacos(A)
IQatan(A),IQatan2(A,B)
IQatan2PU(A,B)
IQsqrt(A),IQisqrt(A)
IQmag(A,B)
IQexp(A)
_IQsin(A), _IQcos(A)
_IQsinPU(A), _IQcosPU(A)
_IQasin(A),_IQacos(A)
_IQatan(A), _IQatan2(A,B)
_IQatan2PU(A,B)
_IQsqrt(A), _IQisqrt(A)
_IQmag(A,B)
_IQexp(A)
sin(A),cos(A)
sin(A*2pi),cos(A*2pi)
asin(A),acos(A)
atan(A),atan2(A,B)
atan2(A,B)/2pi
sqrt(A),1/sqrt(A)
sqrt(A*A + B*B)
exp(A)
trig
and
power
functions
IQsat(A,Pos,Neg)
_IQsat(A,Pos,Neg)
if(A > Pos) A = Pos
if(A < Neg) A = Neg
saturation
A – B
A - B
A - B
substract
>, >=, <, <=, ==, |=, &&, ||
>, >=, <, <=, ==, |=, &&, ||
>, >=, <, <=, ==, |=, &&, ||
boolean
A + B
A + B
A + B
add
A / B
_IQdiv (A , B)
A / B
divide
A * B
_IQmpy(A , B)
A * B
multiply
A = IQ(1.2345)
A = _IQ(1.2345)
A = 1.2345
constant
iq A, B;
_iq A, B;
float A, B;
type
“IQmath” in C++
“IQmath” in C
Floating-Point
Operation

## Slide 14: IQmath Library: Conversion Functions
IQmath.lib > contains library of math functions
IQmathLib.h > C header file
IQmathCPP.h > C++ header file
atoIQ(char)
_atoIQ(char)
atof(char)
string to iq
IQtoQN(A)
_IQtoQN(A)
A
iq to qN
QNtoIQ(A)
_QNtoIQ(A)
A
qN to iq
IQmpyI32int(A,B)
_IQmpyI32int(A,B)
(long) (A * (float) B)
integer(iq*long)
IQmpyI32frac(A,B)
_IQmpyI32frac(A,B)
A - (long) (A * (float) B)
fraction(iq*long)
IQtoF(A)
_IQtoF(A)
A
IQ to float
IQmpyI32(A,B)
_IQmpyI32(A,B)
A * (float) B
iq = iq*long
IQfrac(A)
_IQfrac(A)
A – (long) A
fraction(iq)
IQint(A)
_IQint(A)
(long) A
integer(iq)
IQNtoIQ(A)
_IQNtoIQ(A)
A
iqN to iq
IQtoIQN(A)
_IQtoIQN(A)
A
iq to iqN
“IQmath” in C++
“IQmath” in C
Floating-Point
Operation
IQtoA(A,B,C)
_IQtoA(A,B,C)
sprintf(A,B,C)
IQ to ASCII

## Slide 15: AC Induction Motor Example One of the more complex motor control algorithms
Sensorless, ACI induction machine direct rotor flux control
Goal: motor speed estimation & alpha-axis stator current estimation

## Slide 16: AC Induction Motor Example Park Transform – floating-point C code
#include “math.h”
#define TWO_PI 6.28318530717959
void park_calc(PARK *v)
{
float cos_ang , sin_ang;
sin_ang = sin(TWO_PI * v->ang);
cos_ang = cos(TWO_PI * v->ang);
v->de = (v->ds * cos_ang) + (v->qs * sin_ang);
v->qe = (v->qs * cos_ang) - (v->ds * sin_ang);
}

## Slide 17: AC Induction Motor Example Park Transform - converting to “IQmath” C code
#include “math.h”
#define TWO_PI 6.28318530717959
void park_calc(PARK *v)
{
float cos_ang , sin_ang;
sin_ang = sin(TWO_PI * v->ang);
cos_ang = cos(TWO_PI * v->ang);
v->de = (v->ds * cos_ang) + (v->qs * sin_ang);
v->qe = (v->qs * cos_ang) - (v->ds * sin_ang);
}
#include “IQmathLib.h”
_IQ(6.28318530717959)
_iq
_IQsin(_IQmpy(TWO_PI , v->ang));
_IQcos(_IQmpy(TWO_PI , v->ang));
_IQmpy(v->ds , cos_ang) + _IQmpy(v->qs , sin_ang);
_IQmpy(v->qs , cos_ang) - _IQmpy(v->ds , sin_ang);

## Slide 18: AC Induction Motor Example GLOBAL_Q = 24, system stable
IQmath: speed
IQmath: current
Floating-Point: speed
Floating-Point: current

## Slide 19: What’s Happening Here? Equal Precision in the Computation Region
I8Q24 Fractions:
0
+
-
In the region where these particular computations occur, the precision of single-precision floating-point just happens to equal the precision of the I8Q24 format.
So, both produce similar results!
Floating-Point:
0
+
-
Same precision as I8Q24
Notes: We are using an I8Q24 format. For this particular system, the variable ranges happen to fall such that the precision of floating-point in that range is pretty much the same as the precision of I8Q24. Remember that both single-precision floating-point and IQmath are 32-bit math.
Now there is no doubt some difference in the floating-point and IQmath computations. But, those differences are too small to affect the AC induction motor system in this example.
As we’ll see next, changing the IQ format can dramatically change the results.

## Slide 20: AC Induction Motor Example GLOBAL_Q = 27, system unstable
IQmath: speed
IQmath: current

## Slide 21: AC Induction Motor Example GLOBAL_Q = 16, system unstable
IQmath: speed
IQmath: current

## Slide 22: AC Induction Motor Example Q stability range
The developer must pick the right GLOBAL_Q value!
Unstable
(not enough resolution, quantization problems)
Q18 to Q0
Stable
Q26 to Q19
Unstable
(not enough dynamic range)
Q31 to Q27
Stability Range
Q range

## Slide 23: AC Induction Motor Example Performance comparisons
Benchmark C28x C C28x C C28x C
floating-point floating-point IQmath
std. RTS lib fast RTS lib v1.4d
(150 MHz) (150 MHz) (150 MHz)
B1: ACI module cycles 401 401 625
B2: Feedforward control cycles 421 371 403
B3: Feedback control cycles 2336 792 1011
Total control cycles (B2+B3) 2757 1163 1414
% of available MHz used 36.8% 15.5% 18.9%
(20 kHz control loop)
Notes: C28x compiled on codegen tools v5.0.0, -g (debug enabled), -o3 (max. optimization)
fast RTS lib v1.0beta1
IQmath lib v1.4d

## Slide 24: IQmath Approach Summary
Seamless portability of code between fixed and floating-point devices
  User selects target math type in “IQmathLib.h” file
    #if MATH_TYPE == IQ_MATH
    #if MATH_TYPE == FLOAT_MATH
One source code set for simulation vs. target device
Numerical resolution adjustability based on application requirement
  Set in “IQmathLib.h” file
    #define GLOBAL_Q 18
  Explicitly specify Q value
    _iq20 X, Y, Z;
Numerical accuracy without sacrificing time and cycles
Rapid conversion/porting and implementation of algorithms
IQmath library is freeware - available from TI DSP website
http://www.ti.com/c2000
“IQmath” + fixed-point processor with 32-bit capabilities =

## Slide 25: Lab17: IQ – Math FIR - Filter
CPU copies
result to
buffer during
ADC ISR
ADC
RESULT0
ePWM2
connector
wire
ADCINA0
...
data
memory
pointer rewind
Display using CCS
FIR Filter
TB Counter
Compare
Action Qualifier
ePWM1
ePWM2 triggering ADC on period match using SOC A trigger every 20µs (50 kHz)

## Slide 26: Lab17: IQ – Math FIR - Filter
  Objective:
  Generate a symmetrical 2 kHz PWM signal with 25% duty cycle
  Measure the signal with ADC at a 50 kHz sample rate
  Store the ADC results in a circular result buffer
  Compute the ADC results in a digital finite impulse response (FIR) filter with low-pass characteristics. The Filter is calculated by IQ-Math functions
  Plot the graphs of the filtered and unfiltered signal with Code Composer Studios graph tool
  Compare the results

## Slide 27: MATLAB FDATOOL

## Slide 28: MATLAB FDATOOL
FIR – Lowpass; 4th –order
Corner Frequency: 300 Hz
Sampling Frequency: 50 kHz
Hamming - Window

## Slide 29: MATLAB FDATOOL