## Slide 1: Bioluminescence, fluorescence and fluorescent proteins

## Slide 2
Luminescence
Emission of light
without heat
Incandescence, which is light generated by high temperatures.

## Slide 3: Diversi tipi di LUMINESCENZA
TIPO
CHEMILUMINESCENZA
BIOLUMINESCENZA
FOTOLUMINESCENZA
(fluorescenza, fosforescenza)
ELETTROLUMINESCENZA
RADIOLUMINESCENZA
CAUSA
Reazione chimica
Reazione enzimatica
Assorbimento luce UV-vis
Corrente elettrica in gas ionizzato
Materiale radioattivo incorporato nel “fosforo”

## Slide 4: Diversi tipi di LUMINESCENZA
CHEMILUMINESCENZA
Reazione chimica

## Slide 5: Diversi tipi di LUMINESCENZA
TIPO
CHEMILUMINESCENZA
BIOLUMINESCENZA
FOTOLUMINESCENZA
(fluorescenza, fosforescenza)
ELETTROLUMINESCENZA
RADIOLUMINESCENZA
CAUSA
Reazione chimica
Reazione enzimatica
Assorbimento luce UV-vis
Corrente elettrica in gas ionizzato
Materiale radioattivo incorporato nel “fosforo”

## Slide 6
Bioluminescence
Makes its own light
Fireflies!
Luminescence
Dinoflagellates
Flashlight fish
Notes: One form of luminescence that most divers are familiar with is bioluminescence. This is when animals or plants have chemicals that they can mix together to make light. The source of energy for the light emission is the chemical reaction. An example of this is fireflies – they are able to glow on their own without us having to do anything.
Just about every diver who has dived at night knows that if you turn out your light and shake your body you will see small glowing sparks in the water. This comes from bioluminescence in dinoflagellates, single-celled organisms in the water column. Most people have the terminology confused, and when we talk about fluorescence many divers say that they have already seen it, but they are really confusing it with bioluminescence. You have never seen any corals light up on their own, because they are not bioluminescent, but many are fluorescent.

## Slide 7: Diversi tipi di LUMINESCENZA
TIPO
CHEMILUMINESCENZA
BIOLUMINESCENZA
FOTOLUMINESCENZA
(fluorescenza, fosforescenza)
ELETTROLUMINESCENZA
RADIOLUMINESCENZA
CAUSA
Reazione chimica
Reazione enzimatica
Assorbimento luce UV-vis
Corrente elettrica in gas ionizzato
Materiale radioattivo incorporato nel “fosforo”

## Slide 8
Fluorescence
Glows when you shine light on it
Glow stops when you turn off the light
Corals
Jellyfish
Luminescence
Notes: Fluorescence is one of two kinds of light emission that can happen when you shine the right light on something. The other is phosphorescence.

## Slide 9
Phosphorescence
Luminescence
Glows continues when you turn off the light
Glows when you shine light on it

## Slide 10: Fluorescence and phosphorescence
In phosphorescence the light is re-emitted over a longer time period
In fluorescence the light is immediately re-emitted
Fluorescence is
- the absorption of electromagnetic radiation (light) at one wavelength,
- its re-emission at another, longer wavelength

## Slide 11: Fluorescence
Energy gap

## Slide 12: Electromagnetic Spectrum
Absorb
at high energy
shorter wavelength higher energy
longer wavelength lower energy
Fluorescence
Emit
at low energy
Decreasing energy

## Slide 13: FLUORESCENZA
Emissione di radiazioni di una molecola che torna, da uno stato elettronico eccitato grazie all’assorbimento di luce, a quello fondamentale
L’emissione è spostata verso il rosso rispetto alla eccitazione
Parametri misurabili:
  Spettri di eccitazione ed emissione
  Intensità di fluorescenza
  Tempo di vita
  Polarizzazione

## Slide 14
Emission
Stage 2: Excited-State Lifetime
The excited state exists for a finite time (typically 1–10 nanoseconds)
Stage 1: Excitation
A photon of energy hνEX is supplied by an external source such as an incandescent lamp or a laser and absorbed by the fluorophore, creating an excited electronic singlet state (S1').
Stage 3: Fluorescence Emission
A photon of energy hνEM is emitted, returning the fluorophore to its ground state S0
Excitation

## Slide 16
Resa quantica
La resa quantica
La resa quantica rappresenta la frazione di molecole
de-eccitate per fluorescenza

## Slide 18: Diagramma di uno spettrofluorimetro
Sorgente
Monocromatore di eccitazione
Monocromatore di emissione
campione
Rivelatore
ex
ex
em
em

## Slide 20
Spettri in Soluzione
SPETTRO DI EMISSIONE
si fa una scansione del monocromatore di emissione
Si illumina il campione con luce a lunghezza d’onda costante

## Slide 22
Spettri in Soluzione
SPETTRO DI ECCITAZIONE
Si misura a lunghezza d’onda costante nel monocromatore di emissione
si fa una scansione del monocromatore di eccitazione

## Slide 25
Stokes Shift
495 nm
520 nm
Stokes Shift is 25 nm
Fluorescein
molecule
Fluorescence Intensity
Wavelength

## Slide 27: Fluorofori estrinseci
4’,6’ diamidino-2-fenilindolo

## Slide 29
Gel green

## Slide 30
EtBr
Gel green

## Slide 31: Fluorofori estrinseci
4’,6’ diamidino-2-fenilindolo

## Slide 32
Absorb light at one wavelength and emit light at a specific and longer wavelength

## Slide 33
DAPI (4',6-diamidino-2-phenylindole)
is a fluorescent stain that binds strongly to A-T rich regions in DNA.
It is used extensively in fluorescence microscopy.
As DAPI can pass through an intact cell membrane, it can be used to stain both live and fixed cells, though it passes through the membrane less efficiently in live cells and therefore the effectiveness of the stain is lower.
DAPI has
absorption maximum at a wavelength of 358 nm (ultraviolet)
- emission maximum is at 461 nm (blue).

## Slide 36: Fluorofori estrinseci
4’,6’ diamidino-2-fenilindolo

## Slide 37
Fluorescein
Texas red
Excitation (㎚) | Emission (㎚)
595 | 620
Excitation (㎚) | Emission (㎚)
498 | 517

## Slide 41: Fluorescence Microscopy
Major Function: Localization of specific cellular molecules – example proteins
Major Advantages:
  Sensitivity:“glow” against dark background
  Specificity: immunofluorescence
  Cells may be fixed or living
Fluorescent dyes or proteins (Flurochromes)
  flurochromes may be indirectly or directly associated with the cellular molecule
  Multiple flurochromes may be used simultaneously

## Slide 42
nucleus
MERGE
microtubules
centrosomes
Anti-tubulin MoAb
Goat anti-mouse-Rhodamine
Anti-pericentrin PoAb
Goat anti-mouse-FITC
DAPI

## Slide 43
Anti-vinculin MoAb
Goat anti-mouse-FITC
Rhodamine-Phalloidin
Stress Fibers
Focal Adhesions

## Slide 45
MitoTracker® probes for live cells
MitoTracker® probes are cationic dyes that are selectively sequestered by mitochondria in live cells because of their charge—like other mitochondrial dyes, they depend on the membrane potential for loading

## Slide 46
MitoTracker dyes are cationic fluorophores that accumulate electrophoretically into mitochondria in response to the highly negative mitochondrial membrane potential.
However, unlike rhodamine MitoTracker dyes possess a reactive chloromethyl group that forms a covalent bond with thiols on proteins and peptides, which traps MitoTracker dyes within mitochondria.
Two of the more popular probes are MitoTracker® Deep Red and MitoTracker® Green.

## Slide 47
CellLight® reagents for Golgi complex
Use CellLight® reagents when you want to label the Golgi complex in live cells to follow the dynamics of intracellular behavior.