## Slide 1
METODICHE DI IMMUNOCHIMICA
METODI IMMUNOCHIMICI
- ELISA (Enzyme-Linked Immunoassorbent Assay)
Western blot
Radioimmunotest
Immunoistochimica
Immunoprecipitazione
etc etc
IMMUNOCHIMICA
permette la determinazione quantitativa di molecole (es proteine) in fluidi, tessuti e omogenati

## Slide 3: METODI IMMUNOMETRICI
I metodi immunometrici, sfruttando le caratteristiche uniche di
Affinità - Avidità selettività – specificità
del legame antigene-anticorpo,
Permettono lo sviluppo di metodi altamente specifici per la quantificazione dell’analita, anche in matrici complesse.
Antigene
+
anticorpo
Complesso
antigene-anticorpo
quantificazione del
complesso antigene - anticorpo

## Slide 4
Antibody affinity is the strength of the reaction between
a single antigenic determinant and
a single BINDING site on the antibody.
It is the sum of the attractive and repulsive forces operating between the antigenic determinant and the combining site of the antibody as illustrated
Affinity

## Slide 5
Affinity Vs Avidity

## Slide 6
What is Binding Affinity?
Binding affinity is the strength of the binding interaction between
a single biomolecule (e.g. protein or DNA)
to its ligand/binding partner.
Binding affinity is typically measured and reported by the
equilibrium dissociation constant (KD)
which is used to evaluate and rank order strengths of bimolecular interactions.
K​D is the ratio of (koff)/(kon)
- the antibody dissociation rate (koff), how quickly it dissociates from its antigen
- the antibody association rate (kon) of the antibody, how quickly it binds to its antigen.
1/K​D = K​a is the ratio of (kon)/(koff)

## Slide 7
Ab
An
+
An-Ab
kon
koff
[An-Ab]eq
[An]eq
[Ab]eq
kon
koff
=
INTERACTION ANTIGEN-ANTIBODY
Ka is the equilibrium or affinity constant (generally expressed in L / mol)
it is independent of the concentration of Ag and Ab
it just depends
- the type of molecules
- from the medium
- the temperature
Ka =

## Slide 8
Small KD value = greater binding affinity of the ligand for its target.
larger KD value, = target molecule and ligand are attracted weakly to bind to one another.
What is the typical KD value for an antibody? What would one expect to be a good KD value?
Most antibodies have KD values in the low micromolar (10-6) to nanomolar (10-7 to 10-9) range.
High affinity antibodies generally considered to be in the low nanomolar range (10-9)
with very high affinity antibodies being in the picomolar (10-12) range.
K​D = (koff)/(kon)
(koff)= sec-1
(kon)= M-1 Sec-1
K​D= M
Ka=1/K​D

## Slide 9: Range of Biological Dissociation Constants
Un anticorpo adatto per lo sviluppo di metodi immunometrici deve avere una Ka = 109-1012 M-1
Ka è la costante di Affinità
espressa generalmente in L/mol
adrenocorticoid receptor 10-10
neuropeptide 10-9
trypsin 8 x 10-5
Lambda rep (monomer/dimer) 2 x 10-8
lambda rep (dimer/DNA) 1 x 10-10
1/ Ka = Kd costante di dissociazione all’equilibrio

## Slide 10
L’affinità dell’anticorpo per l’analita può essere determinata graficamente mediante diagramma di Scatchard (VALE X 1 MOLECOLA x 1 Ab).
Riprendendo l’equazione:
[An-Ab]eq
[An]eq
= Keq Abt - Keq [An-Ab]eq
SCATCHARD PLOT (I)
si definisce Abt = [Ab]eq + [An-Ab]eq (concentrazione totale di anticorpo). Riarrangiando l’equazione ed introducendo Abt si ottiene:
Keq =
[An-Ab]eq
[An]eq
[Ab]eq
ka
kd
=

## Slide 11
[An-Ab]eq
[An]eq
= Keq Abt - Keq [An-Ab]eq
Rappresentando [An-Ab]/[An] (rapporto tra analita legato ed analita libero, cioè bound/free)
rispetto ad [An-Ab] (bound) si ottiene un diagramma di Scatchard, dove
la pendenza è – Keq,
l’intercetta sull’asse x è Abt.
SCATCHARD PLOT (II)

## Slide 12
Rappresentando [An-Ab]/[An] (rapporto tra analita legato ed analita libero, cioè bound/free)
rispetto ad [An-Ab] (bound) si ottiene un diagramma di Scatchard, dove la pendenza è – Keq,
l’intercetta sull’asse x è Abt.

## Slide 13
Un anticorpo adatto per lo sviluppo di metodi immunometrici deve avere una Keq = 109-1012 M-1

## Slide 14
The KD values are determined by measuring the kon and koff rates of a specific antibody/antigen interaction and then using a ratio of these values to calculate the KD value

## Slide 15
Ab1
Ab2
Ab3
Ab4
Ab1
Ab2
Ab3
Ab4
K​D = (koff)/(kon)

## Slide 16
K​D = (koff)/(kon)
Ab1
Ab2
Ab3
Ab4

## Slide 18
Isothermal Titration Calorimetry (ITC)
Isothermal Titration Calorimetry (ITC) is a technique used in quantitative studies of a wide variety of biomolecular interactions.
https://www.malvernpanalytical.com/en/products/technology/microcalorimetry/isothermal-titration-calorimetry/
It works by directly measuring the heat
that is either released
or absorbed
during a biomolecular binding event.

## Slide 19
https://www.youtube.com/embed/o_IpWcWKNXI
- When binding occurs, heat is either absorbed or released
- this is measured by the sensitive calorimeter
- gradual titration of the ligand into the sample cell containing the biomolecule of interest.

## Slide 21
Octet BLI Technology and Application Overview
Notes: Hello everyone
I’m going to give a brief overview of Product marketing activities for the Allegro product range
NEXT SLIDE

## Slide 22: Biosensor Surface Chemistry
Optical layer
Two-dimensional binding surface
Biocompatible Matrix - minimizes non-specific binding
Uniform
Non-denaturing
|------ 600 mm ------|

## Slide 23
Analyte binding changes thickness of bio-layer, which is measured at detector
Optical layer reflects simple white light; second reflection from tip of biosensor, both reach detector

## Slide 25: ForteBio BLI Systems: Label-Free Protein Analysis
Cells
Bacteria
Virus
IgM
IgA
IgG, IgD, IgE
Antibody Fragments
Proteins
Peptides
Nucleotides (DNA)
Small Molecules
Atoms
200 nm
1000 nm
0.1 nm
1
1,000
100,000
1,000,000
75 nm
150
MW
Size
7 nm
1 nm
Bacteria
Virus
Antibody - Antigen
Receptor - Ligand
DNA - DNA
DNA - Protein
Antibody Fragment - Antigen
Antigen – Fusion Protein
Antibody - Peptide
Multiple Antibody Pairings
Antibody - Small Molecule
Protein - Small Molecule

## Slide 26: BLI Biosensor Types Available
Biosensor | Application
Antibody-Specific Capture | 
• Anti-Human IgG Fc Capture (AHC) | Human IgG Fc region, kinetic analysis
• Anti-Human IgG Fc Capture (AHQ) | Human IgG Fc region, quantitation
• Anti-Mouse Fc Capture (AMC) | Mouse IgG1, 2a & 2b Fc regions, kinetic analysis
• Anti-Mouse Fc Capture (AMQ) | Mouse IgG1, 2a & 2b Fc regions, quantitation
• Anti-Human Fab-CHI (FAB) | Fab-CH1 domains of human IgG
• Protein A (ProA) | Quantitation of various species IgG
• Protein G (ProG) | Quantitation of various species IgG
• Protein L (ProL) | Quantitation of IgG via kappa light chain
Affinity Tag Capture | 
• Streptavidin (SA) | Biotinylated ligands
• High Precision Streptavidin (SAX) | Biotinylated ligands (4% CV)
• Super Streptavidin (SSA) | Biotinylated ligands (high-density surface, small molecules)
• Anti-GST (GST) | GST-tagged recombinant proteins
• Anti-Penta HIS (HIS) | HIS-tagged recombinant proteins
• Anti-Penta HIS 2nd Gen (HIS2) | HIS-tagged recombinant proteins
• Ni-NTA (NTA) | HIS-tagged recombinant proteins
Immobilization | 
• Amine Reactive 2nd Gen (AR2G) | Covalent coupling to reactive amine groups
• Aminopropylsilane (APS) | Adsorption to hydrophobic moieties

## Slide 27: What ForteBio BLI Systems Provide
Kinetics
ka, kd, KD
Proteins, Abs
Peptides, oligos
Small molecules
Specificity
Function testing
Epitope binning
Rank ordering
Isotyping
Notes: What information does one gain from the Octet? The range is quite versatile – from kinetics data – information such as Ka, Kd and affinity constants for a wide range of molecules to Quantitation consisting of simple single step quantation assay up to more complex multi step assays such as Elisa. Another very valuable way the Octet can help you with your work is to gain specificity information about your molecules. By that I mean such things as functionality testing, epitope binning, ranking order, isotyping, competition assay and the list goes on.

## Slide 28: Biosensor regeneration

## Slide 29: ForteBio BLI Systems: Label-Free Protein Analysis
Definitive Kinetic Analysis
Analyze Unpurified Samples
Straightforward Operation
Fast Protein Quantitation

## Slide 30: ForteBio BLI Systems: Blitz
Needs only 4 µL of sample in drop holder.
Can use 250 µL in tube holder.

## Slide 31: Data Collection on the Blitz
All steps are prompted by the software

## Slide 32: ForteBio BLI Systems: Octet
One biosensor tray
One 96-well sample/reagent plate
8 simultaneous readings
One biosensor tray
Two 96-well or 384-well sample/reagent plates
16 simultaneous readings (Octet 384)
8, 16, 32, 48, or 96 simultaneous readings (Octet HTX)
Octet 96
Octet 384/HTX

## Slide 33: HTX Breakthrough Technology: User-Selectable Read Head
96 sensor – QK384 sensitivity
32 or 48 sensors – QK384 sensitivity
8 or 16 sensors – RED96/384 sensitivity
Notes: What sets the HTX apart?
“You don’t have to choose anymore” We can do it all, high resolution and accelerated workflow
Note. Competitors: Biacore, Proteon, Wasatch, etc. focus on either high resolution kinetics/affinity or throughput. Hydra provides both.

## Slide 34
To explore the variability in biosensor studies, 150 participants from 20 countries were given the same protein samples and asked to determine kinetic rate constants for the interaction.
Analytical Biochemistry Volume 386, Issue 2, 15 March 2009, Pages 194-216 Analytical Biochemistry
A global benchmark study using affinity-based biosensors

## Slide 35
To address these questions, a panel of ten high-affinity monoclonal antibodies was simultaneously evaluated for their binding kinetics against the same antigen on four biosensor platforms: