## Slide 1
Digital Signal Controller
TMS320F28335
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 2: Architecture
Notes: 1

## Slide 2
A(19-0)
D(31-0)
32x32 bit
Multiplier
Sectored
Flash
Program Bus
Data Bus
RAM
Boot
ROM
32-bit
Auxiliary
Registers
3
32-bit
Timers
Real-Time
JTAG
Emulation
CPU
Register Bus
R-M-W
Atomic
ALU
PIE Interrupt Manager
eQEP
12-bit ADC
Watchdog
CAN 2.0B
I2C
SCI
SPI
GPIO
ePWM
eCAP
FPU
McBSP
DMA
6 Ch.
XINTF
DMA Bus
F2833x Block Diagram

## Slide 3: F2833x CPU
32-bit fixed and floating point DSP ; 32 x 32 bit fixed-point MAC
Additional 32 x 32 bit hardware floating point unit
Dual 16 x 16 single-cycle fixed-point MAC (DMAC)
32-/64-bit saturation
Unique real-time debugging capabilities
3
32-bit
Timers
PIE Interrupt Manager
32x32 bit
Multiplier
32-bit
Auxiliary
Registers
CPU
Register Bus
R-M-W
Atomic
ALU
FPU
Program Bus
Data Read Bus
Data Write Bus
Real-Time
JTAG
Emulation

## Slide 4: F2833x Fixed Point Multiplier and ALU
XT (32) or T/TL
MULTIPLIER
32 x 32 or
Dual 16 x 16
P (32) or PH/PL
AH (16)
Data Bus
Data Bus
Program Bus
ALU (32)
32
32
32
32
32
AL (16)
32
32
•
16/32
8/16
Shift R/L (0-16)
ACC (32)
AH.MSB AH.LSB
AL.MSB AL.LSB
32
Shift R/L (0-16)
32
Shift R/L (0-16)
32
16
8/16/32

## Slide 5: F2833x Floating Point Unit FPU
ACC
P
XT
XAR0
XAR1
XAR2
XAR3
XAR4
XAR5
XAR6
XAR7
PC
RPC
DP
SP
ST0
ST1
IER
IFR
DBGIER
C28 Register Set
R0H
R1H
R2H
R3H
R5H
R6H
R7H
R4H
STF
FPU Register Set
RB
R0H – R7H And STF Are Shadowed For Fast Context Save And Restore
32-bit
8 FPU Result Registers
FPU Status
Repeat Block
32-bit
Accumulator, Product, Temporary and
8 Auxiliary
Registers
22-bit
Program Counter Return PC
16-bit
Data Page Pointer Stack Pointer
2 Status
Interrupt Enable
Interrupt Flag
Fixed Point
Floating Point

## Slide 6: F2833x Pointer, DP and Memory
XAR0
XAR1
XAR2
XAR3
XAR4
XAR5
XAR6
XAR7
ARAU
MUX
Data Memory
MUX
DP (16)
Data Bus
Program Bus
6 LSB
from IR
XARn  32-bits
ARn  16-bits
22
32

## Slide 7
Program-read Data Bus (32)
Data-write Address Bus (32)
Program Address Bus (22)
Execution
R-M-W
Atomic
ALU
Real-Time
JTAG
Emulation
Program
Decoder
PC
XAR0
to
XAR7
SP
DP
@X
ARAU
MPY32x32
XT
P
ACC
ALU
Registers
Debug
Register Bus / Result Bus
Data/Program-write Data Bus (32)
Data-read Address Bus (32)
Data-read Data Bus (32)
FPU
R0H
to
R7H
Program
Memory
Data
Memory
Peripherals
External
Interface
F2833x Internal Bus Structure
Notes: This is a top level architecture of the C28x. The instruction set example is used to introduce the architecture. Use the animation to tell the story. Here is an example how I would teach this slide:
The C28x was design to address the need of an effective uni-processor architecture that supports the needs describe in previous slides before. There are 4 major block to the architecture: Program block, Register block, Execution block, and Test & Emulation block. To introduce the data flow we shall take examples from the instruction set.
click - ADD: Here we show a stack relative addressing as a single source operand instruction with the Accumulator as the destination. As the students leading question as you introduce the architecture flow. Here is an example how I may use to teach:
-Q: How does the processor get this instruction? -A: Instruction fetch …, -Q: The instruction address is generate by...? -A: Program Counter …; -click: now talk about the animated flow. Instruction is fetch from the memory and interpreted by the decoder (some processor call this the Instruction Register IR). This is the brain of the processor which generates all the control signals through out the processor based on the instructions coming in.
-Q: After the instruction is decoded what does the CPU needs to get? -A: Data operand …; -click: There are several addressing methods which the programmers can specified for the CPU to use: stack relative, indirect, direct, immediate, and register addressing jut to name a few. We sill cover the addressing modes in details later. -click: what is important is the data flow comes back to the processor, the programmer can also specified the destination either to the register block or the execution block.
Although this is a Harvard architecture, the C environment see memory as a unified memory space with “functions and variables”. The Harvard architecture helps improve in performance. The large address space allow different physical spaces to map as a single unified logical space. (Instructor note: void using references to Program memory and Data memory in the traditional TI DSP. This helps us and the students to think easier in the C environment.
-click: The CPU also supports single cycle dual operand instruction. This requires 2 operands read simultaneously. The processor make use of the program and data buses to archive the high throughput. We will cover more in a later chapter. Internally the data flow back in forth between the Execution and Register blocks using the Register Bus. This tightly couple register block with execution block allow the C28x to be more flexible than the traditional DSP architecture. The multiple on chip buses allow the C28x to be superior than the traditional CISC and RISC architectures.
-click: The C28x also supports various atomic instructions which enable this processor to run a multitask OS efficiently in an embedded environment.
-click: In a complex embedded environment, real time debugging is becoming more important. The C28x is designed with hardware debugging capability built in. This debugger block non intrusively query all internal bus activities and selectively reports the CPU status via the JTAG interface.
Instructors note: This is an example how we can make use of questioning techniques to teach this slide. Hopefully this example would trigger how you could develop your method to teach this slide as well as all the slides the workshop.

## Slide 8
McBSP-A
McBSP-B
XINTF
Zone 0, 6, 7
DMA
6-channels
L4 SARAM
L5 SARAM
L6 SARAM
L7 SARAM
ADC
Result 0-15
Triggers
SEQ1INT / SEQ2INT
MXEVTA / MREVTA
MXEVTB / MREVTB
XINT1-7 / 13
TINT0 / 1 / 2
PIE
DINTCH1-6
PWM1
PWM2
PWM3
PWM4
PWM5
PWM6
SysCtrlRegs.MAPCNF.bit.MAPCNF
(re-maps PWM regs from PF1 to PF3)
F2833x Direct Memory Access

## Slide 9: F2833x Atomic Read/Modify/Write
Registers
ALU / MPY
LOAD
STORE
WRITE
READ
CPU
Mem
Atomic Instructions Benefits:
  Simpler programming
  Smaller, faster code
  Uninterruptible (Atomic)
  More efficient compiler
AND *XAR2,#1234h
2 words / 1 cycles
Atomic Read/Modify/Write
MOV AL,*XAR2
AND AL,#1234h
MOV *XAR2,AL
DINT
EINT
6 words / 6 cycles
Standard Load/Store
Notes: The slide’s purpose is to re-iterate the C28x flexibility architecture which supports the flexibility in the instruction set. It also high light the compact code using the C28x Atomic type instructions.

## Slide 10: F2833x Pipeline
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
Protected Pipeline
  Order of results are as written in source code
  Programmer need not worry about the pipeline
8-stage pipeline
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
F1 F2 D1 D2 R1 R2 E
A
B
C
D
E
F
G
W
W
W
W
W
W
W
W
E & G Access
same address
R1 R2 E W
D2 R1 R2 E W
F1: Instruction Address
F2: Instruction Content
D1: Decode Instruction
D2: Resolve Operand Addr
R1: Operand Address
R2: Get Operand
E: CPU doing “real” work
W: store content to memory
H
Instructions
‘E’ and ‘G’
access same
memory address
Notes: Show the C28x pipe is deeper by breaking into smaller stages. Show how these smaller stages helps speed up the processor throughput. Then show how the protected pipe automatically resolve pipeline conflict. This is how I may teach this slide:
-click: -Q: What phase in the pipeline does the CPU doing the intended work? -A: The “real” intended work done by CPU is in the execution phase. This is when the data flows through the execution “math” channel. Its limitation is the speed of light, how fast can electrons charged move through the silicon. The speed of light is the upper limit that the CPU throughput can archive. The memory devices are slower than the CPU execution speed. Thus the faster the architecture can constantly provide data to the execution phase, the faster the throughput, hence the faster the device.
-click: Looking at the C28x pipeline, all the F, D, R phases are overhead - what it takes to get the data to the execution phase. If one of these phases is slow, the CPU throughput is limited by the slowest pipeline phase. Breaking these phases into smaller function allows them to keep up with the execution phase speed. Thus improve the pipeline efficiency.
-Q: what happen to write phase? Which hardware resources does write phase uses? -A: write data bus: -click: In general most write are hidden from the pipeline delay as long as there is no immediate read from the written address. Write hold off until there is a free cycle in the operand memory read phase. This is when there is an instruction operates on only registers. Data memory bus is free to perform a write. Multiple write can be queue up in a 3 deep FIFO.
-click: -Q: what happen when read to the same address of a queue up write? -A: Pipeline automatically stalled so the operand order are preserved. -click: The main point in the pipeline stall is the software does not need to manage the pipeline. A protected pipeline make ease of programming use, debugging, and maintaining.

## Slide 11
XINTF Zone 6 (1Mw)
XINTF Zone 7 (1Mw)
0x000000
0x000400
0x000800
M1 SARAM (1Kw)
M0 SARAM (1Kw)
Data Program
PIE Vectors
(256 w)
PF 0 (6Kw)
XINTF Zone 0 (4Kw)
reserved
PF 1 (4Kw)
PF 2 (4Kw)
PF 3 (4Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
L4 SARAM (4Kw)
L5 SARAM (4Kw)
L6 SARAM (4Kw)
L7 SARAM (4Kw)
reserved
0x000D00
0x002000
0x006000
0x007000
0x008000
0x009000
0x00A000
0x00C000
0x000E00
0x005000
0x00B000
0x00D000
0x00E000
0x00F000
0x004000
0x010000
0x010000
0x100000
0x200000
reserved
Data Program
FLASH (256Kw)
0x300000
0x33FFF8
0x340000
PASSWORDS (8w)
reserved
User OTP (1Kw)
0x380800
ADC calibration data
0x380080
0x380090
reserved
0x380400
reserved
0x3F8000
Boot ROM (8Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
reserved
0x3F9000
0x3FA000
0x3FB000
0x3FC000
0x3FE000
0x3FFFFF
DMA Accessible:
L4, L5, L6, L7,
XINTF Zone 0, 6, 7
Dual Mapped:
L0, L1, L2, L3
CSM Protected:
L0, L1, L2, L3,
FLASH, ADC CAL,
OTP
0x3FFFC0
BROM Vectors (64w)
TMS320F2833x Memory Map

## Slide 12: Code Security Module
Prevents reverse engineering and protects valuable intellectual property
128-bit user defined password is stored in Flash
128-bits = 2128 = 3.4 x 1038 possible passwords
To try 1 password every 2 cycles at 150 MHz, it would take at least 1.4 x 1023 years to try all possible combinations!
CSM Protected:
L0, L1, L2, L3,
FLASH, ADC CAL,
OTP

## Slide 13: F2833x Fast Interrupt Response Manager
96 dedicated PIE vectors
No software decision making required
Direct access to RAM vectors
Auto flags update
Concurrent auto context save
28x CPU Interrupt logic
28x
CPU
INTM
IFR
IER
96
Peripheral Interrupts 12x8 = 96
12 interrupts
INT1 to INT12
PIE
Register
Map
PIE module For 96 interrupts
T ST0
AH AL
PH PL
AR1 (L) AR0 (L)
DP ST1
DBSTAT IER
PC(msw) PC(lsw)
Auto Context Save
Notes: We make claim that this enable faster interrupt response. We want to introduce this notion in chapter 1. Rather than making claim with out reasoning to back up the claim, I have decide to show some technical detail on mechanism that supports this claim. Here is how I would teach this slide:
We will have a chapter dedicated to understanding the interrupts structure. The intention of this slide is to give you a quick glimpse into what is available that supports a faster interrupt response.
-Q: When you get an interrupt, how quickly do you want to response? How much jitter, and how much response delayed can you tolerate?
-A: It depends on what kind of interrupt.
-click: The CPU supports 256 vector locations allowing multiple interrupts vectors to be directly services without a software look up table. The intention is to allow quickly service the interrupts without software overhead and time delay via branch instructions.
-Q: When the interrupt is serviced, software or hardware manages the flags and context saved & restored? Can these be done with no performance degradation?
-A: ….
-click: Along with minimizing software overhead, the CPU also automatically manages the flags and context saved while the interrupt ISR instruction filling up the pipeline. We will go into the interrupt structure and its hardware assisted support in a later chapter.

## Slide 14: F2833x Operating Modes
C28x Native Mode 1 0
C24x Compatible Mode 1 1
Test Mode (default) 0 0
Reserved 0 1
OBJMODE AMODE
Mode Bits
Compiler Option
Mode Type
Almost all uses will run in C28x Native Mode
The bootloader will automatically select C28x Native Mode after reset
C24x compatible mode is mostly for backwards compatibility with an older processor family
-v28 –m20
-v28
Notes: 1.1.1 Compatibility with other Fixed-Point TMS320 Cores:
The C28x DSP features compatibility modes that minimize the migration effort from the C27x and C2xLP cores. The operating mode of the device is determined by a combination of the OBJMODE and AMODE bits in status register 1 (ST1) as shown in Table 1-1. The OBJMODE bit allows you to select between code compiled for a C28x (OBJMODE == 1) and code compiled for a C27x (OBJMODE == 0). The AMODE bit allows you to select between C28x/C27x instruction addressing modes (AMODE == 0) and C2xLP compatible instruction addressing modes (AMODE == 1).
OBJMODE AMODE
C28x Mode 1 0
C2xLP Source-Compatible Mode 1 1
C27x Object-Compatible Mode+ 0 0
+ The C28x is in C27x compatible mode at reset.
* C28x Mode: In C28x mode you can take advantage of all the C28x native features, addressing modes and instructions. To operate in C28x mode from reset, your code must first set the OBJMODE bit by using the "C28OBJ" (or "SETC OBJMODE") instruction. This book assumes you are operating in C28x mode unless stated otherwise.
* C2xLP Source-Compatible Mode: C2xLP source-compatible mode allows you to run C2xLP source code which has been reassembled using the C28x code generation tools. For more information on operating in this mode and migration from a C2xLP core, refer to Appendices C, D and E.
* C27x Object-Compatible Mode: At reset, the C28x core operates in C27x object-compatible mode. In this mode, the C28x is 100% object-code and cycle-count compatible with the C27x core. For detailed information on operating in C27x object-compatible mode and migrating from the C27x, see Appendix F.
1.1.2 Switching to C28x Mode From Reset
At reset, the C28x core is in C27x Object-Compatible Mode (OBJMODE == 0, AMODE == 0) and is 100% compatible with the C27x core. To take advantage of the enhanced C28x instruction set, you must instead operate the device in C28x mode. To do this, after a reset your code must first set the OBJMODE bit in ST1 by using the "C28OBJ" (or "SETC OBJMODE") instruction.

## Slide 15: Reset – Bootloader
Reset
OBJMODE = 0 AMODE = 0
ENPIE = 0 INTM = 1
Boot determined by state of GPIO pins
Reset vector fetched from boot ROM
0x3F FFC0
Execution
Entry Point
M0 SARAM
Note:
Details of the various boot options will be discussed in the Reset and Interrupts module
Bootloader sets
OBJMODE = 1
AMODE = 0

## Slide 16
High performance 32-bit DSP
32x32 bit or dual 16x16 bit MAC
IEEE single-precision floating point unit
Atomic read-modify-write instructions
Fast interrupt response manager
256Kw on-chip flash memory
Code security module (CSM)
Control peripherals
12-bit ADC module
Up to 88 shared GPIO pins
Watchdog timer
DMA and external memory interface
Communications peripherals
Highlights of the F2833x