## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 9: Serial Communication Interface
32-Bit-Digital Signal Controller
TMS320F2833x

## Slide 2: SCI Pin Connections
Transmitter-data
buffer register
Transmitter
shift register
SCI Device #1
SCIRXD
SCITXD
SCITXD
SCIRXD
SCI Device #2
8
Receiver-data
buffer register
Receiver
shift register
8
Transmitter-data
buffer register
Transmitter
shift register
8
Receiver-data
buffer register
Receiver
shift register
8
(Full Duplex Shown)
RX FIFO_0
RX FIFO_15
RX FIFO_0
RX FIFO_15
TX FIFO_0
TX FIFO_15
TX FIFO_0
TX FIFO_15

## Slide 3: SCI Data Format
This bit present only in Address-bit mode
NRZ (non-return to zero) format
Start
LSB
2
3
4
5
6
7
MSB
Addr/
Data
Parity
Stop 1
Stop 2
Communications Control Register (ScixRegs.SCICCR)
0 = 1 Stop bit
1 = 2 Stop bits
0 = Odd
1 = Even
0 = Disabled
1 = Enabled
0 = Disabled
1 = Enabled
0 = Idle-line mode
1 = Addr-bit mode
# of data bits = (binary + 1)
e.g. 110b gives 7 data bits
Stop
Bits
Even/Odd
Parity
Parity
Enable
Loopback
Enable
Addr/Idle
Mode
SCI
Char2
SCI
Char1
SCI
Char0
7
6
5
4
3
2
1
0
Notes: <number>

## Slide 4: SCI Data Timing
Start Bit
LSB of Data
Majority
Vote
Falling Edge Detected
Start bit valid if 4 consecutive SCICLK periods of zero bits after falling edge
Majority vote taken on 4th, 5th, and 6th SCICLK cycles
SCIRXD
SCICLK
(Internal)
1 2 3 4 5 6 7 8 1 2 3 4 5 6 7 8 1 2
Note: 8 SCICLK periods per data bit

## Slide 5: Multiprocessor Wake-Up Modes
Allows numerous processors to be hooked up to the bus, but transmission occurs between only two of them
Idle-line or Address-bit modes
Sequence of Operation
  1. Potential receivers set SLEEP = 1, which disables RXINT except when an address frame is received
  2. All transmissions begin with an address frame
  3. Incoming address frame temporarily wakes up all SCIs on bus
  4. CPUs compare incoming SCI address to their SCI address
  5. Process following data frames only if address matches

## Slide 6: Idle-Line Wake-Up Mode
Idle time separates blocks of frames
Receiver wakes up with falling edge after SCIRXD was high for 10 or more bit periods
Two transmit address methods
  deliberate software delay of 10 or more bits
  set TXWAKE bit to automatically leave exactly 11 idle bits
Last Data
ST
SP
ST
Data
SCIRXD/
SCITXD
Block of Frames
SP
SP
Last Data
ST
Addr
SP
Idle
Period
10 bits
or greater
Idle
Period
10 bits
or greater
Address frame
follows 10 bit
or greater idle
1st data frame
SP
ST
Addr
Idle periods
of less than
10 bits

## Slide 7: Address-Bit Wake-Up Mode
All frames contain an extra address bit
Receiver wakes up when address bit detected
Automatic setting of Addr/Data bit in frame by setting TXWAKE = 1 prior to writing address to SCITXBUF
Last Data
ST
ST
Data
SCIRXD/
SCITXD
Block of Frames
SP
SP
Last Data
ST
Addr
SP
Idle Period
length of no
significance
First frame within
block is Address.
ADDR/DATA
bit set to 1
1st data frame
0
1
0
0
SP
ST
Addr
1
SP
no additional
idle bits needed
beyond stop bits

## Slide 8: SCI Summary
Asynchronous communications format
65,000+ different programmable baud rates
Two wake-up multiprocessor modes
  Idle-line wake-up & Address-bit wake-up
Programmable data word format
  1 to 8 bit data word length
  1 or 2 stop bits
  even/odd/no parity
Error Detection Flags
  Parity error; Framing error; Overrun error; Break detection
FIFO-buffered transmit and receive
Individual interrupts for transmit and receive
28335 include channel SCI-A and SCI-B
Notes: <number>

## Slide 9: SCI – A Register Set
Address Register Name
0x007050 SCICCR SCI-A communication control register
0x007051 SCICTL1 SCI-A control register 1
0x007052 SCIHBAUD SCI-A baud register, high byte
0x007053 SCILBAUD SCI-A baud register, low byte
0x007054 SCICTL2 SCI-A control register 2 register
0x007055 SCIRXST SCI-A receive status register
0x007056 SCIRXEMU SCI-A receive emulation data buffer
0x007057 SCIRXBUF SCI-A receive data buffer register
0x007059 SCITXBUF SCI-A transmit data buffer register
0x00705A SCIFFTX SCI-A FIFO transmit register
0x00705B SCIFFRX SCI-A FIFO receive register
0x00705C SCIFFCT SCI-A FIFO control register
0x00705F SCIPRI SCI-A priority control register
Note: Interface SCI – B Register Address space is 0x007750…0x00775F

## Slide 10: SCI-A Communication Control Register
ADDR/IDLE
MODE
STOP
BITS
EVEN/ODD
PARITY
PARITY
ENABLE
LOOP BACK
ENABLE
SCI
CHAR2
SCI
CHAR1
SCI
CHAR0
Communications Control Register (SCICCR) – 0x007050
0 = 1 Stop bit
1 = 2 Stop bits
0 = Odd
1 = Even
0 = Disabled
1 = Enabled
0 = Disabled
1 = Enabled
0 = Idle-line mode
1 = Addr-bit mode
7
6
5
4
3
2
1
0
# of data bits = (binary + 1)
e.g. 110b gives 7 data bits

## Slide 11: SCI-A Control Register 1
TXWAKE
reserved
RX ERR
INT ENA
SW
RESET
reserved
SLEEP
TXENA
RXENA
Control Register 1 (SCICTL1) – 0x007051
0 = Receive Error Interrupt disabled
1 = Receive Error Interrupt enabled
Write 0 = Reset SCI
Write 1 = release from Reset
Transmitter wakeup method select
1 = wakeup mode depends on SCICCR.3
0 = no wakeup mode
7
6
5
4
3
2
1
0
0 = sleep mode disabled
1 = sleep mode enabled
0 = transmitter disabled
1 = transmitter enabled
0 = receiver disabled
1 = receiver enabled

## Slide 12: SCI-A Baud Rate
BAUD15
(MSB)
BAUD14
Baud-Select MSbyte Register (SCIHBAUD) – 0x007052
7
6
5
4
3
2
1
0
BAUD13
BAUD12
BAUD11
BAUD10
BAUD9
BAUD8
BAUD6
Baud-Select LSbyte Register (SCILBAUD) – 0x007053
7
6
5
4
3
2
1
0
BAUD5
BAUD4
BAUD3
BAUD2
BAUD1
BAUD7
BAUD0
(LSB)
SCI baud rate =
LSPCLK
(BRR + 1) x 8
LSPCLK
16
, BRR = 1 to 65535
, BRR = 0

## Slide 13: SCI-A Control Register 2 SCICTL2 @ 0x007054
TXRDY
TX
EMPTY
RX/BK
INT ENA
0
TX
INT ENA
1
7
6
5 - 2
reserved
SCI TX READY
0 = SCITXBUF is full
1 = SCITXBUF is empty
SCI TX EMPTY
0 = TXBUF or shift register are loaded with data
1 = Transmit buffer and shift register both empty
reserved
15 - 8
SCI TX INT ENA
0 = Disable TXRDY interrupt
1 = Enable TXRDY interrupt
SCI RX/BK INT ENA
0 = Disable RXRDY/BRKDT interrupt
1 = Enable RXRDY/BRKDT interrupt

## Slide 14: SCI-A Receiver Status Register SCIRXST @ 0x007055
OE
RX
ERROR
RXRDY
BRKDT
FE
PE
RXWAKE
reserved
0 = No error flags set
1 = Error flag(s) set
0 = no new character in SCIRXBUF
1 = new character in SCIRXBUF
1 = Break condition occurred
0 = no break condition
7
6
5
4
3
2
1
0
1 = Framing Error detected
1 = Overrun Error detected
1 = Parity Error detected
1 = Receiver wakeup condition detected
Notes: <number>

## Slide 15: SCI-A FIFO Transmit Register SCIFFTX @ 0x00705A
0
TXFFIL2
SCIFFENA
TXFFST0
TXFFST3
TXFFIENA
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
TXFFIL0
TXFFIL1
TXFFIL4
TXFFIL3
TXFFST1
TXFFINT
CLR
TXFFST2
TXFFINT
TXFFST4
TXFIFO
RESET
SCIRST
TX FIFO Status (read-only)
00000 TX FIFO empty
00001 TX FIFO has 1 word
00010 TX FIFO has 2 words
00011 TX FIFO has 3 words
10000 TX FIFO has 16 words
.
.
.
.
.
.
.
.
.
TX FIFO Interrupt Level
Interrupt when TXFFST4-0
and TXFFIL4-0 match
SCI FIFO
Enhancements
0 = disable
1 = enable
TX FIFO Reset
0 = reset (pointer to 0)
1 = enable operation
TX FIFO
Interrupt
(on match)
Enable
0 = disable
1 = enable
TX FIFO
Interrupt
Flag (read-only)
0 = not occurred
1 = occurred
TX FIFO
Interrupt
Flag Clear
0 = no effect
1 = clear
SCI Reset
0 = reset
1 = enable operation

## Slide 16: SCI-A FIFO Receive Register SCIFFRX @ 0x00705B
0
RXFFIL2
RXFF-
OVF CLR
RXFFST0
RXFFST3
RXFFIEN
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
RXFFIL0
RXFFIL1
RXFFIL4
RXFFIL3
RXFFST1
RXFFINT
CLR
RXFFST2
RXFFINT
RXFFST4
RXFIFO
RESET
RXFF-
OVF
RX FIFO Status (read-only)
00000 RX FIFO empty
00001 RX FIFO has 1 word
00010 RX FIFO has 2 words
00011 RX FIFO has 3 words
10000 RX FIFO has 16 words
.
.
.
.
.
.
.
.
.
RX FIFO Interrupt Level
Interrupt when RXFFST4-0
and RXFFIL4-0 match
RX FIFO Reset
0 = reset (pointer to 0)
1 = enable operation
RX FIFO
Interrupt
(on match)
Enable
0 = disable
1 = enable
RX FIFO
Interrupt
Flag (read-only)
0 = not occurred
1 = occurred
RX FIFO
Interrupt
Flag Clear
0 = no effect
1 = clear
RX FIFO
Overflow
Flag (read-only)
0 = no overflow
1 = overflow
RX FIFO
Overflow
Flag Clear
0 = no effect
1 = clear

## Slide 17: SCI-A FIFO Control Register SCIFFCT @ 0x00705C
0
ABD
CLR
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
CDC
ABD
FFTXDLY
Time delay between every transfer from FIFO
to transmit shift register
in number of SCI baud clock cycles
( 0 to 255 )
CDC calibrate ‘A’
0 = disabled auto-baud alignment
1 = enables auto-baud alignment
Auto Baud
detection
Flag (read-only)
0 = not complete
1 = complete
Auto Baud
detection
Flag Clear
0 = no effect
1 = clear
reserved

## Slide 18
SCI Example 9_1: transmit a text - message
Lab 9_1: Basic SCI Communication
Send a single line text message from F28335 to a PC’s COM-port.
Connect the RS232 – Connector (J12) of the Peripheral Explorer Board with a standard DB9 - cable (1:1) to a serial COM –port of the PC.
Periodic transmission of the message every 2 seconds.
No SCI interrupt services in this lab.
After transmission of the first character we just poll the transmission ready flag (TXEMPTY) before loading the next character into the transmit buffer - and wait again.
A Windows Terminal program is used as the counterpart from the PC’s-side and must be initialized properly for correct function(9,600 bit/s, odd Parity, no protocol).

## Slide 19
More SCI Examples
Lab 9_2: SCI Transmit
  SCI – TX interrupt service
  CPU Timer 0 interrupt service
Lab 9_3: SCI FIFO Transmit Interrupt
  TX FIFO Interrupt Service to send 16 characters
Lab 9_4: SCI Transmit and Receive
  TX and RX FIFO Interrupt services
  F28335 to wait for “Texas” and answer with “Instruments”