## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 11: Controller Area Network F2833x
32-Bit-Digital Signal Controller
TMS320F2833x

## Slide 2: Controller Area Network (CAN)
developed by Robert Bosch GmbH, Germany in 1987
Products available from all microcontroller manufacturers
International Standards: ISO11898 (Europe), SAE J2284 (US) for “high – speed” CAN; ISO 11519-2 for “fault-tolerant low speed” CAN
backbone serial bus system for automotive applications, but also used in industrial automation & control
Event triggered Serial Bus System; Self-Synchronisation
More Features :
    multi master bus access
    random access with collision avoidance (CSMA / CA )
    short message length , at max. 8 Bytes per message
    data rates 100KBPS to 1MBPS
    short bus length, physical length depends on data rate
    self-synchronised bit coding technology
    Robust EMC - behaviour
    build in fault tolerance
Notes: <number>

## Slide 3: Electronic Control Units
Examples for Microcontrollers used in car:
Antilock Break System - ABS ( 1 + 4)
Keyless Entry System(1)
Active Wheel Drive Control (4)
Engine Control (2)
Airbag Sensor Systems (6+) Seat occupation sensors(4)
Automatic Gearbox(1) Electronic Park Brake(1)
diagnostic computer(1)
driver display unit(1)
air conditioning system(1)
    adaptive cruise control(1)
radio / CD-player(2)
collision warning radar(2)
rain/ice/snow sensor systems (1) each)
dynamic drive control(4)
active damping system (4)
driver information system(1)
GPS navigation system(3)
Notes: <number>

## Slide 4: Why a car network like CAN?
 Requirements of an in car network:
  low cost solution
  good and high performance with few overhead transmission
  high volume production
  high reliability and electromagnetic compatibility (EMC)
  data security due to a fail-safe data transmission protocol
  short message length, only a few bytes per message
Where in a car is CAN used?
  communication between electronic control units
  separated CAN – sections at different speed for:
    “Auto - Body” electronic control units” (chassis, light, central locking)
    “Engine” control units and “Power train” modules
    Comfort modules
Notes: <number>

## Slide 5: Automotive network systems
 Other automotive networks than CAN:
  LIN – “Local Interconnect Network”
    Body Electronic; Door, Mirror, Seat, Dashboard, Roof
    20 Kbit/s
    Master / Slave time triggered protocol
    Single wire system; 12 V signal level
    www.lin-subbus.org
  MOST – “Media Oriented Systems Transport”
    Optical System for Multi – Media and infotainment
    Audio, Video, Mobile Phone, GPS
    Fibre optical circular system at 25 Mbit/s or 150 Mbit/s or
    Electrical layer at 50 Mbit/s.
    www.mostcooperation.com
  FlexRay
    Time Triggered Protocol for fail safe applications;
    10 Mbit/s; dual channel redundancy
    www.flexray.com
Notes: <number>

## Slide 6: Implementation / Classification of CAN
Implementation: amount of functionality in CAN- Silicon
Don’t get confused !
Communication is standardized and identical for all implementations of CAN. However, there are two types of hardware implementation and two versions of data format:
Implementation
Data Format
Full - CAN
Basic CAN
Standard
Extended
Notes: <number>

## Slide 7: Basic- and Full-CAN communication
Close coupled MCU-core and CAN
only one transmit buffer
only two receive buffer
only one filter for incoming messages
Software routines are needed to select between incoming messages
provide a message server
extensive acceptance filtering on incoming messages
user configurable mailboxes
mailbox memory area , size of mailbox areas depends on manufacturer
advanced error recognition
Full - CAN
Basic CAN
Notes: <number>

## Slide 8: The Data Format of CAN
    CAN-Version 2.0A
    messages with 11-bit - identifiers
    CAN-Version 2.0B
    messages with 29-bit-identifiers
==> Suitably configured, each implementation ( BASIC or FULL) can handle both standard and extended data formats.
Standard
Extended
Notes: <number>

## Slide 9: The CAN Data Frame
DATA-Frame CAN 2.0A (11-bit-identifier)
DATA-Frame CAN 2.0B (29-bit-identifier)
Notes: <number>

## Slide 10: The CAN Data Frame
each data frame consists of four segments :
(1) arbitration-field :
  denote the priority of the message
  logical address of the message (identifier)
  Standard frame, CAN 2.0A: 11 bit-identifier
  Extended frame, CAN 2.0B: 29 bit-identifier
(2) data field :
  up to 8 bytes per message ,
  a 0 byte message is also permitted
(3) CRC field:
  cyclic redundancy check ; contains a checksum generated by a CRC-polynomial
(4) end of frame field:
  contains acknowledgement, error-messages, end of message
Notes: <number>

## Slide 11: The CAN Data Frame
start bit (1 bit - dominant): beginning of a message; after idle-time falling-edge to synchronize all transmitters
identifier (11 bit): mark the name of the message and its priority ;the lower the value the higher the priority
RTR (1 bit): remote transmission request; if RTR=1 (recessive) no valid data inside the frame - it is a request for receivers to send their messages
IDE (1 bit): Identifier Extension; if IDE=1 then extended CAN-frame
r0 (1 bit): reserved
CDL (4 bit): data length code in byte (0...8)
data (0...8 byte): the data of the message
CRC (15 bit): cyclic redundancy code for error detection, no correction; hamming-distance 6 (up to 6 single bit errors can be detected)
ACK (2 bit): acknowledge; if a receiving node has received a valid message, it must transmit an dominant acknowledge – bit
EOF (7 bit = 1, recessive): end of frame; intentional violation of the bit-stuff-rule ; normally after five recessive bits one stuff-bit follows automatically
IFS (3 bit = 1, recessive): inter frame space; time space to copy a received message from bus-handler into buffer
Extended Frame only :
SRR (1 bit = recessive): substitute remote request ; substitution of the RTR-bit in standard frames
r1 (1 bit ): reserved
Notes: <number>

## Slide 12: The Standardisation of CAN
CAN is an open system and has been standardized by ISO
CAN follows the ISO - OSI seven layer model for open system interconnections
CAN implements layer 1, 2 and 7 only
However, Layer 7 is not standardised
Physical Layer Type | Europe www.iso.org | North America www.sae.org
Single – Wire CAN | n/a | SAE J2411 Single Wire CAN for Vehicle Applications
Low-Speed Fault Tolerant CAN | ISO 11519 - 2 ISO 11898 - 3 | n/a.
High-Speed CAN | ISO 11898 | SAEJ2284
Notes: <number>

## Slide 13: ISO Reference Model
Open Systems Interconnection (OSI):
Layer 1: transmission line(s)
  differential two-wire-line, twisted pair with/without shield
  Transceiver Integrated Circuit
  Optional: fibre optical lines (passive coupled star, carbon )
  Optional: Coding as PWM, NRZ, Manchester Code
  ISO 11898
Layer 2: Data Link Layer
  message format and transmission protocol
  ISO 11898
  CSMA/CA access protocol
Layer 7: Application Layer
  different standards in industry, not standardized in automotive
Notes: <number>

## Slide 14: CAN Layer 7
CAN Application Layer (CAL):
  European CAN user group ”CAN in Automation (CiA)”
  originated by Philips Medical Systems 1993
  CiA DS-201 to DS-207
  standardised communication objects, -services and -protocols (CAN-based Message Specification)
  Services and protocols for dynamic attachment of identifiers (DBT)
  Services and protocols for initialise, configure and obtain the net (NMT)
  Services and protocols for parametric set-up of layer 2 &1 (LMT)
  Automation, medicine, traffic-industry
OSEK/VDX
  “Offene Systeme für Elektronik im Kraftfahrzeug”
  Standard of European automotive electronics industry
  include services of a standardised real-time-operating system
  Network Management Services
  Communication Services
Notes: <number>

## Slide 15: CAN Layer 7
CANopen :
  European Community funded project “ESPRIT”
  1995 : CANopen profile :CiA DS-301
  1996 : CANopen device profile for I/O : CiA DS-401
  1997 : CANopen drive profile
  industrial control , numeric control in Europe
DeviceNet :
  Allen-Bradley, now ODVA-group (www. odva.org)
  device profiles for drives, sensors and actuators
  master-slave communication as well as peer to peer
  industrial control , mostly USA
Smart Distributed Systems (SDS)
  Honeywell , device profiles
  only 4 communication functions , less hardware resources
  industrial control and PC-based control
Notes: <number>

## Slide 16: Bus Access Procedure
The “Ethernet”: CSMA / CD
CSMA /CD:
Carrier
    Sense
    Multiple
    Access with
    Collision
Detection
Note: This flowchart does NOT apply to CAN! See following page
Notes: <number>

## Slide 17: CAN Access Procedure: CSMA/CA
CSMA/ CA: “Carrier Sense Multiple Access with Collision Avoidance”
access-control with non destructive bit-wide arbitration
if there is a collision , the “winner” continues
the message with higher priority is not delayed!
real-time capability for high prioritised messages
the lower the identifier, the higher the priority
Notes: <number>

## Slide 18: CSMA/CA (cont.)
CSMA / CA =
"bit - wide arbitration during transmission with simultaneous receiving and comparing of the transmitted message"
means :
  if there is a collision within the arbitration-field, only the nodes with lower priorities cancel transmission.
  The node with the highest priority continues with the transmission of the message.
Notes: <number>

## Slide 19: CAN Physical Layers
CAN - High - Speed (ISO 11898):
Notes: <number>

## Slide 20: CAN High speed Node
F2833x with on-chip
CAN module
CAN Transceiver
CAN - bus
Txd
Rxd
CAN_L
CAN_H
SN65HVD23X
Notes: <number>
TI transceiver: SN75LBC031
- interfaces the single ended CAN controller with the differential CAN bus.
- transmission rate up to 1Mbit/s
2 states on the bus:
recessive: CAN_H = CAN_L = 2.5V
dominant: CAN_H = 3.5V and CAN_L = 1.5V

## Slide 21: CAN Error – Frame
any node that detects a bus error generates an error - frame
an error frame is transmitted as soon as an error has been detected, e.g. inside a data frame
consists of two fields: Error Flag Field; Error Delimiter Field
Error Delimiter Field:
  8 recessive bits
  allow bus nodes to restart bus communication after an error
Error Flag Field:
  Type depends on the error-state of the node:
    error active: 6 consecutive dominant error bits; all other nodes will respond to this violation with their own error frames  Error Flag Field = 6…12 dominant bits
    error passive: 6 consecutive recessive bits plus 8 error delimiter bits = 14 recessive bits
      receiver: does not corrupt the message
      transmitter: other nodes may respond with active error frames
Notes: <number>

## Slide 22: CAN Error – Frame
data
error frame
Inter frame space
6 bit error flag
6..12 bit error overlay
8 bit error delimiter
Active error frame
Example1: Active error frame
Notes: <number>

## Slide 23: CAN Error – Frame
data
error frame
Inter frame space
6 bit error flag
8 bit error delimiter
passive error frame from a receiver
data
error frame
Inter frame space
6 bit passive error flag
6 bit active error overlay
from another active node
8 bit error delimiter
passive error frame from a transmitter
Notes: <number>

## Slide 24: CAN Error – Frame
data
Transmitter X
CAN - Tx
Example: active error frame
Receiver Y
CAN - Tx
Receiver Z
CAN - Tx
CAN
Bus - level
1
2
3
4
4
5
6
6
8
3
6
Notes: <number>

## Slide 25: CAN Error – Frame
1
Node X sees a bit error
2
Node X generates an active error flag field
3
Nodes Y, Z realize a stuff bit error after bit 6 of the active error flag field
(note: if the corrupted data frame had dominant bits, the stuff bit error is detected earlier)
4
Nodes Y,Z transmit their own active error flag field of 6 dominant bits
5
All nodes transmit the recessive error delimiter field. Node Y and Z see
no difference @ bus level, but node X detects a delay of 6 bits between bus level and its own output  First node to message error
6
After the last 8 recessive error delimiter bits @ CAN-bus and 3 bit of inter frame space a new arbitration is entered by node X, e.g. it has to compete again with other nodes
Notes: <number>

## Slide 26: CAN Error Recognition
Bit-Error
  the transmitted bit doesn’t read back with the same digital level (except arbitration and acknowledge- slot )
Bit-Stuff-Error
  more than 5 continuous bits read back with the same digital level (except ‘end of frame’-part of the message )
CRC-Error
    the received CRC-sum doesn’t match with the calculated sum
Format-Error
    Violation of the data-format of the message , e.g.: CRC-delimiter is not recessive or violation of the ‘end -of-frame’-field
Acknowledgement-Error
    transmitter receives no dominant bit during the acknowledgement slot, i.e. the message was not received by another node.
Notes: <number>

## Slide 27: CAN Error Status
Purpose: avoid persistent disturbances of the CAN by switching off defective nodes
three Error States :
Error Active: normal mode, messages will be received and transmitted. In case of error an active error frame will be transmitted.
Error Passive: after detection of a certain number of errors, the node reaches this state. Messages will be received and transmitted but in case of an error the node sends a passive error frame.
Bus Off: the node is separated from CAN, neither transmission nor receive of messages is allowed and the node is no longer able to transmit error frames.
Notes: <number>

## Slide 28: CAN Error Counter
transitions will be carried out automatically by the CAN-chip
states are managed by 2 Error Counters :
Receive Error Counter (REC)
Transmit Error Counter (TEC)
Possible situations :
a) a transmitter recognises an error:
TEC:=TEC + 8
b) a receiver sees an error : REC:=REC + 1
c) a receiver sees an error, after transmitting an error frame: REC:=REC + 8
d) if an ‘error active’-node find’s a bit-stuff-error during transmission of an error frame: TEC:=TEC+ 1
e) successful transmission: TEC:=TEC - 1
f) successful receive: REC:=REC - 1
State - Diagram:
Notes: <number>

## Slide 29: F2833x CAN Features
Fully CAN protocol compliant, version 2.0B
Supports data rates up to 1 Mbps
Thirty-two mailboxes
  Configurable as receive or transmit
  Configurable with standard or extended identifier
  Programmable receive mask
  Supports data and remote frame
  Composed of 0 to 8 bytes of data
  Uses 32-bit time stamp on messages
  Programmable interrupt scheme (two levels)
  Programmable alarm time-out
Programmable wake-up on bus activity
Self-test mode

## Slide 30: F2833x CAN Block Diagram
Memory Management
Unit
CPU Interface,
Receive Control Unit
Timer Management Unit
eCAN Memory
(512 Bytes)
Register and Message
Object Control
Mailbox RAM
(512 Bytes)
32-Message Mailbox
of 4 x 32-Bit Words
32
32
Receive Buffer
Transmit Buffer
Control Buffer
Status Buffer
SN65HVD23x
3.3-V CAN Transceiver
.
.
CAN Bus
32
32
Data
Address
eCAN0INT
eCAN1INT

## Slide 31: F2833x CAN Memory
Data Space
CAN
0x00 6000
0x00 0000
0x 3F FFFF
0x00 61FF
6080
6040
61FF
Control and
Status Register
Message
Object
Time Stamps
Mailbox 0
Mailbox 1
Mailbox 31
Local
Acceptance
Masks
Message
Object
Time Out
60C0
6108
6100

## Slide 32: CAN Control & Status Register
6000
CANME
CANMD
6002
6004
CANTRS
CANTRR
6006
6008
CANTA
CANAA
600A
600C
CANRMP
CANRML
600E
6010
CANRFP
CANGAM
6012
6014
CANMC
CANBTC
6016
6018
CANES
CANTEC
601A
601C
CANREC
6020
CANGIM
CANGIF1
6022
6024
CANMIM
CANMIL
6026
6028
CANOPC
CANTIOC
602A
602C
CANRIOC
602E
CANLNT
CANTOC
6030
6032
CANTOS
CANGIF0
601E
31
0
31
0
6034
reserved
reserved
6036
6038
reserved
reserved
603A
603C
reserved
reserved
603E

## Slide 33
CAN Mailbox Enable Register (CANME) – 0x006000
15
16
31
CANME[15:0]
CANME[31:16]
0
Mailbox Enable Bits
0 = corresponding mailbox is disabled
1 = The corresponding mailbox is enabled. A mailbox must be disabled before
writing to the contents of any mailbox identifier field.
CAN Mailbox Direction Register (CANMD) – 0x006002
15
16
31
CANMD[15:0]
CANMD[31:16]
0
Mailbox Direction Bits
0 = corresponding mailbox is defined as a transmit mailbox.
1 = corresponding mailbox is defined as a receive mailbox.

## Slide 34
CAN Transmission Request Set Register (CANTRS) – 0x006004
15
16
31
CANTRS[15:0]
CANTRS[31:16]
0
Mailbox Transmission Request Set Bits (TRS)
0 = no operation. NOTE: Bit will be cleared by CAN-Module logic after successful transmission.
1 = Start of transmission of corresponding mailbox. Set to 1 by user software;
OR by CAN –logic in case of a Remote Transmit Request.
CAN Transmission Request Reset Register (CANTRR) – 0x006006
15
16
31
CANTRR[15:0]
CANTRR[31:16]
0
Mailbox Transmission Reset Request Bits (TRR)
0 = no operation.
1 = setting TRRn cancels a transmission request, if not already in progress.

## Slide 35
CAN Transmission Acknowledge Register (CANTA) – 0x006008
15
16
31
CANTA[15:0]
CANTA[31:16]
0
Mailbox Transmission Acknowledge Bits (TA)
0 = the message is not sent.
1 = if the message of mailbox n is sent successfully, the bit n of this register is set.
Note: To reset a TA bit by software: write a ‘1’ into it.
CAN Abort Acknowledge Request Register (CANAA) – 0x00600A
15
16
31
CANAA[15:0]
CANAA[31:16]
0
Mailbox Abort Acknowledge Bits (AA)
0 = The transmission is not aborted.
1 = The transmission of mailbox n is aborted.
Note: To reset a AA bit by software: write a ‘1’ into it.

## Slide 36
CAN Receive Message Pending Register (CANRMP) – 0x00600C
15
16
31
CANRMP[15:0]
CANRMP[31:16]
0
Mailbox Receive Message Pending Bits (RMP)
0 = the mailbox does not contain a message.
1 = the mailbox contains a valid message.
Note: To reset a RMP bit by software: write a ‘1’ into it.
CAN Receive Message Lost Register (CANRML) – 0x00600E
15
16
31
CANRML[15:0]
CANRML[31:16]
0
Mailbox Receive Message Lost Bits (RML)
0 = no message was lost.
1 = an old unread message has been overwritten by a new one in that mailbox.
Note: To reset a RML bit by software: write a ‘1’ into it.

## Slide 37
CAN Remote Frame Pending Register (CANRFP) – 0x006010
15
16
31
CANRFP[15:0]
CANRFP[31:16]
0
Mailbox Remote Frame Pending Bits (RFP)
0 = no remote frame request was received.
1 = a remote frame request was received by the CAN module.
Note: To reset a RFP bit by software: write a ‘1’ into the corresponding TRR bit.

## Slide 38
CAN Global Acceptance Mask Register (CANGAM) – 0x006012
15
16
31
CANGAM[15:0]
CANGAM[28:16]
0
Acceptance Mask Identifier Bit (AMI)
0 = the identifier extension bit in the mailbox determines which messages shall be received.
Filtering is not applicable.
1 = standard and extended frames can be received. In case of an extended frame all 29 bits of the identifier
and all 29 bits of the GAM are used for the filter. In case of a standard frame only bits 28-18 of the identifier
and the GAM are used for the filter.
AMI
reserved
30-29
28
Note : This Register is used in Standard Can Controller (SCC) mode only. It is hers a single
input filter for mailboxes 6…15, if the AME bit (MID.30) of the corresponding mailbox is set.
CANGAM is not used in extended eCAN – Mode!
Global Acceptance Mask (GAM)
0 = bit position must match the corresponding bit in register CANMIDn.
1 = bit position of the incoming identifier is a “don’t’ care”.

## Slide 39
CAN Master Control Register (CANMC) – 0x006014
15
16
31
reserved
0
MBCC
MBNR
Mailbox Timestamp counter clear (MBCC)
0 = no operation
1 = timestamp counter is reset to 0 after a successful transmission or reception of mailbox 16.
ABO
CDR
WUBA
DBO
PDR
CCR
SCB
TCC
SRES
STM
4
14
13
12
11
10
9
8
7
6
5
Timestamp counter MSB clear (TCC)
0 = no operation
1 = timestamp counter MSB is reset to 0
SCC Compatibility bit (SCB)
0 = standard CAN mode (SCC)
1 = high end CAN (HECC) mode
Change Configuration Request (CCR)
0 = software requests normal operation
1 = software requests write access to CANBTC, CANGAM, LAM[0] and LAM[3].
A request is granted by the CAN module with flag CCE ( CANES) = 1.
Standard CAN Mode SCC:
Reduced functionality;
Mailboxes 0...15 only
3 acceptance masks only
No timestamp features
High end CAN Mode HECC:
Full functionality;
Mailboxes 0...31
32 acceptance masks

## Slide 40
CAN Master Control Register (CANMC) – 0x006014
15
0
MBCC
MBNR
ABO
CDR
WUBA
DBO
PDR
CCR
SCB
TCC
SRES
STM
4
14
13
12
11
10
9
8
7
6
5
Data Byte Order (DBO) in Mailbox Registers
MDH[31:0] and MDL[31:0]
0 = MDH[31:0] : Byte 4,5,6,7 ; MDL[31:0] : Byte 0,1,2,3
1 = MDH[31:0] : Byte 7,6,5,4 ; MDL[31:0] : Byte 3,2,1,0
Wake up on bus activity (WUBA)
0 = Module leaves power down only
after writing a 0 to PDR
1 = Module leaves power down on
any bus activity
Change data field request (CDR)
0 = normal operation
1 = software requests access to the data field in 2MBNR”.
NOTE: software must clear this bit after access is done.
Auto bus on (ABO)
0 = “bus off’ state is permanent.
1 = “bus off” state is left into “bus on”
after 128*11 recessive bits have been received.
Self Test Mode (STM)
0 = normal mode
1 = Module generates its own ACK
Software Reset(SRES)
0 = no effect
1 = CAN Module reset
Mailbox Number(MBNR)
Number , used for CDR
Power Down Mode Request (PDR)
0 = normal operation
1 = power down mode is requested.
NOTE: bit is automatically cleared
upon wakeup from power down!

## Slide 41
CAN Bit-Timing Configuration
CAN protocol specification splits the nominal bit time into four different time segments:
  SYNC_SEG
    Used to synchronize nodes
    Length : always 1 Time Quantum (TQ)
  PROP_SEG
    Compensation time for the physical delay times within the net
    Twice the sum of the signal’s propagation time on the bus line, the input comparator delay and the output driver delay.
    Programmable from 1 to 8 TQ
  PHASE_SEG1
    Compensation for positive edge phase shift
    Programmable from 1 to 8 TQ
  PHASE_SEG2
    Compensation time for negative edge phase shift
    Programmable from 2 to 8 TQ

## Slide 42
TCAN = TQ + tseg1 + tseg2
CAN Bit-Timing Configuration
tseg1: PROP_SEG + PHASE_SEG1
tseg2: PHASE_SEG2
TQ: SYNCSEG
CAN Nominal Bit Time
SYNCSEG
sjw
sjw
tseg2
tseg1
TQ
Sample Point
Transmit Point

## Slide 43
CAN Bit-Timing Configuration
According to the CAN – Standard the following bit timing rules apply:
  tseg1  tseg2
  3/BRP ≤ tseg1 ≤ 16 TQ
  3/BRP ≤ tseg2 ≤ 8 TQ
  1 TQ ≤ sjw ≤ MIN[ 4*TQ , tseg2]
  BRP  5, if three sample mode is used

## Slide 44
CAN Bit-Timing Configuration Register (CANBTC) – 0x006016
Baud Rate Prescaler (BRP):
defines the Time Quantum (TQ):
31
reserved
BRP.2
BRP.3
BRP.4
BRP.5
BRP.0
BRP.1
16
BRP.7
BRP.6
23
24
Note:
BaseCLK = SYSCLK / 2 for 283xx, 2803x devices
BaseCLK = SYSCLK for 281x, 280x and 2801x devices

## Slide 45
Synchronisation Jump Width (SJW)
CAN Bit-Timing Configuration Register (CANBTC) – 0x006016
Time Segment 1( tseg1)
15
reserved
TSEG1
SJW
TSEG2
0
SAM
SBG
7
8
2
3
6
9
10
11
Time Segment 2( tseg2)
Sample Points (SAM)
0 = one sample at sample point
1 = 3 samples at sample point – majority vote
Synchronisation Edge Select (SBG)
0 = re synchronisation with falling edge only
1 = re-sync. with rising & falling edge

## Slide 46
CAN Bit-Timing Examples
Bit Configuration for BaseCLK = 75 MHz
Sample Point at 80% of Bit Time :
Example 100 kbit/s
  TQ = (49+1)/ 75 MHz = 0.667 µs
  tseg1 = 0.667 µs (10 + 1) = 7.337 µs  tCAN = 10 µs;
  tseg2 = 0.667 µs (2 + 1) = 2 µs
CAN - data rate | BRP | TSEG1 | TSEG2
1 Mbit/s | 4 | 10 | 2
500 kbit/s | 9 | 10 | 2
250 kbit/s | 19 | 10 | 2
125 kbit/s | 39 | 10 | 2
100 kbit/s | 49 | 10 | 2
50 kbit/s | 99 | 10 | 2

## Slide 47
CAN Error and Status Register (CANES) – 0x006018
Warning Status (EW)
0 = values of both error counters are less than 96
1 = one error counter has reached 96
Error Passive State (EP)
0 = CAN is in Error Active Mode
1 = CAN is in Error Passive Mode
31
reserved
BO
ACKE
SE
CRCE
EW
EP
16
BE
SA1
23
24
17
18
19
20
21
22
FE
Bus Off State (BO)
0 = normal operation
1 = CANTEC has reached the limit of 256. Module
has been switched of the bus.
Stuff Bit Error (SE)
0 = normal operation
1 = a stuff bit error has occurred.
Acknowledgement Error (ACKE)
0 = normal operation
1 = CAN module has not received an ACK.
Cyclic Redundancy Check Error (CRCE)
0 = normal operation
1 = a wrong CRC was received.
Stuck at dominant Error (SA1)
0 = The CAN module detected a recessive bit
1 = The CAN module never detected a recessive bit.
Bit Error (BE)
0 = no bit error detected
1 = a received bit does not match a transmitted bit
(outside of the arbitration field).
Form Error (FE)
0 = normal operation
1 = one of the fixed form bit fields of a message was wrong.

## Slide 48
CAN Error and Status Register (CANES) – 0x006018
Transmit Mode (TM)
0 = CAN controller is not transmitting a message.
1 = CAN controller is transmitting a message.
Receive Mode (RM)
0 = CAN controller is not receiving a message.
1 = CAN controller is receiving a message.
15
reserved
Res.
PDA
CCE
SMA
TM
RM
0
1
2
3
4
5
6
Power Down Mode Acknowledge (PDA)
0 = normal operation
1 = CAN module has entered power down mode.
Change Configuration Enable (CCE)
0 = CPU cannot write into
configuration registers.
1 = CPU has write access into
configuration registers.
Suspend Mode Acknowledge (SMA)
0 = normal operation
1 = CAN module has entered suspend mode.
Note: Suspend mode is activated by the debugger
when the DSP is not in run mode.

## Slide 49
CAN Transmit Error Counter Register (CANTEC) – 0x00601A
CAN Receive Error Counter Register (CANREC) – 0x00601C
15
16
31
reserved
0
Transmit Error Counter (TEC)
Value TEC is incremented or decremented according to the CAN protocol specification
reserved
TEC
15
16
31
reserved
0
Receive Error Counter (REC)
Value REC is incremented or decremented according to the CAN protocol specification
reserved
REC

## Slide 50
CAN Global Interrupt Mask Register (CANGIM) – 0x006020
Global Interrupt Level (GIL)
For Interrupts TCOF,WDIF,WUIF,BOIF and WLIF
0 = mapped into HECC_INT_REQ[0] line – GIF0
1 = mapped into HECC_INT_REQ[1] line – GIF1
Interrupt Mask Bits:
MTOM = Mailbox Timeout Mask
TCOM = Timestamp Counter Overflow Mask
AAM = Abort Acknowledge Interrupt Mask
WDIM = Write Denied Interrupt Mask
WUIM = Wake-up Interrupt Mask
RMLIM = Receive message lost Interrupt Mask
BOIM = Bus Off Interrupt Mask
EPIM = Error Passive Interrupt Mask
WLIM = Warning level Interrupt Mask
Interrupt Mask Bits
0 = Interrupt disabled
1 = Interrupt enabled
15
16
31
reserved
0
Res.
reserved
GIL
WLIM
EPIM
BOIM
RMLIM
WUIM
WDIM
AAM
I0EN
I1EN
1
14
13
12
11
10
9
8
7
3
2
TCOM
MTOM
17
18
Interrupt 1 Enable (I1EN)
0 = HECC_INT_REQ[1] line is disabled
1 = HECC_INT_REQ[1] line is enabled
Interrupt 0 Enable (I0EN)
0 = HECC_INT_REQ[0] line is disabled
1 = HECC_INT_REQ[0] line is enabled

## Slide 51
CAN Global Interrupt Flag 0 Register (CANGIF0) – 0x00601E
Mailbox Interrupt Vector (MIV0)
Indicates the number of the message object that set the
global mailbox interrupt flag (GMIF0)
Interrupt Flag Bits:
MTOF0 = Mailbox Timeout Flag
TCOF0 = Timestamp Counter Overflow Flag
GMIF0 = Global Mailbox Interrupt Flag
AAIF0 = Abort Acknowledge Interrupt Flag
WDIF0 = Write Denied Interrupt Flag
WUIF0 = Wake-up Interrupt Flag
RMLIF0 = Receive message lost Interrupt Flag
BOIF0 = Bus Off Interrupt Flag
EPIF0 = Error Passive Interrupt Flag
WLIF0 = Warning level Interrupt Flag
Interrupt Flag Bits
0 = Interrupt has not occurred
1 = Interrupt has occurred
15
16
31
reserved
0
GMIF0
Res.
MIV0.2
WLIF0
EPIF0
BOIF0
RMLIF0
WUIF0
WDIF0
AAIF0
MIV0.0
MIV0.1
1
14
13
12
11
10
9
8
7-5
3
2
TCOF0
MTOF0
17
18
MIV0.4
MIV0.3
4

## Slide 52
CAN Global Interrupt Flag 1 Register (CANGIF1) – 0x006022
Mailbox Interrupt Vector (MIV1)
Indicates the number of the message object that set the
global mailbox interrupt flag (GMIF1)
Interrupt Flag Bits:
MTOF1 = Mailbox Timeout Flag
TCOF1 = Timestamp Counter Overflow Flag
GMIF1 = Global Mailbox Interrupt Flag
AAIF1 = Abort Acknowledge Interrupt Flag
WDIF1 = Write Denied Interrupt Flag
WUIF1 = Wake-up Interrupt Flag
RMLIF1 = Receive message lost Interrupt Flag
BOIF1 = Bus Off Interrupt Flag
EPIF1 = Error Passive Interrupt Flag
WLIF1 = Warning level Interrupt Flag
Interrupt Flag Bits
0 = Interrupt has not occurred
1 = Interrupt has occurred
15
16
31
reserved
0
GMIF1
Res.
MIV1.2
WLIF1
EPIF1
BOIF1
RMLIF1
WUIF1
WDIF1
AAIF1
MIV1.0
MIV1.1
1
14
13
12
11
10
9
8
7-5
3
2
TCOF1
MTOF1
17
18
MIV1.4
MIV1.3
4

## Slide 53
CAN Mailbox Interrupt Mask Register (CANMIM) – 0x006024
15
16
31
CANMIM[15:0]
CANMIM[31:16]
0
Mailbox Interrupt Mask Bits (MIM)
0 = mailbox interrupt is disabled.
1 = mailbox interrupt is enabled. An Interrupt is generated if a
message has been transmitted successfully or if a message has
been received without an error.
CAN Mailbox Interrupt Level Register (CANMIL) – 0x006026
15
16
31
CANMIL[15:0]
CANMIL[31:16]
0
Mailbox Interrupt Level Bits (MIL)
0 = mailbox interrupt is generated on HECC_INT_REQ[0] line.
1 = mailbox interrupt is generated on HECC_INT_REQ[1] line.

## Slide 54
CAN Overwrite Protection Control Register (CANOPC) – 0x006028
15
16
31
CANOPC[15:0]
CANOPC[31:16]
0
Overwrite Protection Control Bits (OPC)
0 = the old message in mailbox N may be overwritten by a new one.
This will be notified by the receive message lost bit RML[n].
1 = an old message in mailbox N is protected against being overwritten
by a new one.
Thus, the next mailboxes are checked for a matching ID.
If no other mailbox is found, the new message is lost.

## Slide 55
CAN I/O Control Register (CANTIOC) – 0x00602A
TXFUNC
0 = CANTX pin is a normal I/O pin.
1 = CANTX is used for CAN transmit functions.
15
16
31
reserved
reserved
0
TXIN
TXFUNC
TXDIR
TXOUT
2
1
3
TXDIR
0 = CANTX pin is an input pin if configured as a normal I/O pin.
1 = CANTX pin is an output pin if configured as a normal I/O pin.
TXOUT
Output value for CANTX pin, if configured as normal output pin
TXIN
0 = Logic 0 present on pin CANTX.
1 = Logic 1 present on pin CANTX.

## Slide 56
CAN I/O Control Register (CANRIOC) – 0x00602C
RXFUNC
0 = CANRX pin is a normal I/O pin.
1 = CANRX is used for CAN receive functions.
15
16
31
reserved
reserved
0
RXIN
RXFUNC
RXDIR
RXOUT
2
1
3
RXDIR
0 = CANRX pin is an input pin if configured as a normal I/O pin.
1 = CANRX pin is an output pin if configured as a normal I/O pin.
RXOUT
Output value for CANRX pin, if configured as normal output pin
RXIN
0 = Logic 0 present on pin CANRX.
1 = Logic 1 present on pin CANRX.

## Slide 57
CAN Local Network Time Register (CANLNT) – 0x00602E
15
16
31
LNT[15:0]
LNT[31:16]
0
LNT is a Free Running Counter, Clocked from the bit clock of the CAN module.
LNT is written into the time stamp register (MOTS ) of the corresponding mailbox when a received message has been stored or a message has been transmitted.
LNT is cleared when mailbox #16 is transmitted or received. Thus mailbox #16 can be used for a global network time synchronization.

## Slide 58
CAN Time Out Control Register (CANTOC) – 0x006030
31
0
31
TOS[31:0]
TOC[31:0]
0
Time Out Control Bits (TOC)
0 = Time Out function is disabled for mailbox n.
1 = Time Out function is enabled for mailbox n.
If LNT is greater than the corresponding MOTO register, a time out event will be generated
CAN Time Out Status Register (CANTOS) – 0x006032
Time Out Status Flags (TOS)
0 = No Time Out occurred for mailbox n.
1 = The value in LNT is greater or equal to the value in the corresponding MOTO register

## Slide 59: CAN Local Acceptance Mask Register 0x00 6040 - 0x00 607F
reserved
15
16
28
30-29
31
LAMn[15:0]
LAMn[28:16]
LAMI
0
0 = IDE bit of mailbox determines which message shall be received
1 = extended or standard frames can be received.
extended: all 29 bit of LAM are used for filter against all 29 bit of mailbox .
standard: only first eleven bits of mailbox and LAM [28-18] are used.
LAMn[28-0]: Masking of identifier bits of incoming messages
1 = don’t care ( accept 1 or 0 for this bit position ) of incoming identifier.
0 = received identifier bit must match the corresponding message identifier bit (MID).
Note: There are two operating modes of the CAN module : “HECC” and “SCC”.
In “SCC” (default after reset ) LAM0 is used for mailboxes 0 to 2, LAM3 is used for mailboxes 3 to 5
and the global acceptance mask (CANGAM) is used for mailboxes 6 to 15.
In “HECC” ( CANMC:13 = 1) each mailbox has its own mask register LAM0 to LAM31.

## Slide 60: CAN Message Object Time Stamp 0x00 6080 - 0x00 60BF
15
16
31
MOTSn[15:0]
MOTSn[31:16]
0
A free running counter (register CANLNT) is used to get a stamp
of the time of reception or transmission of a message.
CANLNT is a 32 bit timer that is clocked by the CAN – bit – time unit.
The current content of CANLNT is written into MOTSn when a received message has been stored or a message has been transmitted successfully.

## Slide 61: CAN Message Object Time-Out 0x00 60C0 - 0x00 60FF
15
16
31
MOTOn[15:0]
MOTOn[31:16]
0
If the value in CANLNT is equal or greater than the value in MOTOn, the appropriate bit in register CANTOS will be set , assuming this feature was allowed in CANTOC.
Also, an Interrupt Service can be triggered from such an event.

## Slide 62: CAN Mailbox Memory 0x00 6100 - 0x00 61FF
AME
15
16
29
30
31
IDn[15:0]
IDn[28:16]
IDE
0
AAM
28
Message Identifier Register (MID) Mailbox n
Identifier Extension Bit
0 = Standard Identifier (11 Bits)
1 = Extended Identifier (29 Bits)
Acceptance Mask Enable Bit ( receiver only)
0 = no Acceptance Mask used. All identifier bits must match to receive the message
1 = the corresponding Mailbox Acceptance Mask is used
Auto Answer Mode Bit ( transmitter only)
0 = mailbox does not reply to remote requests.
1 = if a matching Remote Request is received, the contents of this mailbox will be sent.
Message Identifier
Standard Frames : IDn[28:18] are used
Extended Frames : IDn[28:0] are used
Address | Content
0x6100 | MSGID Mailbox 0
0x6102 | MSGCTRL Mailbox 0
0x6104 | CANMDL Mailbox 0; 4 lower data bytes
0x6106 | CANMDH Mailbox 0; 4 upper data bytes

## Slide 63: CAN Mailbox Memory 0x00 6100 - 0x00 61FF
RTR
15
16
4
13
31
reserved
reserved
0
DLC
3
Message Control Field Register (MCF) Mailbox n
Transmit Priority Level
Priority compared to the other 31 mailboxes.
Highest number has highest priority.
Data Length Code
Valid numbers are 0 to 8.
Remote Transmission Request
0 = no RTR requested.
1 = for receiver mailboxes:
if TRS bit is set, a remote frame is transmitted and the corresponding
data frame will be received in the same mailbox.
1 = for transmit mailboxes:
if TRS bit is set, a remote frame is transmitted but the corresponding
data frame has to be received in another mailbox.
TPL
reserved
12
8
7
5

## Slide 64: CAN Mailbox Memory 0x00 6100 - 0x00 61FF
23
24
15
31
Data Byte 0
0
Message Data Low (MDL) Register with DBO = 0 Mailbox n
16
8
7
Data Byte 1
Data Byte 3
Data Byte 2
23
24
15
31
Data Byte 3
0
Message Data Low (MDL) Register with DBO = 1 Mailbox n
16
8
7
Data Byte 2
Data Byte 0
Data Byte 1

## Slide 65: CAN Mailbox Memory 0x00 6100 - 0x00 61FF
23
24
15
31
Data Byte 4
0
Message Data High (MDH) Register with DBO = 0 Mailbox n
16
8
7
Data Byte 5
Data Byte 7
Data Byte 6
23
24
15
31
Data Byte 7
0
Message Data High (MDH) Register with DBO = 1 Mailbox n
16
8
7
Data Byte 6
Data Byte 4
Data Byte 5

## Slide 66
CAN Example : transmit a frame
Lab 11_1: Transmit a CAN message
  CAN baud rate: 100 kbit/s
  Transmit a one byte message every second
  Message Identifier 0x 1000 0000 (extended frame)
  Use Mailbox #5 as transmit mailbox
  Message content: current value of a binary counter
  Transceiver SN65HVD230 is used
  Connect CAN at header J4 of Peripheral Explorer
    J4-1: CAN_H
    J4-2: CAN_L

## Slide 67
CAN Example : receive a frame
Lab 11_2: Receive a CAN message
  CAN baud rate : 100 kbit/s
  Message Identifier 0x 1000 0000 ( extended frame)
  Use Mailbox #1 as receive mailbox
  Display the binary counter at LEDs LD1 to LD4 (GPIO9, GPIO11, GPIO34 and GPIO49)
Pin Nr. | Signal | Description
1 | - | Reserved
2 | CAN_L | CAN Bus Signal (dominant low)
3 | CAN_GND | CAN ground
4 | - | Reserved
5 | CAN_SHLD | Optional shield
6 | GND | Optional CAN ground
7 | CAN_H | CAN Bus Signal (dominant high)
8 | - | Reserved
9 | CAN_V+ | Optional external voltage supply Vcc