## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 4: Numerical Systems
Digital Signal Controller
TMS320F2833x

## Slide 2: Floating-Point, Integer and Fixed-Point
Two basic categories of processors:
  Floating-Point
  Integer/Fixed-Point
What is the difference?
What are advantages / disadvantages ?
Real-Time Control:
  Most microcontrollers are Fixed-Point!
  F2833x supports both worlds in hardware!
Notes: <number>

## Slide 3: Processor Types
Floating-Point Processors
  Internal Hardware Unit to support Floating - Point Operations
  Examples: Intel’s Pentium Series , Texas Instruments C6000 DSP
  High dynamic range for numeric calculation
  Usually more expensive
Integer / Fixed-Point Processors
  Fixed-Point Arithmetic Unit
  Almost all embedded controllers are fixed point machines
  Examples: all microcontroller families, e.g. Freescale S12X, Infineon C166, Texas Instruments MSP430, Atmel AVR
  Lowest price per MIPS
Notes: <number>

## Slide 4: Standard IEEE-754 Single Precision Floating-Point
s
eeeeeeee
fffffffffffffffffffffff
0
31
30
23
22
23 bit mantissa (fraction)
8 bit exponent
1 bit sign
Advantage  Exponent gives large dynamic range
Disadvantage  Precision of a number depends on its exponent
Case 1: if e = 255 and f = 0, then v = NaN
Case 2: if e = 255 and f = 0, then v = [(-1)s]*infinity
Case 3: if 0 < e < 255, then v = [(-1)s]*[2(e-127)]*(1.f)
Case 4: if e = 0 and f = 0, then v = [(-1)s]*[2(-126)]*(0.f)
Case 5: if e = 0 and f = 0, then v = [(-1)s]*0
/
/

## Slide 5: Floating-Point does not solve everything!
Example: x = 10.0 (0x41200000)
+ y = 0.000000240 (0x3480D959)
z = 10.000000240
RIGHT?
WRONG!
You cannot represent 10.000000240 with
single-precision floating-point
0x412000000 = 10.000000000
10.000000240  can’t represent!
0x412000001 = 10.000001000
So z gets rounded down to 10.000000000

## Slide 6: Integer Numbering System Basics
Binary Numbers
01102 = (0*8)+(1*4)+(1*2)+(0*1) = 610
111102 = (1*16)+(1*8)+(1*4)+(1*2)+(0*1) = 3010
Two’s Complement Numbers
01102 = (0*-8)+(1*4)+(1*2)+(0*1) = 610
111102 = (1*-16)+(1*8)+(1*4)+(1*2)+(0*1) = -210

## Slide 7: Four-Bit Integer Multiplication
0100
x 1101
00000100
0000000
000100
+ 11100
11110100
Accumulator
Data Memory
11110100
4
x -3
-12
?
Is there another (superior) numbering system?

## Slide 8: Binary Fractions
1
0
1
1
•
-1
1/2
1/4
1/8
= -1 + 1/4 + 1/8 = -5/8
Fractions have the nice property that
fraction x fraction = fraction

## Slide 9: Four-Bit IQ - Multiplication
0100
x 1101
00000100
0000000
000100
11100
11110100
11110100
1/2
x - 3/8
-3/16
Accumulator
.
.
Data Memory
-1/4
1110
.

## Slide 10: Fractional Representation
S IIIIIIII
fffffffffffffffffffffff
0
31
32 bit mantissa
Advantage  Precision same for all numbers in an IQ format
Disadvantage  Limited dynamic range compared to Floating-Point
-2I + 2I-1 + … + 21 + 20 . 2-1 + 2-2 + … + 2-Q
“IQ” – Format
“I”  INTEGER – Fraction
“Q”  QUOTIENT – Fraction

## Slide 11: IQ - Examples
S fff
0
3
Most negative decimal number: -1.0 = 1.000 B
Most positive decimal number: + 0.875 = 0.111 B
Smallest negative decimal number: -1*2-3 (-0.125) = 1.111 B
Smallest positive decimal number: 2-3 (+0.125) = 0.001 B
I1Q3 – Format:
Range: -1.0 …. 0.875 ( + 1.0)
Resolution: 2-3

## Slide 12: IQ - Examples
SII f
0
3
Most negative decimal number: -4.0 = 100.0 B
Most positive decimal number: + 3.5 = 011.1 B
Smallest negative decimal number: -1 * 2-1 (- 0.5) = 111.1 B
Smallest positive decimal number: 2-1 (+0.5) = 000.1 B
I3Q1 – Format:
Range: -4.0 …. +3.5 ( + 4.0)
Resolution: 2-1

## Slide 13: IQ - Examples
S fff ffff ffff ffff ffff ffff ffff ffff
0
31
Most negative decimal number: -1.0
1.000 0000 0000 0000 0000 0000 0000 0000 B
Most positive decimal number:  + 1.0
0.111 1111 1111 1111 1111 1111 1111 1111 B
Smallest negative decimal number: -1*2-31
1.111 1111 1111 1111 1111 1111 1111 1111 B
Smallest positive decimal number: 2-31
0.000 0000 0000 0000 0000 0000 0000 0001 B
I1Q31 – Format:
Range: -1.0 …. (+1.0)
Resolution: 2-31

## Slide 14: IQ - Examples
S III IIII ffff ffff ffff ffff ffff
0
31
Most negative decimal number: -128
1000 0000. 0000 0000 0000 0000 0000 0000 B
Most positive decimal number:  + 128
0111 1111. 1111 1111 1111 1111 1111 1111 B
Smallest negative decimal number: -1*2-24
1111 1111. 1111 1111 1111 1111 1111 1111 B
Smallest positive decimal number: 2-24
0000 0000. 0000 0000 0000 0000 0000 0001 B
I8Q24 – Format:
Range: -128 …. (+128)
Resolution: 2-24

## Slide 15: IQ-Math can do better!
I8Q24 Example: x = 10.0 (0x0A000000)
+ y = 0.000000240 (0x00000004)
z = 10.000000240 (0x0A000004)
Exact Result (this example)

## Slide 16: How is a fraction coded?
~ 1
0
–½
–1
½
Fractions
~ 32K
0
–16K
–32K
16K
Integers
7FFF
0000
C000
8000
4000
Hex
void main(void) {
int coef = 32768 * 707 / 1000;
}

*32768
Example: represent the fraction number 0.707
Notes: <number>
How do we represent fractions in the DSP?
MOV ACC, #0.7
The assembler understands only integer values. Fractions must be normalized to be used in assembly code.
Ways to introduce fractions into assembly code and C code are shown. Remember, the 32768 represents the largest integer value in a 16 bit system. Thus, 32K times a fraction will yield a number which represents that fraction.
[DSP27]The assembler simply doesn't support mixed-type math (int and float) in expression analysis. Never has.
What I explained before was a different way to solve this problem which the assembler does support. Starting with version 6.65, the assembler expression analyzer allows you to write expressions with intermediate results much bigger than 16-bits signed. The final result of the expression still has to fit in 16-bits, but any intermediate step can be as big as 128-bits signed, which is an insanely huge number.
That means you can write your example below as ...
x .word (234 * 454)/10000
and get exactly what you want.

## Slide 17: Fractional vs. Integer
Range
  Integers have a maximum range determined by the number of bits
  Fractions have a maximum range of ±1
Precision
  Integers have a maximum precision of 1
  Fractional precision is determined by the number of bits

## Slide 18: Lab4: Fixed-point and Floating-point
Benchmark Multiply Operation
k = i * i
Test setup:
Integer multiply operation
Floating-Point multiply by Floating-Point Library
Floating-Point multiply by Floating-Point Hardware unit
 | Fixed-point | Floating-Point-Library | Floating-Point-Hardware
code size (words) | 3 | 89 | 9
clock cycles (6.67 ns) | 3 | 112 | 5
Benchmark result: