## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 6: Interrupt System F2833x
Digital Signal Controller
TMS320F2833x

## Slide 2: F2833x Core Interrupt Lines
F2833x
CORE
2 non-maskable interrupts (RS, “selectable” NMI)
14 maskable interrupts (INT1 – INT14)
INT1
INT2
INT3
INT4
INT5
INT6
INT7
INT8
INT9
INT10
INT11
INT12
INT13
INT14
RS
NMI

## Slide 3: F2833x Reset Sources
Watchdog Timer
RS pin active
To RS pin
RS
F2833x Core

## Slide 4: Reset – Bootloader
Reset
OBJMODE = 0 AMODE = 0
ENPIE = 0 INTM = 1
Boot determined by state of GPIO pins
Reset vector fetched from boot ROM
0x3F FFC0
Execution Bootloading
Entry Point Routines
FLASH SCI-A / SPI-A
M0 SARAM I2C
OTP eCAN-A
XINTF McBSP-A
GPIO / XINTF
Bootloader sets
OBJMODE = 1
AMODE = 0

## Slide 5: Bootloader Options
1 1 1 1 jump to FLASH address 0x33 FFF6
1 1 1 0 bootload code to on-chip memory via SCI-A
1 1 0 1 bootload external EEPROM to on-chip memory via SPI-A
1 1 0 0 bootload external EEPROM to on-chip memory via I2C
1 0 1 1 Call CAN Boot to load from eCAN-A mailbox 1
1 0 1 0 bootload code to on-chip memory via McBSP-A
1 0 0 1 jump to XINTF Zone 6 address 0x10 0000 for 16-bit data
1 0 0 0 jump to XINTF Zone 6 address 0x10 0000 for 32-bit data
0 1 1 1 jump to OTP address 0x38 0400
0 1 1 0 bootload code to on-chip memory via GPIO port A (parallel)
0 1 0 1 bootload code to on-chip memory via XINTF (parallel)
0 1 0 0 jump to M0 SARAM address 0x00 0000
0 0 1 1 branch to check boot mode
0 0 1 0 branch to Flash without ADC calibration (TI debug only)
0 0 0 1 branch to M0 SARAM without ADC calibration (TI debug only)
0 0 0 0 branch to SCI-A without ADC calibration (TI debug only)
87 /
XA15
86 /
XA14
85 /
XA13
84 /
XA12
GPIO pins

## Slide 6: Reset Code Flow - Summary
M0 SARAM (1Kw)
FLASH (256Kw)
OTP (1Kw)
0x33 FFF6
0x38 0400
0x30 0000
0x00 0000
0x3F E000
0x3F FFC0
Boot ROM (8Kw)
BROM vector (64w)
0x3F F9CE
Boot Code




RESET
Execution Entry
Point Determined
By GPIO Pins
Bootloading
Routines
(SCI-A, SPI-A, I2C, eCAN-A, McBSP-A GPIO, XINTF)
0x3F F9CE
XINTF Zone 6 (x16 / x32) 0x10 0000
0x00 0000

## Slide 7: Register Bits Initialized at Reset
Register bits defined by reset
PC 0x3F FFC0 PC loaded with reset vector
ACC 0x0000 0000 Accumulator cleared
XAR0 - XAR7 0x0000 0000 Auxiliary Registers
DP 0x0000 Data Page pointer points to page 0
P 0x0000 0000 P register cleared
XT 0x0000 0000 XT register cleared
SP 0x0400 Stack Pointer to address 0400
RPC 0x00 0000 Return Program Counter cleared
IFR 0x0000 no pending interrupts
IER 0x0000 maskable interrupts disabled
DBGIER 0x0000 debug interrupts disabled

## Slide 8: Control Bits Initialized at Reset
Status Register 0 (ST0)
SXM = 0 Sign extension off
OVM = 0 Overflow mode off
TC = 0 test/control flag
C = 0 carry bit
Z = 0 zero flag
Status Register 1 (ST1)
INTM = 1 Disable all maskable interrupts - global
DBGM = 1 Emulation access/events disabled
PAGE0 = 0 Stack addressing mode enabled/Direct addressing disabled
VMAP = 1 Interrupt vectors mapped to PM 0x3F FFC0 – 0x3F FFFF
SPA = 0 stack pointer even address alignment status bit
LOOP = 0 Loop instruction status bit
EALLOW = 0 emulation access enable bit
IDLESTAT = 0 Idle instruction status bit
AMODE = 0 C27x/C28x addressing mode
OBJMODE = 0 C27x object mode
M0M1MAP = 1 mapping mode bit
XF = 0 XF status bit
ARP = 0 ARP points to AR0
N = 0 negative flag
V = 0 overflow bit
PM = 000 set to left-shift-by-1
OVC = 00 0000 overflow counter

## Slide 9: Interrupt Sources
ePWM, eCAP, eQEP, ADC, SCI, SPI, I2C, eCAN,
McBSP, DMA, WD
Internal Sources
External Sources
XINT1 – XINT7
TZx
XRS
XNMI_XINT13
NMI
F2833x CORE
INT1
INT13
INT2
INT3
INT12
INT14
XRS
•
•
•
PIE
(Peripheral
Interrupt
Expansion)
TINT2
TINT1
TINT0

## Slide 10: Maskable Interrupt Processing Conceptual Core Overview
A valid signal on a specific interrupt line causes the latch to display a “1” in the appropriate bit
1
0
1
(IFR)
“Latch”
INT1
INT2
INT14
Core
Interrupt
F2833x
Core
(INTM)
“Global Switch”
(IER)
“Switch”
If the individual and global switches are turned “on” the interrupt reaches the core

## Slide 11: Interrupt Flag Register (IFR)
RTOSINT
DLOGINT
INT14
INT13
INT12
INT11
INT10
INT9
8
9
10
11
12
13
14
15
INT8
INT7
INT6
INT5
INT4
INT3
INT2
INT1
0
1
2
3
4
5
6
7
Pending : IFR Bit = 1
Absent : IFR Bit = 0
Compiler generates atomic instructions (non-interruptible) for setting/clearing IFR
If interrupt occurs when writing IFR, interrupt has priority
IFR(bit) cleared when interrupt is acknowledged by CPU
Register cleared on reset
/*** Manual setting/clearing IFR ***/
extern cregister volatile unsigned int IFR;
IFR |= 0x0008; //set INT4 in IFR
IFR &= 0xFFF7; //clear INT4 in IFR
Notes: <number>

## Slide 12: Interrupt Enable Register (IER)
RTOSINT
DLOGINT
INT14
INT13
INT12
INT11
INT10
INT9
8
9
10
11
12
13
14
15
INT8
INT7
INT6
INT5
INT4
INT3
INT2
INT1
0
1
2
3
4
5
6
7
Enable: Set IER Bit = 1
Disable: Clear IER Bit = 0
Compiler generates atomic instructions (non-interruptible) for setting/clearing IER
Register cleared on reset
/*** Interrupt Enable Register ***/
extern cregister volatile unsigned int IER;
IER |= 0x0008; //enable INT4 in IER
IER &= 0xFFF7; //disable INT4 in IER
Notes: <number>

## Slide 13: Interrupt Global Mask Bit
INTM used to globally enable/disable interrupts:
  Enable: INTM = 0
  Disable: INTM = 1 (reset value)
INTM modified from assembly code only:
INTM
ST1
Bit 0
/*** Global Interrupts ***/
asm(“ CLRC INTM”); //enable global interrupts
asm(“ SETC INTM”); //disable global interrupts
Notes: <number>

## Slide 14: Peripheral Interrupt Expansion - PIE
Peripheral Interrupts 12x8 = 96
IFR
IER
INTM
28x
Core
28x Core Interrupt logic
PIE module for 96 Interrupts
INT1.x interrupt group
INT2.x interrupt group
INT3.x interrupt group
INT4.x interrupt group
INT5.x interrupt group
INT6.x interrupt group
INT7.x interrupt group
INT8.x interrupt group
INT9.x interrupt group
INT10.x interrupt group
INT11.x interrupt group
INT12.x interrupt group
INT1 – INT 12
12 Interrupts
96
INT1.1
INT1.2
INT1.8
1
0
1
•
•
•
•
•
•
INT1
PIEIFR1
PIEIER1
Interrupt Group 1
INT13 (TINT1 / XINT13)
INT14 (TINT2)
NMI

## Slide 15: PIE Registers
INTx.2
INTx.3
INTx.4
INTx.5
INTx.6
INTx.7
INTx.8
INTx.1
0
1
2
3
4
5
6
7
15 - 8
reserved
PIEIFRx register (x = 1 to 12)
INTx.2
INTx.3
INTx.4
INTx.5
INTx.6
INTx.7
INTx.8
INTx.1
0
1
2
3
4
5
6
7
15 - 8
reserved
PIEIERx register (x = 1 to 12)
reserved
PIEACKx
PIE Interrupt Acknowledge Register (PIEACK)
1
2
4
3
5
6
7
8
9
0
10
11
15 - 12
ENPIE
PIEVECT
PIECTRL register
0
15 - 1
#include “DSP2833x_Device.h”
PieCtrlRegs.PIEIFR1.bit.INTx4 = 1; //manually set IFR for XINT1 in PIE group 1
PieCtrlRegs.PIEIER3.bit.INTx5 = 1; //enable CAPINT1 in PIE group 3
PieCtrlRegs.PIEACK.all = 0x0004; //acknowledge the PIE group 3
PieCtrlRegs.PIECTRL.bit.ENPIE = 1; //enable the PIE

## Slide 16: F2833x PIE Interrupt Assignment Table
INTx.8
INTx.7
INTx.6
INTx.5
INTx.4
INTx.3
INTx.2
INTx.1
INT1
WAKEINT
TINT0
ADCINT
XINT2
XINT1
SEQ2INT
SEQ1INT
INT2
EPWM6
_TZINT
EPWM5
_TZINT
EPWM4
_TZINT
EPWM3
_TZINT
EPWM2
_TZINT
EPWM1
_TZINT
INT3
EPWM6
_INT
EPWM5
_INT
EPWM4
_INT
EPWM3
_INT
EPWM2
_INT
EPWM1
_INT
INT4
ECAP6
_INT
ECAP5
_INT
ECAP4
_INT
ECAP3
_INT
ECAP2
_INT
ECAP1
_INT
INT5
EQEP2
_INT
EQEP1
_INT
INT6
MXINTA
MRINTA
MXINTB
MRINTB
SPITXINTA
SPIRXINTA
INT7
DINTCH6
DINTCH5
DINTCH4
DINTCH3
DINTCH2
DINTCH1
INT8
SCITXINTC
SCIRXINTC
I2CINT2A
I2CINT1A
INT9
ECAN1
_INTB
ECAN0
_INTB
SCITXINTB
SCIRXINTB
SCITXINTA
SCIRXINTA
INT10
INT11
INT12
LUF
LVF
XINT7
XINT6
XINT5
XINT4
XINT3
ECAN0
_INTA
ECAN1
_INTA

## Slide 17: Default Interrupt Vector Table at Reset
Vector Offset
Memory
0
BROM Vectors 64w
ENPIE = 0
0x3F FFC0
0x3F FFFF
PIE Vectors 256w
0x00 0D00
DATALOG
RTOSINT
EMUINT
NMI
02
04
06
08
0A
0C
0E
10
12
14
16
18
1A
1C
1E
20
22
24
26
28-3E
ILLEGAL
USER 1-12
INT1
INT2
INT3
INT4
INT5
INT6
INT7
INT8
INT9
INT10
INT11
INT12
INT13
INT14
RESET
00
Default Vector Table
Re-mapped when
ENPIE = 1
PieVectTableInit{ }
Used to initialize PIE vectors
Notes: <number>

## Slide 18: PIE Vector Mapping (ENPIE = 1)
PIE vector location – 0x00 0D00 – 256 words in data memory
RESET and INT1-INT12 vector locations are re-mapped
CPU vectors are re-mapped to 0x00 0D00 in data memory
INT13 0x00 0D1A XINT13 Interrupt or CPU Timer 1 (RTOS)
INT14 0x00 0D1C CPU Timer 2 (RTOS)
DATALOG 0x00 0D1D CPU Data logging Interrupt
…… …… ……
USER12 0x00 0D3E User-defined Trap
INT1.1 0x00 0D40 PIEINT1.1 Interrupt Vector
…… …… ……
…… …… ……
INT12.1 0x00 0DF0 PIEINT12.1 Interrupt Vector
INT1.8 0x00 0D4E PIEINT1.8 Interrupt Vector
INT12.8 0x00 0DFE PIEINT12.8 Interrupt Vector
…… …… ……
PIE vector address PIE vector Description
not used 0x00 0D00 Reset vector (never fetched here)
Vector name
INT1 0x00 0D02 INT1 re-mapped to PIE group below
…… …… …… re-mapped to PIE group below
INT12 0x00 0D18 INT12 re-mapped to PIE group below

## Slide 19: Device Vector Mapping - Summary
_c_int00:
. . .
CALL main()
main()
{ initialization();
. . .
}
Initialization()
{
Load PIE Vectors
Enable the PIE
Enable PIEIER
Enable Core IER
Enable INTM
}
PIE Vector Table
256 Word RAM
0x00 0D00 – 0DFF
RESET
<0x3F FFC0>
Reset Vector <0x3F F9A9> = Boot Code
Flash Entry Point <0x33 FFF6 > = LB _c_int00
User Code Start < _c_int00 >

## Slide 20: Interrupt Response - Hardware Sequence
Note: some actions occur simultaneously, none are interruptible
CPU Action Description
T ST0
AH AL
PH PL
AR1 AR0
DP ST1
DBSTAT IER
PC(msw) PC(lsw)
Registers  stack 14 Register words auto saved
0  IFR (bit) Clear corresponding IFR bit
0  IER (bit) Clear corresponding IER bit
1  INTM/DBGM Disable global ints/debug events
Vector  PC Loads PC with int vector address
Clear other status bits Clear LOOP, EALLOW, IDLESTAT
Notes: <number>
LOOP: Use in LOOPZ and LOOPNZ instructions. This bit is set when the instruction is still active.
EALLOW: Emulation allow. This bit is set to allow retime debugger feature.
IDLESTAT: Another bit use in emulation.

## Slide 21: Interrupt Latency
Latency
Depends on wait states, ready, INTM, etc.
Maximum latency:
Recognition delay (3) and SP alignment (1)
4
Minimum latency (to when real work occurs in the ISR):
Internal interrupts: 14 cycles
External interrupts: 16 cycles
Get vector (3 reg. pairs saved)
3
PF1/PF2/D1 of ISR instruction (3 reg. pairs saved)
3
Save return address
1
D2/R1/R2 of ISR instruction
3
Sync ext. signal
(ext. interrupt only)
2
cycles
Above is for PIE enabled or disabled
Assumes ISR in internal RAM
Internal interrupt occurs here
ext. interrupt occurs here
ISR instruction executed on next cycle
Notes: <number>

## Slide 22: F2833x CPU Timers
RESET
Timer Reload
SYSCLKOUT
TCR.4
16 - Bit divide down
TDDRH:TDDR
16 - Bit prescaler
PSCH:PSC
32 - Bit period
PRDH:PRD
32 - Bit counter
TIMH:TIM
BORROW
INT

## Slide 23: F2833x Timer Interrupt System
IFR
IER
INTM
28x
Core
28x Core Interrupt logic
PIE unit
INT1.7 interrupt
INT1
TINT1 / XINT13
TINT2
TINT0
INT13
INT14

## Slide 24: F2833x Timer Registers
Address Register Name
0x0000 0C00 TIMER0TIM Timer 0, Counter Register Low
0x0000 0C01 TIMER0TIMH Timer 0, Counter Register High
0x0000 0C02 TIMER0PRD Timer 0, Period Register Low
0x0000 0C03 TIMER0PRDH Timer 0, Period Register High
0x0000 0C04 TIMER0TCR Timer 0, Control Register
0x0000 0C06 TIMER0TPR Timer 0, Prescaler Register
0x0000 0C07 TIMER0TPRH Timer 0, Prescaler Register High
0x0000 0C08 TIMER1TIM Timer 1, Counter Register Low
0x0000 0C09 TIMER1TIMH Timer 1, Counter Register High
0x0000 0C0A TIMER1PRD Timer 1, Period Register Low
0x0000 0C0B TIMER1PRDH Timer 1, Period Register High
0x0000 0C0C TIMER1TCR Timer 1, Control Register
0x0000 0C0D TIMER1TPR Timer 1, Prescaler Register
0x0000 0C0F TIMER1TPRH Timer 1, Prescaler Register High
0x0000 0C10 to 0C17 Timer 2 Registers ; same layout as above

## Slide 25: F2833x Timer Control Registers TIMERxTCR
Emulator Interaction
1x = run free
0
reserved
TRB
1
2
3
4
5
6
7
reserved
reserved
TSS
reserved
reserved
reserved
TIE
reserved
FREE
8
9
10
11
12
13
14
15
reserved
SOFT
reserved
reserved
TIF
Timer Stop Status
0 = start / 1 = stop
Timer Reload Bit
1 = reload
Timer Interrupt Flag
Write 1 clear bit
Timer Interrupt Enable
Write 1 to enable INT