## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 8: Analogue Digital Converter F2833x
Digital Signal Controller
TMS320F2833x

## Slide 2: ADC Module
12-bit resolution Analogue to Digital Converter
Sixteen analog input channels, voltage range 0…3V
Equation:
  Vin = Analogue input voltage, range 0…3V
  Vref+ = 3.0V Vref- = 0V n = 12
  D = digital result, 12 Bit resolution
Maximum Conversion Rate: 12.5 MSPS (80 ns)
Two analog input multiplexers / two sample/hold units
Sequential and simultaneous sampling modes
Auto sequencing capability - up to 16 auto conversions
Sixteen individually addressable result registers
Trigger sources for start-of-conversion
  External trigger, S/W or ePWM - Modules
Notes: <number>

## Slide 3: ADC Operating Modes
Sequencer Mode:
  Cascaded Sequencer Mode (16 states)
  Dual Sequencer Mode (2 x 8 states)
Sampling Mode:
  Sequential Sampling (1 channel at a time)
  Simultaneous Sampling (2 channels at a time)
Start Mode:
  Single Sequence Mode (stop at end of sequence)
  Continuous Mode (wrap sequencer at end of sequence)

## Slide 4: ADC Sequencer in Cascaded Mode
12-bit A/D
Converter
SOC
EOC
Software
ADCINA0
ADCINA1
ADCINA7
ADCINB0
ADCINB1
ADCINB7
S/H
A
S/H
B
MUX
MUX
A
RESULT0
RESULT1
RESULT2
RESULT15
Result
MUX
ePWM_SOC_A
ePWM_SOC_B
MUX
B
Ch Sel (CONV00)
Ch Sel (CONV01)
Ch Sel (CONV02)
Ch Sel (CONV03)
Ch Sel (CONV15)
MAX_CONV1
Autosequencer
Start Sequence
Trigger
SEQ1
ADC full-scale input range is 0 to 3V
External Pin
(GPIO/XINT2_ADCSOC)
Notes: <number>

## Slide 5: ADC Sequencer in Dual - Sequencer Mode
RESULT8
RESULT9
RESULT15
Result
MUX
RESULT0
RESULT1
RESULT7
Result
MUX
12-bit A/D
Converter
S/H
A
S/H
B
MUX
Software
ePWM_SOC_A
External Pin
SOC1/
EOC1
Sequencer
Arbiter
SOC2/
EOC2
Software
ePWM_SOC_B
ADCINA0
ADCINA1
ADCINA7
ADCINB0
ADCINB1
ADCINB7
MUX
A
MUX
B
MUX
MUX
Ch Sel (CONV00)
Ch Sel (CONV01)
Ch Sel (CONV07)
MAX_CONV1
Autosequencer
Start Sequence
Trigger
SEQ1
(GPIO/XINT2_ADCSOC)
Ch Sel (CONV08)
Ch Sel (CONV09)
Ch Sel (CONV15)
MAX_CONV2
Autosequencer
Start Sequence
Trigger
SEQ2
Notes: <number>

## Slide 6: F2833x ADC Clock Diagram
CLKIN
(30 MHz)
HSPCLK
(150 MHz)
ADCCLKPS
bits
ADCTRL3
0110b
FCLK
(12.5 MHz)
FCLK = HSPCLK/(2*ADCCLKPS)
ADCCLK =
FCLK/(CPS+1)
ADCCLK
(12.5 MHz)
CPS bit
ADCTRL1
0b
To ADC pipeline
sampling window
ACQ_PS
bits
ADCTRL1
0111b
SYSCLKOUT
(150 MHz)
PLLSTS
DIVSEL
bits
10b (/2)
To CPU
sampling window = (ACQ_PS + 1)*(1/ADCCLK)
PCLKCR0.ADCENCLK = 1
HISPCP
HSPCLK
bits
000b (/1)
PLLCR
DIV
bits
1010b (x10)
Note: Maximum F2833x ADCCLK is 25 MHz, but INL (integral nonlinearity error) is greater above 12.5 MHz. See the device datasheet (SPRU812A) for more information.
Notes: <number>

## Slide 7: Analog-to-Digital Converter Registers
ADCTRL1 ADC Control Register 1
ADCTRL2 ADC Control Register 2
ADCTRL3 ADC Control Register 3
ADCMAXCONV ADC Maximum Conversion Channels Register
ADCCHSELSEQ1 ADC Channel Select Sequencing Control Register 1
ADCCHSELSEQ2 ADC Channel Select Sequencing Control Register 2
ADCCHSELSEQ3 ADC Channel Select Sequencing Control Register 3
ADCCHSELSEQ4 ADC Channel Select Sequencing Control Register 4
ADCASEQSR ADC Autosequence Status Register
ADCRESULT0 ADC Conversion Result Buffer Register 0
ADCRESULT1 ADC Conversion Result Buffer Register 1
ADCRESULT2 ADC Conversion Result Buffer Register 2
ADCRESULT14 ADC Conversion Result Buffer Register 14
ADCRESULT15 ADC Conversion Result Buffer Register 15
ADCREFSEL ADC Reference Select Register
ADCOFFTRIM ADC Offset Trim Register
ADCST ADC Status and Flag Register
Register Description
Notes: <number>

## Slide 8: ADC Control Register 1
Emulation Suspend Mode
00 = free run (do not stop)
01 = stop after current sequence
10 = stop after current conversion
11 = stop immediately
ADC Module Reset
0 = no effect
1 = reset (set back to 0
by ADC logic)
Acquisition Time Prescale (S/H)
ACQ Window = (ACQ_PS + 1)*(1/ADCCLK)
SUSMOD
ACQ_PS
CPS
7
RESET
15
reserved
11 - 8
13 - 12
14
Conversion Prescale
0: ADCCLK = FCLK / 1
1: ADCCLK = FCLK / 2
Upper Register:
Structure Variable in C: AdcRegs.ADCTRL1
Notes: <number>

## Slide 9: ADC Control Register 1
Sequencer Mode
0 = dual mode
1 = cascaded mode
Continuous Run
0 = stops after reaching
end of sequence
1 = continuous (starts all over
again from “initial state”)
Sequencer Override
(functions only if CONT_RUN = 1)
0 = sequencer pointer resets to “initial state” at end of MAX_CONVn
1 = sequencer pointer resets to “initial state” after “end state”
SEQ_OVRD
SEQ_CASC
3 - 0
CONT_RUN
reserved
4
5
6
Lower Register:
Structure Variable in C: AdcRegs.ADCTRL1
Notes: <number>

## Slide 10: ADC Control Register 2
Interrupt Enable (SEQ1)
0 = interrupt disable
1 = interrupt enable
ePWM SOC B
(cascaded mode only)
0 = no action
1 = start by ePWM
signal
Reset SEQ1
0 = no action
1 = immediate reset
SEQ1 to “initial state”
Start Conversion (SEQ1)
0 = clear pending SOC trigger
1 = software trigger-start SEQ1
ePWM SOC A
SEQ1 Mask Bit
0 = cannot be started
by ePWM trigger
1 = can be started
by ePWM trigger
Interrupt Mode (SEQ1)
0 = interrupt every EOS
1 = interrupt every other EOS
RST_SEQ1
9
ePWM_SOCB
_SEQ
12
reserved
11
15
SOC_SEQ1
INT_ENA
_SEQ1
INT_MOD
_SEQ1
reserved
ePWM_SOCA
_SEQ1
8
14
13
10
Upper Register:
Structure Variable in C: AdcRegs.ADCTRL2
Notes: <number>

## Slide 11: ADC Control Register 2
Interrupt Enable (SEQ2)
0 = interrupt disable
1 = interrupt enable
External SOC (SEQ1)
0 = no action
1 = start by signal from
ADCSOC pin
Start Conversion (SEQ2)
(dual-sequencer mode only)
0 = clear pending SOC trigger
1 = software trigger-start SEQ2
ePWM SOC B
SEQ2 Mask Bit
0 = cannot be started
by ePWM trigger
1 = can be started
by ePWM trigger
Interrupt Mode (SEQ2)
0 = interrupt every EOS
1 = interrupt every other EOS
RST_SEQ2
1
EXT_SOC
_SEQ1
4
reserved
3
7
SOC_SEQ2
INT_ENA
_SEQ2
INT_MOD
_SEQ2
reserved
ePWM_SOCB
_SEQ2
0
6
5
2
Lower Register:
Reset SEQ2
0 = no action
1 = immediate reset
SEQ2 to “initial state”
Structure Variable in C: AdcRegs.ADCTRL2
Notes: <number>

## Slide 12: ADC Control Register 3
Sampling Mode Select
0 = sequential sampling mode
1 = simultaneous sampling mode
ADC Clock Prescale
0 : FCLK = HSPCLK
1 to F : FCLK = HSPCLK / (2*ADCCLKPS)
ADC Bandgap and Reference Power Down
00 = powered down
11 = powered up
ADC Power Down
(except Bandgap & Ref.)
0 = powered down
1 = powered up
ADCBGRFDN
ADCCLKPS
SMODE_SEL
0
15 - 8
reserved
4 - 1
7 - 6
ADCPWDN
5
Structure Variable in C: AdcRegs.ADCTRL3

## Slide 13: Maximum Conversion Channels Register
Bit fields define the number of conversions per trigger (binary+1)
Each sequencer starts at the “initial state” and advances sequentially
Each will wrap at the “end state” unless software resets it sooner
MAX_
CONV 2_2
MAX_
CONV 2_1
MAX_
CONV 2_0
MAX_
CONV 1_3
MAX_
CONV 1_2
MAX_
CONV 1_1
MAX_
CONV 1_0
reserved
Cascaded Mode
Dual Mode
SEQ2
SEQ1
SEQ1 SEQ2 Cascaded
Initial state CONV00 CONV08 CONV00
End state CONV07 CONV15 CONV15
0
1
2
3
4
5
6
15-7
Structure Variable in C: AdcRegs.ADCMAXCONV

## Slide 14: ADC Input Channel Select Sequencing Control Register
ADCCHSELSEQ1
15 - 12 11 - 8 7 - 4 3 - 0
CONV03 CONV02 CONV01 CONV00
ADCCHSELSEQ2
CONV07 CONV06 CONV05 CONV04
ADCCHSELSEQ3
CONV11 CONV10 CONV09 CONV08
ADCCHSELSEQ4
CONV15 CONV14 CONV13 CONV12
Structure Variable in C: AdcRegs.ADCCHSELSEQ1 … AdcRegs.ADCCHSELSEQ4
ADC input channels are binary counted:
ADCINA0 = 0000 ADCINB0 = 1000
ADCINA1 = 0001 ….
… ADCINB7 = 1111

## Slide 15: Example - Sequencer “Start/Stop” Operation
Configuration Requirements:
ePWM triggers the ADC
  Three auto conversions (V1, V2, V3) off trigger 1 (CTR = 0)
  Three auto conversions (I1, I2, I3) off trigger 2 (CTR = PRD)
ADC in cascaded sequencer and sequential sampling modes
V1, V2, V3
I1, I2, I3
V1, V2, V3
I1, I2, I3
ePWM
Time Base
Counter
ePWM
Output

## Slide 16: Example - Sequencer “Start/Stop” Operation
MAX_CONV1 is set to 2 and Channel Select Sequencing Control Registers are set to:
Once reset and initialized, SEQ1 waits for a trigger
First trigger, three conversions performed: CONV00 (V1), CONV01 (V2), CONV02 (V3)
SEQ1 waits for second trigger
Second trigger, three conversions performed: CONV03 (I1), CONV04 (I2), CONV05 (I3)
End of second sequence, ADC Results registers have the following values:
SEQ1 waits at current state for another trigger
ISR to read results and reset SEQ1
Bits  15-12 11-8 7-4 3-0
I1 V3 V2 V1 ADCCHSELSEQ1
x x I3 I2 ADCCHSELSEQ2
RESULT0 V1
RESULT1 V2
RESULT2 V3
RESULT3 I1
RESULT4 I2
RESULT5 I3

## Slide 17: ADC Conversion Result Registers
Input Digital AdcRegs. ADCRESULTx AdcMirror. ADCRESULTx
Voltage Result
3.0 0xFFF 1111|1111|1111|0000 0000|1111|1111|1111
1.5 0x7FF 0111|1111|1111|0000 0000|0111|1111|1111
0.00073 1 0000|0000|0001|0000 0000|0000|0000|0001
0 0 0000|0000|0000|0000 0000|0000|0000|0000
LSB
MSB
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
LSB
MSB
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
AdcRegs.ADCRESULTx, x = 0 - 15 (2 wait-state read)
AdcMirror.ADCRESULTx, x = 0 - 15 (0 wait-state read)
Notes: <number>

## Slide 18: How Can We Handle Signed Input Voltages?
Example: -1.5 V  Vin  +1.5 V
1) Add 1.5 volts to the analog input
Vin
1.5V
ADCINx
GND
ADCLO
-
+
R
R
R
-
+
R
R
C28x
#include “DSP2833x_Device.h”
#define offset 0x07FF
void main(void)
{
int16 value; // signed
value = AdcMirror.ADCRESULT0 – offset;
}
2) Subtract “1.5” from the digital result

## Slide 19: ADC Reference Selection
The F28335 ADC has an internal reference with temperature stability of ~50 PPM/°C *
As an option one can use an external reference device
  External reference choices: 2.048 V, 1.5 V, 1.024 V
  The reference value DOES NOT change the 0 - 3 V full-scale range of the ADC
The ADCREFSEL register controls the reference choice
13 - 0
reserved
15 - 14
REF_SEL
ADC Reference Selection
00 = internal (default)
01 = external 2.048 V
10 = external 1.5 V
11 = external 1.024 V
Structure Variable in C: AdcRegs.ADCREFSEL

## Slide 20: Lab 8_1: Dual AD - Conversion
Objective:
AD-Conversion of ADCIN_A0 and ADCIN_A1
Sampling frequency generated by ePWM2: 50kHz
ADCIN_A0 and ADCIN_A1 are connected to two variable resistors VR1, VR2 at Peripheral Explorer Board.
VR1 and VR2 voltage range: 0 Volt to 3.3 Volt
Automatic start of ADC by ePWM2 period event
ADC-Interrupt Service Routine to read out the ADC results
main loop to alternately show the results of ADCINA0 or ADCINA1 at 4 LEDs (LD1, LD2, LD3 and LD4) of the Peripheral Explorer Board as a “light-beam”.

## Slide 21: Additional Registers used in Lab8_1:
  ePWM2 Time Base Control : TBCTL
  ePWM2 Time Base Period : TBPRD
  ePWM2 Time Base Counter : TBCNT
  ePWM2 Event Trigger Prescale : ETPS
  ePWM2 Event Trigger Select : ETSEL
  ADC – Control 1 : ADCTRL1
  ADC – Control 2 : ADCTRL2
  ADC – Control 3 : ADCTRL3
  Channel Select Sequencer 1 : ADCCHSELSEQ1
  Max. number of conversions : ADCMAXCONV
  ADC - Result 0 : ADCRESULT0
  ADC - Result 1 : ADCRESULT1

## Slide 22: Optional Lab8_2
Modify Lab 6 (“4 – bit Counter”):
  use the Analogue Input ADCIN0 to change
  the counter speed
  use a LED-frequency range between 50Hz and 1 Hz
  use (1) a linear or (2) a logarithm scale
  between Fmin and Fmax.