## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 10: Serial Peripheral Interface F2833x
Digital Signal Controller
TMS320F2833x

## Slide 2: SPI Data Flow
SPI Shift Register
SPI Shift Register
SPI Device #1 - Master
SPI Device #2 - Slave
Simultaneous transmits and receive
SPI Master provides the clock signal
shift
shift
clock

## Slide 3: SPI Block Diagram
SPIRXBUF.15-0
SPIDAT.15-0
SPICLK
SPISOMI
SPISIMO
LSPCLK
baud
rate
clock
polarity
clock
phase
C28x - SPI Master Mode Shown
SPITXBUF.15-0
LSB
MSB
TX FIFO_0
TX FIFO_15
RX FIFO_0
RX FIFO_15

## Slide 4: SPI Data Character Justification
Programmable data length of 1 to 16 bits
Transmitted data of less than 16 bits must be left justified
  MSB transmitted first
Received data of less than 16 bits are right justified
User software must mask-off unused MSB’s
11001001XXXXXXXX
XXXXXXXX11001001
SPIDAT – Device #1
SPIDAT - Device #2

## Slide 5: SPI-A Registers
Address Register Name
0x007040 SPICCR SPI-A configuration control register
0x007041 SPICTL SPI-A operation control register
0x007042 SPISTS SPI-A status register
0x007044 SPIBRR SPI-A baud rate register
0x007046 SPIRXEMU SPI-A receive emulation buffer register
0x007047 SPIRXBUF SPI-A serial receive buffer register
0x007048 SPITXBUF SPI-A serial transmit buffer register
0x007049 SPIDAT SPI-A serial data register
0x00704A SPIFFTX SPI-A FIFO transmit register
0x00704B SPIFFRX SPI-A FIFO receive register
0x00704C SPIFFCT SPI-A FIFO control register
0x00704F SPIPRI SPI-A priority control register

## Slide 6: SPI-A Configuration Control Register SPICCR @ 0x007040
0
1
2
7
6
5-4
reserved
SPI CHAR.3-0
character length = number + 1
e.g. 0000b  length = 1
1111b  length = 16
SPI SW RESET
0 = SPI flags reset
1 = normal operation
CLOCK POLARITY
0 = rising edge data transfer
1 = falling edge data transfer
reserved
15-8
3

## Slide 7: SPI-A Operation Control Register SPICTL @ 0x007041
0
1
2
15-5
4
3
reserved
CLOCK PHASE
0 = no CLK delay
1 = CLK delayed 1/2 cycle
OVERRUN INT ENABLE
0 = disabled
1 = enabled
MASTER/SLAVE
0 = slave
1 = master
TALK
0 = transmission disabled,
SPISIMO at high impedance
1 = transmission enabled
SPI INT ENABLE
0 = disabled
1 = enabled
Notes: <number>

## Slide 8: SPI-A Baud Rate Register SPIBRR @ 0x007044
15-7
6-0
reserved
SPI BIT RATE
SPICLK signal =
LSPCLK
(SPIBRR + 1)
LSPCLK
4
, SPIBRR = 3 to 127
, SPIBRR = 0, 1, or 2
Need to set this only when in master mode!
Notes: <number>

## Slide 9: SPI-A Status Register SPISTS @ 0x007042
7
6
4-0
SPI INT FLAG (read only)
Set to 1 when transfer completed
Interrupt requested if SPI INT ENA
bit set (SPICTL.0)
Cleared by reading SPIBRXUF
RECEIVER OVERRUN (read/clear only)
Set to 1 if next reception completes before SPIRXBUF read
Interrupt requested if OVERRUN INT ENA bit set (SPICTL.4)
Cleared by writing a 1
reserved
reserved
15-8
TX BUF FULL (read only)
Set to 1 when char written
to SPITXBUF
Cleared when char in SPIDAT
5
Notes: <number>

## Slide 10: SPI-A FIFO Transmit Register SPIFFTX @ 0x00704A
0
TXFFIL2
SPIFFEN
TXFFST0
TXFFST3
TXFFIEN
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
TXFFIL0
TXFFIL1
TXFFIL4
TXFFIL3
TXFFST1
TXFFINT
CLR
TXFFST2
TXFFINT
TXFFST4
TXFIFO
RESET
reserved
TX FIFO Status (read-only)
00000 TX FIFO empty
00001 TX FIFO has 1 word
00010 TX FIFO has 2 words
00011 TX FIFO has 3 words
10000 TX FIFO has 16 words
.
.
.
.
.
.
.
.
.
TX FIFO Interrupt Level
Interrupt when TXFFST4-0
and TXFFIL4-0 match
SPI FIFO
Enhancements
0 = disable
1 = enable
TX FIFO Reset
0 = reset (pointer to 0)
1 = enable operation
TX FIFO
Interrupt
(on match)
Enable
0 = disable
1 = enable
TX FIFO
Interrupt
Flag (read-only)
0 = not occurred
1 = occurred
TX FIFO
Interrupt
Flag Clear
0 = no effect
1 = clear

## Slide 11: SPI-A FIFO Receive Register SPIFFRX @ 0x00704B
0
RXFFIL2
RXFF-
OVF CLR
RXFFST0
RXFFST3
RXFFIEN
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
RXFFIL0
RXFFIL1
RXFFIL4
RXFFIL3
RXFFST1
RXFFINT
CLR
RXFFST2
RXFFINT
RXFFST4
RXFIFO
RESET
RXFF-
OVF
RX FIFO Status (read-only)
00000 RX FIFO empty
00001 RX FIFO has 1 word
00010 RX FIFO has 2 words
00011 RX FIFO has 3 words
10000 RX FIFO has 16 words
.
.
.
.
.
.
.
.
.
RX FIFO Interrupt Level
Interrupt when RXFFST4-0
and RXFFIL4-0 match
RX FIFO Reset
0 = reset (pointer to 0)
1 = enable operation
RX FIFO
Interrupt
(on match)
Enable
0 = disable
1 = enable
RX FIFO
Interrupt
Flag (read-only)
0 = not occurred
1 = occurred
RX FIFO
Interrupt
Flag Clear
0 = no effect
1 = clear
RX FIFO
Overflow
Flag (read-only)
0 = no overflow
1 = overflow
RX FIFO
Overflow
Flag Clear
0 = no effect
1 = clear

## Slide 12: SPI Summary
Provides synchronous serial communications
  Two wire transmit or receive (half duplex)
  Three wire transmit and receive (full duplex)
Software configurable as master or slave
  C28x provides clock signal in master mode
Data length programmable from 1-16 bits
125 different programmable baud rates