## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 14: Flash Programming F2833x
32-Bit-Digital Signal Controller
TMS320F2833x

## Slide 2: Startup Sequence from Flash Memory
0x33 FFF6
0x30 0000
0x3F F000
0x3F FFC0
Boot ROM (8Kw)
BROM vector (32w)
0x3F F9CE
Boot Code
RESET
0x3F F9CE
{SCAN GPIO}
FLASH (256Kw)
Passwords (8w)
_c_int00
LB
“rts2800_ml.lib”
“user” code sections
_c_int00
main ( )
{
}
2
3
4
5
1
……
……
……

## Slide 3: TMS320F28335 Flash Memory Map
Data & Program Space
Address Range
0x30 0000 – 0x30 7FFF
0x30 8000 – 0x30 FFFF
0x31 0000 – 0x31 7FFF
0x31 8000 – 0x31 FFFF
0x32 0000 – 0x32 7FFF
0x32 8000 – 0x32 FFFF
0x33 0000 – 0x33 7FFF
0x33 8000 – 0x33 FF7F
0x33 FF80 – 0x33 FFF5
0x33 FFF6 – 0x33 FFF7
0x33 FFF8 – 0x33 FFFF
Sector H; 32K x 16
Sector G; 32K x 16
Sector F; 32K x 16
Sector E; 32K x 16
Sector D; 32K x 16
Sector C; 32K x 16
Sector B; 32K x 16
Sector A; (32K-128) x 16
Program to 0x0000 when using Code Security Mode !
Flash Entry Point; 2 x 16
Security Password; 8 x 16

## Slide 4: Basic Flash Operation
Flash is arranged in pages of 128 addresses
Wait states are specified for consecutive accesses within a page, and random accesses across pages
OTP has random access only
Must specify the number of SYSCLKOUT wait-states
  Reset defaults are maximum values!
Flash configuration code must not run from Flash memory!
FBANKWAIT
@ 0x00 0A86
RANDWAIT
reserved
15
0
4 3
8 7
PAGEWAIT
reserved
12 11
FOTPWAIT
@ 0x00 0A87
OTPWAIT
reserved
15
0
4 3
*** Refer to the F2833x datasheet for detailed numbers ***
  For 150 MHz, PAGEWAIT = 5, RANDWAIT = 5, OTPWAIT = 8
  For 100 MHz, PAGEWAIT = 3, RANDWAIT = 3, OTPWAIT = 5

## Slide 5: Speeding Up Code Execution in Flash: Flash Pipelining (for code fetch only)
16 or 32 dispatched
16
64
Aligned 64-bit fetch
2-level deep fetch buffer
64
F2833x Core decoder unit
Flash Pipeline Enable
0 = disable (default)
1 = enable
ENPIPE
reserved
15
0
1
FOPT @ 0x00 0A80

## Slide 6: Other Flash Configuration Registers
Address Name Description
0x00 0A80 FOPT Flash option register
0x00 0A82 FPWR Flash power modes registers
0x00 0A83 FSTATUS Flash status register
0x00 0A84 FSTDBYWAIT Flash sleep to standby wait register
0x00 0A85 FACTIVEWAIT Flash standby to active wait register
0x00 0A86 FBANKWAIT Flash read access wait state register
0x00 0A87 FOTPWAIT OTP read access wait state register
FPWR: Save power by putting Flash/OTP to ‘Sleep’ or ‘Standby’ mode; Flash will automatically enter active mode if a Flash/OTP access is made
FSTATUS: Various status bits (e.g. PWR mode)
FSTDBYWAIT: Specify number of cycles to wait during wake-up from sleep to standby
FACTIVEWAIT: Specify number of cycles to wait during wake-up from standby to active
Defaults for these registers are often sufficient – See “TMS320F2833x System
Control and Interrupts Reference Guide,” SPRUFB0, for more information

## Slide 7: Flash Programming Basics
The DSP CPU itself performs the flash programming
The CPU executes Flash utility code from RAM that reads the Flash data and writes it into the Flash
We need to get the Flash utility code and the Flash data into RAM
FLASH
CPU
RAM
TMS320F2833x
JTAG
Emulator
SPI
SCI
RS232
Flash Utility Code
Flash Data
eCAN
XINTF
I2C
ROM
Bootloader
GPIO

## Slide 8: Flash Programming Basics
Sequence of steps for Flash programming:
Minimum Erase size is a sector
Minimum Program size is a bit!
Important not to lose power during erase step: If CSM passwords happen to be all zeros, the CSM will be permanently locked!
Chance of this happening is quite small! (Erase step is performed sector by sector)
1. Erase - Set all bits to zero, then to one
Program - Program selected bits with zero
Verify - Verify flash contents
Algorithm Function

## Slide 9: Flash Programming Utilities
Code Composer Studio Plug-in (uses JTAG)
Third-party JTAG utilities
  SDFlash JTAG from Spectrum Digital (requires SD emulator)
  Signum System Flash utilities (requires Signum emulator)
  BlackHawk Flash utilities (requires Blackhawk emulator)
SDFlash Serial utility (uses SCI boot)
Gang Programmers (use GPIO boot)
  BP Micro programmer
  Data I/O programmer
Build your own custom utility
  Use a different ROM bootloader method than SCI
  Embed flash programming into your application
  Flash API algorithms provided by TI
* TI web has links to all utilities (http://www.ti.com/c2000)

## Slide 10: Code Composer Studio Flash Plug-In

## Slide 11: Code Security Module (CSM)
Data reads and writes from restricted memory are only allowed for code running from restricted memory
All other data read/write accesses are blocked:
  JTAG emulator/debugger, ROM boot loader, code running in external memory or unrestricted internal memory
Access to the following on-chip memory is restricted:
0x008000
0x009000
0x00A000
0x300000
0x340000
0x3F8000
0x3FA000
0x380400
0x3F9000
FLASH (256Kw)
128-Bit Password
OTP (1Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
0x00B000
0x3FB000
Dual
Mapped
Flash Registers
0x000A80

## Slide 12: CSM Password
128-bit user defined password is stored in Flash
128-bit KEY registers are used to lock and unlock the device
  Mapped in memory space 0x00 0AE0 – 0x00 0AE7
  Registers “EALLOW” protected
0x33FFF8 - 0x33FFFF
CSM Password
Locations (PWL)
FLASH (256Kw)
0x300000
128-Bit Password
0x33FFF8

## Slide 13: CSM Registers
Address Name Reset Value Description
0x00 0AE0 KEY0 0xFFFF Low word of 128-bit Key register
0x00 0AE1 KEY1 0xFFFF 2nd word of 128-bit Key register
0x00 0AE2 KEY2 0xFFFF 3rd word of 128-bit Key register
0x00 0AE3 KEY3 0xFFFF 4th word of 128-bit Key register
0x00 0AE4 KEY4 0xFFFF 5th word of 128-bit Key register
0x00 0AE5 KEY5 0xFFFF 6th word of 128-bit Key register
0x00 0AE6 KEY6 0xFFFF 7th word of 128-bit Key register
0x00 0AE7 KEY7 0xFFFF High word of 128-bit Key register
0x00 0AEF CSMSCR 0xFFFF CSM status and control register
Key Registers – accessible by user; EALLOW protected
Address Name Reset Value Description
0x33 7FF8 PWL0 user defined Low word of 128-bit password
0x33 7FF9 PWL1 user defined 2nd word of 128-bit password
0x33 7FFA PWL2 user defined 3rd word of 128-bit password
0x33 7FFB PWL3 user defined 4th word of 128-bit password
0x33 7FFC PWL4 user defined 5th word of 128-bit password
0x33 7FFD PWL5 user defined 6th word of 128-bit password
0x33 7FFE PWL6 user defined 7th word of 128-bit password
0x33 7FFF PWL7 user defined High word of 128-bit password
PWL in memory – reserved for passwords only

## Slide 14: Locking and Unlocking the CSM
The CSM is locked at power-up and reset
To unlock the CSM:
  Perform a dummy read of each password in the Flash
  Write the correct passwords to the key registers
New Flash Devices (PWL are all 0xFFFF):
  When all passwords are 0xFFFF – only a read of the PWL is required to bring the device into unlocked mode

## Slide 15: CSM Caveats
Never program all the PWL’s as 0x0000
  Doing so will permanently lock the CSM
Flash addresses 0x337F80 to 0x337FF5, inclusive, must be programmed to 0x0000 to securely lock the CSM
Remember that code running in unsecured RAM cannot access data in secured memory
  Don’t link the stack to secured RAM if you have any code that runs from unsecured RAM
Do not embed the passwords in your code!
  Generally, the CSM is unlocked only for debug
  Code Composer Studio can do the unlocking

## Slide 16: CSM Password Match Flow
Flash device secure after reset or runtime
Do dummy read of PWL 0x33 7FF8 – 0x33 7FFF
Start
Device permanently locked
CPU access is limited – device cannot be debugged or reprogrammed
Device unlocked
User can access on-chip secure memory
Write password to KEY registers 0x00 0AE0 – 0x00 0AE7
(EALLOW) protected
Correct password?
Is PWL = all Fs?
Is PWL = all 0s?
Yes
Yes
Yes
No
No
No

## Slide 17: CSM C-Code Examples
volatile int *PWL = &CsmPwl.PSWD0; //Pointer to PWL register file
volatile int i, tmp;
for (i = 0; i<8; i++) tmp = *PWL++; //Dummy reads of PWL locations
asm (” EALLOW”); //KEY regs are EALLOW protected
CsmRegs.KEY0 = PASSWORD0; //Write the passwords
CsmRegs.KEY1 = PASSWORD0; //to the Key registers
CsmRegs.KEY2 = PASSWORD2;
CsmRegs.KEY3 = PASSWORD3;
CsmRegs.KEY4 = PASSWORD4;
CsmRegs.KEY5 = PASSWORD5;
CsmRegs.KEY6 = PASSWORD6;
CsmRegs.KEY7 = PASSWORD7;
asm (” EDIS”);
asm(” EALLOW”); //CSMSCR reg is EALLOW protected
CsmRegs.CSMSCR.bit.FORCESEC = 1; //Set FORCESEC bit
asm (”EDIS”);
Unlocking the CSM:
Locking the CSM:

## Slide 18
Lab 14: Load an application into Flash
  Use Solution for Lab6 to begin with
  Modify the project to use internal Flash for code
  Add “DSP2833x_CodeStartBranch.asm” to branch from Flash entry point ( 0x33 FFF6) to C - library function “_c_int00”
  Add TI - code to set up the speed of Flash
  Add a function to move the speed-up code from Flash to SARAM Adjust Linker Command File
  Use CCS plug-in tool to perform the Flash download
  Disconnect emulator and re-power the board!
  Code should be executed out of Flash
  For details see procedure in textbook!