## Slide 1
Texas Instruments Incorporated
European Customer Training Centre
University of Applied Sciences Zwickau
Module 15: Boot –ROM and – Loader
32-Bit-Digital Signal Controller
TMS320F2833x

## Slide 2
XINTF Zone 6 (1Mw)
XINTF Zone 7 (1Mw)
0x000000
0x000400
0x000800
M1 SARAM (1Kw)
M0 SARAM (1Kw)
Data Program
PIE Vectors
(256 w)
PF 0 (6Kw)
XINTF Zone 0 (4Kw)
reserved
PF 1 (4Kw)
PF 2 (4Kw)
PF 3 (4Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
L4 SARAM (4Kw)
L5 SARAM (4Kw)
L6 SARAM (4Kw)
L7 SARAM (4Kw)
reserved
0x000D00
0x002000
0x006000
0x007000
0x008000
0x009000
0x00A000
0x00C000
0x000E00
0x005000
0x00B000
0x00D000
0x00E000
0x00F000
0x004000
0x010000
0x010000
0x100000
0x200000
reserved
Data Program
FLASH (256Kw)
0x300000
0x33FFF8
0x340000
PASSWORDS (8w)
reserved
User OTP (1Kw)
0x380800
ADC calibration data
0x380080
0x380090
reserved
0x380400
reserved
0x3F8000
Boot ROM (8Kw)
L0 SARAM (4Kw)
L1 SARAM (4Kw)
L2 SARAM (4Kw)
L3 SARAM (4Kw)
reserved
0x3F9000
0x3FA000
0x3FB000
0x3FC000
0x3FE000
0x3FFFFF
DMA Accessible:
L4, L5, L6, L7,
XINTF Zone 0, 6, 7
Dual Mapped:
L0, L1, L2, L3
CSM Protected:
L0, L1, L2, L3,
FLASH, ADC CAL,
OTP
0x3FFFC0
BROM Vectors (64w)
TMS320F2833x Memory Map

## Slide 3: Reset – Bootloader
Reset
OBJMODE = 0 AMODE = 0
ENPIE = 0 INTM = 1
Boot determined by state of GPIO pins
GPIO 87, 86, 85, 84
Reset vector fetched from Boot ROM
0x3F FFC0
Boot loader sets:
OBJMODE = 1
AMODE = 0
M0SARAM 0x000000
FLASH 0x33FFF6
OTP 0x380400
XINTF 0x100000
Direct Code Entry Points
SCI - A SPI - A
I2C - A eCAN - A
McBSP - A
XINTF (parallel) GPIO (parallel)
Start Boot loader code
0x3FF9CE:

## Slide 4: Boot Loader Options
GPIO pins
87 86 85 84
1 1 1 1 jump to FLASH address 0x33 FFF6
0 1 0 0 jump to M0 SARAM address 0x00 0000
0 1 1 1 jump to OTP address 0x38 0400
1 0 0 1 jump to XINTF 16 address 0x10 0000
1 0 0 0 jump to XINTF 32 address 0x10 0000
1 1 1 0 boot load code to on-chip memory via SCI - A port
1 1 0 1 boot load code to on-chip memory via SPI - A port
1 1 0 0 boot load code to on-chip memory via I2C - A port
1 0 1 1 boot load code to on-chip memory via eCAN - A port
1 0 1 0 boot load code to on-chip memory via McBSP - A port
0 1 1 0 boot load code to on-chip memory via GPIO (parallel)
0 1 0 1 boot load code to on-chip memory via XINTF (parallel)
Boot Mode
Notes: <number>

## Slide 5: Reset Code Flow - Summary
M0 SARAM (1Kw)
FLASH (256Kw)
OTP (1Kw)
0x33 FFF6
0x38 0400
0x30 0000
0x00 0000
0x3F E000
0x3F FFC0
Boot ROM (8Kw)
BROM vector (64w)
0x3F F9CE
Boot Code




RESET
Execution Entry
Point Determined
By GPIO Pins
Bootloading
Routines
(SCI-A, SPI-A, I2C, eCAN-A, McBSP-A GPIO, XINTF)
0x3F F9CE
XINTF Zone 6 (x16 / x32) 0x10 0000
0x00 0000

## Slide 6: F2833x BOOT-ROM Memory Map
Address Range | Function | Format
0x3FE000 – 0x3FE501 | IQ - Math sine/cosine table | 641 x 32 bit; I2Q30
0x3FE502 – 0x3FE711 | IQ - Math normalized inverse | 264 x 32 bit; I3Q29
0x3FE712 – 0x3FE823 | IQ - Math normalized sqrt | 137 x 32 bit; I2Q30
0x3FE824 – 0x3FE9E7 | IQ - Math normalized arctan | 226 x 32 bit; I2Q30
0x3FE9E8 – 0x3FEB4F | IQ – Math round / saturation | 180 x 32 bit; I2Q30
0x3FEB50 – 0x3FEBC7 | IQ – Math min / max table | 60 x 32 bit; I31Q1 – I1Q31
0x3FEBC8 – 0x3FEBDB | IQ – Math exp(x) table | 10 x 32 bit; I1Q31
0x3FEBDC – 0x3FF0DD | FPU sine/cosine table | 641 x 32 bit; float
0x3FF0DE – 0x3FF261 | FPU normalized arctan | 194 x 32 bit; float
0x3FF262 – 0x3FF275 | FPU exp(x) table | 10 x 32 bit; float
0x3FF276 – 0x3FF34B | reserved | 
0x3FF34C – 0x3FF9ED | Boot Loader Functions | F2833x machine code
0x3FF9EE – 0x3FFFB8 | reserved | 
0x3FFFB9 – 0x3FFFBF | ROM version and | 
0x3FFFC0 – 0x3FFFFF | Reset and Interrupt vectors | 32 x 32 bit address
Notes: <number>

## Slide 7: F2833x BOOT-ROM Vector Table
Vector
Address
Content
RESET
INT1
INT2
INT3
INT4
INT5
INT6
INT7
INT8
INT9
INT10
INT11
INT12
INT13
INT14
DLOGINT
0x3F FFC0
0x3F FFC2
0x3F FFC4
0x3F FFC6
0x3F FFC8
0x3F FFCA
0x3F FFCC
0x3F FFCE
0x3F FFD0
0x3F FFD2
0x3F FFD4
0x3F FFD6
0x3F FFD8
0x3F FFDA
0x3F FFDC
0x3F FFDE
0x3F FC00
0x00 0042
0x00 0044
0x00 0046
0x00 0048
0x00 004A
0x00 004C
0x00 004E
0x00 0050
0x00 0052
0x00 0054
0x00 0056
0x00 0058
0x00 005A
0x00 005C
0x00 005E
Vector
RTOSINT
reserved
NMI
ILLEGAL
USER 1
USER 2
USER 3
USER 4
USER 5
USER 6
USER 7
USER 8
USER 9
USER 10
USER 11
USER 12
Address
0x3F FFE0
0x3F FFE2
0x3F FFE4
0x3F FFE6
0x3F FFE8
0x3F FFEA
0x3F FFEC
0x3F FFEE
0x3F FFF0
0x3F FFF2
0x3F FFF4
0x3F FFF6
0x3F FFF8
0x3F FFFA
0x3F FFFC
0x3F FFFE
Content
0x00 0060
0x00 0062
0x00 0064
0x00 0066
0x00 0068
0x00 006A
0x00 006C
0x00 006E
0x00 0070
0x00 0072
0x00 0074
0x00 0076
0x00 0078
0x00 007A
0x00 007C
0x00 007E

## Slide 8: Boot Loader Data Stream Structure
1
0x10AA : Key for memory width = 16 bit
2-9
Reserved for future use
10
Entry Point PC[22:16]
11
Entry Point PC[15:0]
12
Block Size (words); if 0 then end of transmission
13
Destination Address of block ; Addr[31:16]
14
Destination Address of block ; Addr[15:0]
15
First word of block
N
Last word of block
N+1
Block Size (words)
N+2
Destination Address of block ; Addr[31:16]
N+3
Destination Address of block ; Addr[15:0]

## Slide 9: Boot Loader Data Stream Example
10AA ; Key for 16-Bit memory stream
0000
0000
0000
0000
0000
0000
0000
0000
003F ; PC – starting point after load is complete: 0x3F 8000
8000
0005 ; 5 words in block 1
003F
9010 ; First block is loaded into 0x3F 9010
0001 ; first data word
0002
0003
0004
0005 ; last data
0002 ; Second block is two words long
003F ; Second block is loaded into 0x3F 8000
8000
7700 ; first data
7625 ; last data
0000 ; next block zero length = end of transmission

## Slide 10: F2833x Boot Loader Transfer Procedure
Read first word(W1)
W2:W1=
0x08AA?
Read BlockSize(R)
Read Entry Point
16bit data size
R = 0?
Read BlockAddress
Transfer R words from
source to destination
Return and Jump
to Entry Point
Read second word
lower 8 bit
W1 =
0x10AA?
8bit data size
Format Error
No
No
No
Yes
Yes
Yes

## Slide 11: F2833x Init Boot Function
Init Boot
RESET
Initialize C28x:
OBJMODE = 1
AMODE = 0
M0M1MAP = 1
DP = 0
OVM = 0
SPM = 0
SP = 0x00 0400
Dummy Read
CSM passwords
Call
BootModeSelect
ExitBoot

## Slide 12: F2833x SCI Boot Loader Function
F2833x
SCI-A
Host/ e.g.
PC‘s COM1
RS 232
e.g.
Texas
Instruments
MAX3221
RS 232
TxD
TxD
RxD
RxD
3
2

## Slide 13: F2833x SCI Boot Function
SCI Boot
Enable SCI-A Clock
Set LSPCLK to /4
Enable SCI-A Tx and
Rx - Pin
Setup SCI-A:
1 stop,8 data ,no parity
No loopback
Disable SCI-A INT
Disable SCI-A FIFO
Prime SCI-A baud rate
register
Enable Autobaud
detection
Autobaud
Lock ?
Echo auto baud
character
Read KeyValue
Valid Key?
FLASH
Start Boot Load
Sequence
No
No
Yes
Yes

## Slide 14: F2833x parallel Boot Loader (GPIO)
C28x
GPIO
Host/ e.g.
PC‘s COM1
GPIO - 26
16
GPIO15...GPIO0
GPIO - 27
GPIO26
GPIO27
1
2
3
4
5
6
1: F28x indicates: “ready to receive”
2: Host signals “data active at GPIO-B”
3: F28x indicates “read is complete”
4: Host acknowledges “cycle completed”
5: F28x indicates: “ready for more data”

## Slide 15: F2833x GPIO Boot Function
GPIO Boot
Read KeyValue
( 8 or 16 Bit size)
Initialize GPIO
GPIO0…15 = input
GPIO27 = input
GPOI26 = output
Valid Key?
FLASH
Call Parallel Copy Data
Read Entry Point
Read and discard
8 reserved words
Jump
Entry Point
No
Yes

## Slide 16: Host GPIO Boot Function
Start Download
F28x ready?
(GPIO26=0)
Deactivate GPIO27 =1
Load data
Signal that data avail.
GPIO27 =0
Yes
F28x ack?
(GPIO26=1)
More Data?
End Download
Yes
Yes
No
No
No

## Slide 17: F2833x SPI Boot Loader Function
F2833x
SPI - A
Serial EEPROM
DIN
DOUT
CLK
/CS
SPI – MOSI (GPIO16)
SPI – SOMI (GPIO17)
SPI – CLK (GPIO18)
SPI – STE (GPIO19)
EEPROM – Types:
Atmel: AT25C256; see chapter 13
Xicor: X25256
ST: M95080
and others
Note:
SPI – loader is 8bit only, it does not support 16bit data stream
EEPROM data stream must start at address 0x0000

## Slide 18: F2833x SPI Boot Loader Data Stream
1
LSB = 0xAA ( Key for 8bit transfer)
2
MSB = 0x08 ( Key for 8bit transfer)
3
LSB = LSPCLK value
4
MSB = SPIBRR value
5-18
reserved
19
Entry Point [23:16]
20
Entry Point [31:24]
21
Entry Point [7:0]
22
Entry Point [15:8]
23 ...
Blocks of data: block size/destination/data as shown
Byte
Content

## Slide 19: F2833x SPI Boot Function
SPI - Boot
Valid Key?
( 0x08AA )
Enable SPI clock
Set LSPCLK to 4
No
Enable SPI pin –
functionality
Setup SPI:
8-bit character
Internal SPI-clock
SPI-Master
Slowest baud rate (0x7F)
Relinquish from RESET
Set chip enable
GPIO-F3 = 1
Send Read Command
To EEPROM
Address = 0x0000
Read KeyValue
Read LSPCLK value
Requested
LSPCLK = 2?
Change LSPCLK
FLASH
C
No
Yes
Yes

## Slide 20: F2833x SPI Boot Function (cont.)
Read SPIBRR value
Requested
SPIBRR = 0x7F?
Change SPIBRR
Jump EntryPoint
C
Yes
Read 7 reserved words
Read Entry Point
Read Data Blocks
No

## Slide 21: Lab15_1: SCI – A boot loader
  Use Lab6 (“binary counter”) as starting point
  Change the Hardware Boot Sequence from FLASH to SCI -A (close Jumper J3)
  Use a SCI – connection to your PC:
  Use tool “hex2000.exe” to generate download stream
  Use a PC terminal program to download code