## Slide 1: Sustainable Cities 2 – Urban form and urban structure
659EC
A.Y. 2025/2026
Dr. Giuseppe Borruso
Department of Economics, Business, Mathematics and Statistics
University of Trieste
E-mail. giuseppe.borruso@deams.units.it
Ph. +39 040 558 7008
Notes: Slides with (*) in footnotes have been modified by Jean-Paul Rodrigue materials concerning “Transportation Geography”. Slides with (*) in footnotes are referred to “Transport and the Urban Environment” materials (see copyright). I have modified and elaborated materials in order to be suitable for the current course.
For references visit http://people.hofstra.edu/geotrans
Copyright © 1998-2010, Dr. Jean-Paul Rodrigue, Dept. of Global Studies & Geography, Hofstra University. For personal or classroom use ONLY.

## Slide 2: Topics
World urban population
Cities: a definition
Transport, urban form and spatial structure
The analysis of urban structure
  The global models
  The urban density
  The bid rent and the models of urban structure
The urban crisis and the urban lifecycle
Case study: the Megalopolis

## Slide 3: Transportation, Urban Form and Spatial Structure

## Slide 4: Transportation, Urban Form and Spatial Structure
Copyright © 1998-2010, Dr. Jean-Paul Rodrigue, Dept. of Global Studies & Geography, Hofstra University. For personal or classroom use ONLY. This material (including graphics) is not public domain and cannot be published, in whole or in part, in ANY form (printed or electronic) and on any media without consent. This includes conference presentations. Permission MUST be requested prior to use.
Infrastructures
Modes
Users
Transportation
Urban Form
Spatial
imprint
Urban Spatial Structure
Spatial
interaction
Notes: 4
**

## Slide 5: One Hour Commuting According to Different Urban Transportation Modes
Copyright © 1998-2010, Dr. Jean-Paul Rodrigue, Dept. of Global Studies & Geography, Hofstra University. For personal or classroom use ONLY. This material (including graphics) is not public domain and cannot be published, in whole or in part, in ANY form (printed or electronic) and on any media without consent. This includes conference presentations. Permission MUST be requested prior to use.
Streetcar line
Freeway
Walking
Streetcar
Cycling
Automobile
Automobile with
freeways
10 km
Notes: 5
Source: adapted from P. Hugill, (1995), p. 213.
**

## Slide 6: Evolution of the Spatial Structure of a City
Copyright © 1998-2010, Dr. Jean-Paul Rodrigue, Dept. of Global Studies & Geography, Hofstra University. For personal or classroom use ONLY. This material (including graphics) is not public domain and cannot be published, in whole or in part, in ANY form (printed or electronic) and on any media without consent. This includes conference presentations. Permission MUST be requested prior to use.
A
B
C
Core activities
Central activities
Peripheral activities
Central area
Major transport axis
Notes: 6
**

## Slide 7: Evolution of Transportation and Urban Form in North American and European Cities
Copyright © 1998-2010, Dr. Jean-Paul Rodrigue, Dept. of Global Studies & Geography, Hofstra University. For personal or classroom use ONLY. This material (including graphics) is not public domain and cannot be published, in whole or in part, in ANY form (printed or electronic) and on any media without consent. This includes conference presentations. Permission MUST be requested prior to use.
I - Walking-horsecar era (1800-1890)
II - Streetcar era (1890-1920)
III - Automobile era (1920-1945)
IV - Highway era (1945-)
II
III
IV
II
III
IV
I
I
Streetcar line
Highway
North America
Europe
Notes: 7
*

## Slide 8
The city as an egg
https://bigthink.com/strange-maps/534-the-eggs-of-price-an-ovo-urban-analogy/

## Slide 9
The city as an egg
https://www.researchgate.net/figure/The-Form-of-the-City-Vancutsem-2010-adapted-from-The-City-as-an-Egg-Source-Price_fig2_255717111

## Slide 10: The analysis of urban structure
The global model
The urban density
The bid rent and the models of urban structure

## Slide 11: The analysis of urban structure
Partial models – concern the location of specific sectors of activity;
Global models – concern the location of all residential and production forms of an urban area
Role of transport in shaping the distribution of types of land use:
  in terms of transport costs;
  in terms of accessibility and urban land value

## Slide 12: Global models
Effort to highlight an order within the topographical and functional structure of a city
Different models used to represent and study such ‘order’ :
  Circular Models i (Burgess, 1967)
    Urban values decrease regularly from city centre
  Sectors Models (Hoyt, 1932)
    elaboration: inner city’s structure is influenced by radial road, pre-existing nuclei, geomorphology, etc.
  Multi-centre Models (Harris and Ullman, 1945)
    Development of no single centres but in a number of centres within urban area:
      Specialized request for soil;
      Concentration of activities;
      Conflict between different activities in land use;
      Bid-rent differences

## Slide 13: Bugess’ model of land use
IV – working class area
V – residential area
VI – suburban area
I - Loop (downtown; CBD)
II – industries
III – transition area
LOOP
Little
Sicily
Apartment Houses
Bungalow
Section
Single Family Dwellings
Residential District
Ghetto
Two Plan
Area
Second Immigrant
Settlement
Model
Chicago, years ‘20
Black Belt
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
13
(*)

## Slide 14: Models: ‘sectors’ (Hoyt) and ‘nuclei’ (Harris and Ullman)
2
3
4
4
5
3
3
1
3
3
3
1 CBD
2 Wholesale and light manufacturing
3 Low-class residential
4 Middle-class residential
5 High-class residential
1
2
3
4
5
3
3
6
7
8
9
6 Heavy manufacturing
7 Sub business district
8 Residential suburb
9 Industrial suburb
Sector
Nuclei
2
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
14
(*)

## Slide 15: Urban density
Topographic and functional structures: different characteristics for different cities
The distribution of urban density maintains similar characteristics for all cities
Density decreases following a negative exponential function of distance from urban centre.
Pd = P0 * e – gd
  Pd = population density at distance d from the centre (CBD)
  – g = factor of negative slope of the density function
  P0 = density of the central area

## Slide 16: Profiles of urban density
a) Pd = P0 * e – gd
b) Pd = P0 * e – gd2
c) ‘volcano’
Density
Distance
CBD
Density
Distance
CBD
Density
Distance
CBD

## Slide 17: Evolution of urban densities in North America and Europe
Density
Distance
North America
I
II
III
IV
Density
Distance
Europe
I
II
III
IV
I – Before mechanized transport
II – first forms of mechanized transport (tram)
III – Motorization (bus, private cars)
IV - Suburbanization
r(NA)
r(E)
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
17
(*)

## Slide 18: The bid-rent (I)
Pattern of land uses depend on a variety of settlements’ decisions
Decisions guided by economic process operating gin the system. The distribution of urban areas’ use represent a visual and structured phenomenon.
Basic aspects:
  Each activity derives utility from every site of the urban area;
  Utility is measured by the rent an activity is willing to pay for the use;
  Among the different rents from the utility of the site, the maximum one will determine the market value

## Slide 19: The bid-rent (II)
In the long run the market competition in urban areas will result in the optimal use of each site
The rent is influenced by elements as the evaluation of the exchange between the major rent paid for the use of a site with higher accessibility and the transport costs’ savings compared to a less accessible site
The competition for land use minimizes the effects of distance on the urban area
The spatial distribution of urban rent is function of the transport cost.

## Slide 20: The bid-rent (III)
Savings in transport costs can lead to payments of extra-rents;
More accessible sites in urban areas are NOT occupied by activities that pay more BUT by those that can gain the higher advantage from that part of urban land;
Bid rent become land values and depend on different accessibilities of sites within the urban area

## Slide 21: The bid-rent (IV)
Land values are important to comprehend the internal geographical economic structure of a city :
Different motivations for residential uses;
Production is affected by land value as an expression of accessibility:
  Land value is maximum in the city centre and decreases when moving gto peripheries;
  Higher land values close to main radial road than in the space between them;
  Higher land values, with respect to the distance from the city centre, can be found at intersection between major radial roads and ring roads
Accessibility has different meanings for different activities:
  Retail – closeness to potential market;
  Services – closeness to places of supply of complimentary services;
  Industry – availability of suited soils; Transport; public services, closeness to other industries;
  Residential – closeness to working places, shopping centres; also environmental and social qualities

## Slide 22: Von Thunen’s model of land use
The isolated state
Modified conditions
River
Secondary market
Extensive stock grazing
Three-field crop rotation system
Arable and pastures
Intensive crop rotation
forestry
dairy & vegetables
Central market
Replay
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
22
(*)

## Slide 23: Bid rent and land use
rent
Distance
A- Retail
B- Industry and retail
C - Apartments
D – Detached houses
1 – bid rent lines
2 – Overlay of rents
City borders
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
23
(*)

## Slide 24: Bid-rent
P
Q
distance
A
B
C
B
A
rent
A’
B’
C
C’
Area A: commercial land use
Area B: industrial land use
Area C: residential land use
Curve AA’: commercial activities’ rent
Curve BB’: industrial activities rent
Curve CC’: residential activities rent
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
24

## Slide 25: Bid rent
1 km
5 km
10 km
S = 3.14
S = 75.40
S = 235.62
1/S
ΔD
Δ1/S
S = π D2
Rent
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
25
(*)

## Slide 26: Variations to bid-rent theory
A – CBD
B – Commerce / industry
C – residential high– medium density
D – sub-centres
E – Suburbia
rent
A
B
C
D
E
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
26
(*)

## Slide 27: Land use value for activity sector according to the distance from the CBD
Distance from the centre
Land use value
Retail
Residential (several components families)
Residential (single families)
Notes: Diparimento di Scienze Geografiche e Storiche - Introduzione ai GIS
27
(*)